AEG LAVAMAT 47280 aqua control, LAVAMAT 47080 aqua control

A „Vége”** jelzõlámpa 4-szer villog*** és a kijelzõben az E40

hibakód jelenik meg:

A tetõ lezárása nem megfelelõ.

A „Vége”** jelzõlámpa 2-szer villog*** és a kijelzõben az E20

hibakód jelenik meg:

A kifolyószûrõ eltömõdött.

A kifolyócsõ megtört, vagy

megcsavarodott.

Túl magasan van a kifolyócsõ.

Az ürítõ szivattyú eltömõdött.

A kifolyó szifon eltömõdött

-----------------------------------------------------------------------------

ARISTON-INDESIT

F01 - "Motor vezérlési hiba" elektronika hiba, vagy testzárlatos motor

F02 - "Motor áll" Motor szakadás vagy Tachogenerátor hiba

F03 - NTC Thermisztor hiba, vagy elektronika hiba

F04 - Vízszintszabályzó hiba (egyszerre "0" és "Túltöltés" szint is)

F05 - Szivattyú hiba (nem ürít, dugulás)

F06 - Prk. hiba (nincs meg a megfelelõ kód, nem jár a TIMER)

F07 - Fûtési hiba nem fût (fûtõbetét szakadt)

F08 - Fûtési hiba túlfût (fûtõbetét testzárlat, vagy vízszintszabályzó kontakthibás, panel bepárásodva, hibás)

F09 - SETUP hiba (nem egyezik a yP és az EEPROM verziója, elektronika hiba)

F10 - Vízszint érzékelési hiba (sem "0" sem "I" szint/"0"+"I")

F11 - Szivattyú "Feedback" hiba (szivattyú szakadt vagy nincs csatlakoztatva)

F12 - Nincs kapcsolat a kezelõ panellal

F13 - Szárítási NTC hibás

F14 - Szárító fûtõbetét szakadt

F15 - Szárító fûtõbetét testzárlatos, vagy vízszintszabályzó hiba

F16 - dob retesz kapcsoló hibás (csak felültöltõs gépnél)

F17 - Ajtóretesz hiba

F18 - Kezelõegység hiba

----------------------------------------------------------------------------

DAEWOO DWD-F1011, DWD-F1012, DWD-F1013, DWD-F1212

E2 - Vízszintszabályzó jel nincs (bekapcs után E9 is)

E5 - Kezelõegység hiba

E6 - Motor hiba

E8 - Motor forgás nincs, vagy nem érzékeli (tachogenerátor hiba, vez. panel hibás)

E9 - Vízszintszabályzó hiba

E16- Panel hiba

PEF- Szûrõ el van dugulva (v. PFE?)

H2 - NTC rövidzárlat, vagy szakadás

H4 - Víz nélkül is megy a fûtés

H5 - Túlfût

H6 - Nem fût, fûtõbetét hiba

H8 - Víz nélkül is megy a fûtés

LE - Ajtókapcsoló nem zár

IE - nem kap vizet

OE - nem tud üríteni

UE - ruha nincs elrendezõdve

-----------------------------------------------------------------------------

DELTON WMD1032T, VDM642L, VDM1042T

LOUIS AXTON WFLA-800, WFLA-1000,

ORION OMU800/V, OMU1000/V,

REGAL VRM642,

SEG W-1247, W-1447

VESTEL,

WELTECH VWM842T,

ZANUSSI ZWT185W

Err01 - Start/pause lámpa villog         	- ajtó nincs becsukva

Err02 - Standby lámpa villog   			- nem kap vizet

Err03 - Start/p+Standby lámpa villog     	- nem ürít

Err04 - Program vége lámpa villog        	- túltöltött vagy szivattyú szakadt

Err05 - Start/p+Program vége villog      	- fûtõbetét vagy NTC hiba (túlfût)

Err06 - Standby+Program vége villog 		- motor hiba (szakadás)

Err07 - Start/pause+Standby+Program vége villog - motor hiba

Err08 - Standby+Program vége folyamatosan ég 	- hálózati fesz túl magas vagy

260V< fesz <150V			  túl alacsony

-----------------------------------------------------------------------------

ELECTROLUX EWT9120W EWT10120

Piros LED adja a tizeseket, a zöld az egyesek számát

E11 - nincs víz

E13 - nincs elég víz

E21 - nem tudott leüríteni

E23 - nincs csatlakozva a szivattyú

E24 - szivattyú vezérlés hiba (triak?)

E31 - vízszintszabálízó hiba

E32 - vízszintszabályzó nem áll üresbe

E33 - vízszint nem éri el az I szintet 1/3 perc alatt

E34 - vízszint nem éri el az II szintet 1/3 perc alatt

E35 - túltöltés

E36 - vízszint vlmi habérzékelésnél

E37 - vízszint vlmi habérzékelésnél

E38 - légcsapda?

E39 - vízszszab. hiba?

E3A - fûtésrelé hiba

E41 - ajtó nyitva / zár hibás

E42 - ajtókapcsoló hiba

E43 - ajtózár vezérlés hiba

E44 - ajtózár vezérlés hiba

E45 - ajtózár vezérlés hiba

E51 Motortriac short circuit

E52 No signal from tachogenerator

E53 Motor triac sensing failure Input voltage allw ays 0V or 5V

E54 Motor relay defect

E55 Motor circuit interrupted

E56 No signal from tachogenerator, No signal after 15 min

E57 Inverter current goes above threshold (>15A)

E58 Motor phase current goes above threshold (>4,5A)

E59 No tacho signal for 3 seconds after new speed target

E5A Heat Sink temperature goes above threshold (88°C)

E5B DC bus voltage goes below threshold (<175V)

E5C DC bus voltage goes above threshold (>430V)

E5D FCV cannot receive and/or transmit a message for more

E5E There are communication problems in betw een FCV

E5F FCV control board is continuously asking for configuration

E61 Insufficient heating

E62 Overheating: Temperature greater 88°C for a time longer than 5 min

E66 Heating element defect Replace pressure sw itch antboil 2 2 A X

E68 Leakage current in the appliance too high.

E70 E71 NTC short circuit

E74 NTC isn't in the correct position in the tub Check the position 3 S X X X X X

E80 E82 Wrong selector reset postion detection Replace electronic A X X X X X X X

E83 Wrong selector reading Wrong configuration of the machine 4 S X X X X X X X

E84 Recirc. pump sensoring failure Input voltage allw ays 0V or 5V

E85 Recirculation pump defect Replace recirculation pump 2 A X X X X X

E91 Interrupted communication Replace cable,

E92 Incongruence betw een In/Output electronic and electronic In/Output electronic is incompatible 1 A X X X X X X

w ith electronic

E93 Configuration error Wrong configuration of the machine 1 A X X X X X X X X

E94 Lost of cycle datas Wrong configuration of the machine 1 A X X X X X X X X

E95 Communication error betw een microprocessor and EEPROM Replace electronic 0 A X X X X X X X

E96 Incongruence betw een Hardw are-version and Wrong configuration of the machine 0 A X X

cycles configuration Replace electronic

E97 Incongruence betw een selector and cycles configuration Wrong configuration of the machine 0 A X X X X X X X

Replace electronic

E98 Incongruence betw een Replace electronic 0 A X

motor control board and electronic Replace w iring

E99 Connection betw een loudspeaker and In/Output electronic Replace loudspeaker 0 A X X

Replace w iring

E9A Firmw are betw een loudspeaker and In/Output electronic not ok Replace In/Output electronic 0 A X X

EA0 EA1 DSP defect Replace DSP, Replace electronic 5 S X X X X X X X X

Replace w iring, Cut drive belt

EA2 DPS sensing defect Replace electronic X

EA3 DPS unable to lock motor pully Replace DSP, Replace electronic X

Replace w iring, Cut drive belt

EA4 DPS defect Replace DPS X

Replace electronic

Replace w iring

EA5 Triac for DPS defect Replace electronic X

EA6 Drum have blocked in the first ca. 30sec. Cut drive belt, Replace DSP 0 A X X X X X

Drum lid not closed

EA6 Drum have blocked in the first ca. 3sec. Cut drive belt, Replace DSP 0 A X

Drum lid not closed

EB0 EB1 Pow er supply frequency out of limits Wrong or disturbed pow er supply line 0 A X X X X X X

Replace electronic

EB2 Pow er supply voltage too high Wrong or disturbed pow er supply line 0 A X X X X X X

Replace electronic

EB3 Pow er supply voltage too low Wrong or disturbed pow er supply line 0 A X X X X X X

Replace electronic

EBE Line Safe relay faulty Replace electronic 2 A X

EBF Line Safe "sensing" faulty Replace electronic 2 A X

EC1 Inlet valve blocked Replace inlet valve, Replace electronic 2 A X X

Replace w iring

EC2 Turbidity sensor defect Replace turbidity sensor X

EF0 EF1 Filter dirty Cleaning drainhose and filter S X X X X X X

Drainhose closed Checking drainpump

Time for draining to long

EF2 Detergent overdosing Cleaning drainhose and filter 6 A X X X X X X

To much foam during the drain phase Checking drainpump

Filter dirty Not overdosing

Drainhose closed

EF3 Aqua Control system activated Leakage in the machine 2 A X X X X X X

Drain pump cable defective Replace cable

Drain pump interruption Replace drain pump

EF4 No signal from flow meter w ith electro valves sw itched on Water tap closed or mains pressure 0 X X X

insufficient.

EF5 Interrupted the spinning phase Pay attention to the quantity of laundry, 0 X

Unbalance to high, unbalance >1200gr check stationary behaviour of w asher

EH0 EH1 Pow er supply frequency out of limits Wrong or disturbed pow er supply line 0 A X

Replace electronic

EH2 Pow er supply voltage too high Wrong or disturbed pow er supply line 0 A X

Replace electronic

EH3 Pow er supply voltage too low Wrong or disturbed pow er supply line 0 A X

Replace electronic

EHE Line Safe relay faulty Replace electronic 2 A X

EHF Line Safe "sensing" faulty Replace electronic 2 A X

-----------------------------------------------------------------------------

FAGOR FET-311, FET-309

d01 - vízfelvétel az 1. szintet nem érte el 6 perc alatt

d02 - üríréskor a 0. szintet nem érte el 6 perc alatt

d03 - víz nem melegszik 120 ill. 40 perc alatt sem.

d04 - motor túlvezérlés, kontrollálatlan forgás

d05 - NTC hiba

d06 - tachogenerátor jel nincs

d07 - ajtókapcsoló nem zárt be, vagy motor csatlakozási hiba

d09 - programválasztó kapcsoló hiba

d10 - túltöltés

d12 - ?

d13 - a kívánt cf. fordulatot nem érte el

d17 - dobpozicionáló nem ad impulzusokat

d20 - vízterelõ motor v. kapcsoló hiba

d21 - elektronika hiba

-----------------------------------------------------------------------------

FAGOR 2FS-3611

F01 - nem kap vizet

F02 - nem ürít

F03 -

F04 -

F05 - NTC szakadt

F06 - nem fût (6-8 perc után)

F07 - szivattyú szakadás

F08 -

F09 - motorkõr, vagy tachogenerátor szakadt

-----------------------------------------------------------------------------

FAGOR 3F-109, 3F-211

F01 - Nem kap vizet 10 perc után sem (LED5-6 egyszerre villog)

F02 - Nem tud üríteni                (LED6-7 egyszerre villog)

F04 - Ajtóretesz nem zár             (LED5-7 felváltva villog)

F06 - ? program végén jelezte

F07 - Szivattyú szakadt              (LED5-6-7-10 egyszerre villog)

F08 - Motor vezérlési hiba

-----------------------------------------------------------------------------

Gorenje WA50080, WA50100

2 - ajtó nem zárt

3 - nem kap vizet

7 - nem ürít

-----------------------------------------------------------------------------

HAIER HMS1000TVE

Err1 - Ajtókapcsoló nyitott

Err2 - Nem ürített le

Err4 - ? pr végén jelentkezett

Err5 - Nem kap vizet

-----------------------------------------------------------------------------

INDESIT DE73 mosogatógép

Should a Fault occur in use, the LCD display will show a fault Code to indicate

the area of the fault & on faults A01 to A05 inclusive all active settings are

reset & all loads deactivated :

A01 = Acquastop operated due to leak / overfill - machine drains until empty + lmin.

A02 = Heater Relay open circuit/short circuit or Thermistor or Safety T/Stat o/c or

s/c or Element machine fills to Level Switch & Wash Pump runs.

A03 = Thermistor open circuit /short circuit - machine drains until Level Switch

resets +1minute

A04 = Unable to sense/reach temperature in 70mins. - machine drains until Level

Switch resets + lminute

A05 = Level Switch not resetting in within 3' 20" of drain commencing - machine

drains until Level Switch resets +1 minute

A06 = Not used see also H20 at end

A07 = Wash pump Triac closed/open circuit - check that Drain Pump is not disconnected

or Aquastop operated

A08 = Auxiliary Wash Pump Triac closedlopen circuit - check Wash Motor operation-

machine drains until Level switch resets+30"

A09 = Main Wash Pump Triac closed/open circuit - cheek Wash Motor operation-

machine drains until Level Switch resets+30"

A10 = Fill Solenoid valve Triac closedlopen circuit - check valve/operation -

machine drains until Level Switch resets+30"

A11 = 1/2 load Solenoid Valve Triac or alternating Wash Motor action -

check Solenoid Valve operation & alternating Motor action, replace Module if required -

machine drains until Level Switch resets +30"

A12 = Relay with open circuit - check Heater, replace Module if required -

machine drains until Level Switch resets+30"

A13 = Dispenser Triac incorrect operation closed/open circuit -

Wash Cycle completes but with Dispenser Lid notfunctioning correctly

A14 = Syphoning - Drain hose to low ??? (undocumented error code)

H20 = Static 'Fill Time exceeding 6 minutes - cheek for blockages/low pressure

5)b) Faults with no Fault Code display

* Solenoid Valve Triac malfunction closed/open circuit -.

Wash Cycle completes but with Salt collection not functioning correctly ie,

hard water problems

* Fan Triac &/or Heater malfunction closedlopen circuit -.

Wash Cycle completes but with poor Drying

* Eeprom malfunction - appliance finishes cycle before it is completed & stops.

Should a fault occur in use, the Fault Codes above will be displayed &

should initially be used as a guide in your diagnosis..

Note that after switching on the machine upon your arrival, a short delay may

occur before that fault is displayed.

-----------------------------------------------------------------------------

LEHELUX PA5580A520

(Készenléti LED jelzi)

1x ajtóretesz nem zárt be.

2x nem kap vizet

3x nem ürít

4x túltölt

5X NTC szakadt, vagy zárlatos

6x ?

7X motorkör, vagy tachogenerátor szakadt

12x mikrokapcsoló nyitott

-----------------------------------------------------------------------------

LG ?

IE - Nem vesz vizet (4 perc alatt a min. vagy 25 perc alatt a szükségeset)

UE - Ruha elrendezettlenség

OE - Nem ürít (8 perc alatt sem)

FE - (Overflow) túltöltés

PE - Vízszintszabályzó hiba

dE - Ajtókapcsoló nem zár

tE - Termisztor vagy fûtõbetét hiba

-----------------------------------------------------------------------------

LG 1041WF, 1040WF

FE - vízszintszabályzó hiba

PE - túltöltés

PE : Sensing water pressure error

FE : Problem of overfilling water

dE : Door is not closed

LE : Over load in motor

CE : Over load in motor

IE : Water inlet trouble

OE : Drainage trouble

UE : Imbalance trouble

tE : Water temperature trouble

-----------------------------------------------------------------------------

LG WD-8013C

összes hõfok villog+7x sípol termisztor>42K v. szakadás

össz hõfok+össz cf.+össz opc villog+7x sípol - ajtóretesz nem zárt

SW8 lámpái villognak+7x sípol - nem kap vizet

össz opc+össz SW8 villog+7x sípol - vízszintszabályzó hiba (lehet hogy az össz cf is villog?)

-----------------------------------------------------------------------------

LG WD-8021C

IE szelep hiba (8perc után még mindíg 24,8 KHz felett)

FE nem ürít (8')

OE túltöltés

PE vízszintszab. hiba

dE ajtókapcsoló 16"

tE NTC hiba (szakadt v. rövidzár)

UE cf balans (rázkódás)

EE EEPROM hiba

SE motor hiba (2')

CL gyerekzár aktív

-----------------------------------------------------------------------------

LG WD-10302TP

IE szelep hiba (8perc után még mindíg 24,8 KHz felett) OK!

FE nem ürít (8')

OE túltöltés

PE vízszintszab. hiba

dE ajtókapcsoló 16"

tE NTC hiba (szakadt v. rövidzár)

UE cf balans (rázkódás)

EE EEPROM hiba

SE motor hiba (2')

CL gyerekzár aktív

-----------------------------------------------------------------------------

LG WD-10302 NUP

IE - Nem vesz vizet (4 perc alatt a min. vagy 25 perc alatt a szükségeset)

UE - Ruha elrendezettlenség

OE - Nem ürít (8 perc alatt sem)

FE - (Overflow) túltöltés

PE - Vízszintszabályzó hiba

dE - Ajtókapcsoló nem zár

tE - Termisztor vagy fûtõbetét hiba

-----------------------------------------------------------------------------

LG WD-80150

IE - Nem vesz vizet (4 perc alatt a min. vagy 25 perc alatt a szükségeset)

UE - Ruha elrendezettlenség

OE - Nem ürít (8 perc alatt sem)

FE - (Overflow) túltöltés

PE - Vízszintszabályzó hiba

dE - Ajtókapcsoló nem zár

tE - Termisztor vagy fûtõbetét hiba

-----------------------------------------------------------------------------

SAMSUNG Silver Nano F1045AV, B1245AV

tE - termisztor szakadás, vagy rövidzár

dE - ajtóretesz nem zárt be

3E - nem forgat

4E - nem kap vizet 2 perc alatt sem éri el a legalsó szintet

OE - túltöltés

HE2- nem melegszik a víz

-----------------------------------------------------------------------------

SAMSUNG F-843, F-1043, R-1043, P-1253

0E túltöltés

dE ajtóretesz nem zár

tE termisztor szakadás vagy zárlat

1E vízszintszabályzó hiba (nincs jel)

3E motor nem forog

4E nincs víz (nem tölt)

5E nem ürít

6E nem fût (víz nem melegszik)

HE túlfûtés

UE kiegyensúlyozatlanság

dE Ha a motor szakadt, vizet nem vesz, majd dE hibajelzés

bE Motor triak zárlat

-----------------------------------------------------------------------------

SAMSUNG P1205J

door - ajtó nem zárt

E1   - nem kap vizet

E2   - nem ürít

E3   - túltöltés

E7   - nincs vízszintszabályzó jel

E8   - túlfût, NTC hiba (zárlat vagy szakadás)

E6   - motor tacho túlpörög

-----------------------------------------------------------------------------

TECHWOOD WV1042

E01 (elõm+fõmosás LED villog) - Ajtóretesz nem zárt

E02 (elõmosás+öblités villog) - Mem kap vizet

E03 ?

E04 (elõmosás+öblités villog) - Szivattyú kör szakadt

E05 (fõmosás+cf LED villog) - NTC zárlat, vagy szakadás

-----------------------------------------------------------------------------

Wellinton VWM1242 LCD ORION OMU 1200CE4

E-01 - ajtó nincs becsukva, vagy nem nyit a program végén.

E-02 - 5-8 perce nem kap vizet (megelõzi az OUt jelzés)

E-03 - nem ürít

E-04 - túltöltött vagy szivattyú szakadt

E-05 - fûtõbetét vagy NTC hiba (túlfût/nem fût)

E-06 - motor hiba (szakadás)

E-07 - motor hiba

E-08 - hálózati fesz túl magas vagy túl alacsony 260V< fesz <150V

OUt  - nem kap vizet, vagy alacsony hálózati feszültség.

-----------------------------------------------------------------------------

WHIRLPOOL AWM-6080, AWM-6100, AWM-6105, AWM-6122, AWM-8105, AWM-8123, AWM-8125, AWM-8142

FH (F01) szelep hiba (nem vesz vizet /6 perc után)

FA  Aquastop aktiv

FP (F03) nem ürit (vízszintszab. vagy sziv. hiba /6 perc után)

F05 NTC (szakadt v. zárlatos)

F06 Tachogenerátor jel nincs

F07 Motor triak zárlatos

F09 Túltöltés

F11 Kezelõegység hiba (12C bus)

F14 EEPROM hiba

F16 Kezelõegység hiba

F18 Kezelõegység hiba

F20 Kezelõegység hiba

F21 Kezelõegység hiba

-----------------------------------------------------------------------------

WHIRLPOOL AWO/D 45135, AWO/D 43136, AWE2214, AWE2316, AWE6514, AWE6516, AWO5125

Villáskulcs piros LED-je ég + START villog + folyamatjelzõk adják a hibakódot (EDCBA)

EDCBA

---x- 02 FA  AQUASTOP aktív túltöltés

--x-- 04 F04 fûtõbetét hiba 30C-ot nem éri el 40 perc alatt, vagy NTC hiba

--x-x 05 F05 NTC hiba (szakadt vagy rövidzár)

--xx- 06 F06 Tachogenerátor hiba

--xxx 07 F07 Motor vezérlés hiba (vezérlõ panel) (fûtõbetét+terhelni a motort!!!)

-x--- 08 F08 Fûtõbetét hiba (szakadt?, testzárlat?)

-xx-- 12 F12 Fûtõbetét hiba (szakadt?, testzárlat?)

-xx-x 13 F13 Ajtó nyitva

-xxx- 14 F14 EEPROM hiba

-xxxx 15 F15 Dobpozicionáló jeladó hiba

x--x- 18 Fod Hab érzékelése

x-x-x 21 F21 Kezelõegység hiba

x-xxx 23 F23 Vízszintszabályzó hiba (fűtőbetét testzárlat?)

xx--- 24 F24 Túltöltés

xx-x- 26 F26 Szivattyú vezérlési hiba (panel hiba)

xx-xx 27 F27 Motor irányváltási hiba (panel hiba) csak tesztprogramban

xxx-- 28 F28 Motor csatlakoztatási hiba

-----------------------------------------------------------------------------

Whirlpool AWE-8525, AWE-8725, AWT-7105, AWT-7125, AWT-8127

PF = Power Failure?

FH  H O O O viz hiány

FA  O H O O aquastop

FP  H H O O szivattyú

F4  O O H O fütõbetét vagy NTC hiba

F5  H O H O NTC hiba

F6  O H H O tachogenerátor hiba

F7  H H H O motorvezérlés hiba (panel)

F8  O O O H fütõszál vezérlési hiba (panel)

F9  H O O H vizszint szabályzó hiba

F11 H H O H kezelõegység hiba

F12 O O H H fütõbetét hiba

F13 H O H H vizeloszto egység hiba

F14 O H H H eeprom hiba

F15 H H H H dobpozicionáló érzékelõ hiba

-----------------------------------------------------------------------------

WHIRLPOOL mosogatógép (966)

kijelzõ/startlámpa

F1/1x  villan 1s szünet- NTC Failure (termiszot hiba)

F2/2x  villan 1s szünet- Water Leakage (túlfolyásérzékelõ)

F3/3x  villan 1s szünet- Failure in Heating System (fûtési hiba)

F4/4x  villan 1s szünet- Draining Failure (szivattyúzási hiba)

F5/5x  villan 1s szünet- szórókar hiba (kijelzõ nem jelzi, csak villog)

F6/6x  villan 1s szünet- Water Tap Closed (vízszelep zárva)

F7/7x  villan 1s szünet- Flow Meter Failure (áramlásérzékelõ hiba)

F8/8x  villan 1s szünet- Water Level Failure (vízszintyzabályzási hiba)

F9/9x  villan 1s szünet- Continuous Waterinlet (indokolatlan folyamatos vízfelvétel)

F0/10x villan 1s szünet- Sensor Failure (szennyezõdés érzékelõ hiba)

FA/11x villan 1s szünet- OWI Fehler (vlmi túltöltés?)

FB/12x villan 1s szünet- MDV Fehler (?)

FC/13x villan 1s szünet- ASA Fehler (vízkeménységjelzõ)

LED Flasing - szórókar hiba

-----------------------------------------------------------------------------

WHIRLPOOL hatodik érzékes szutykokhoz

Whirpool Oven/Range/Stove Fault Codes (Including 2 and 4 digit codes)

Note: Depending upon the brand of appliance, there can be many different names for the 'clock' component. Electronic Range Control, ERC, Electronic Oven Control, EOC, control board, and clock all refer to the same part.

4 Digit Fault Codes

F1-E0 - EEPROM Communication Error - Disconnect power for at least 30 seconds and then reconnect. Allow at least a minute after power has been restored and if error code reappears, replace control board (clock).

F1-E1 - EEPROM Checksum Error - Disconnect power for at least 30 seconds and then reconnect. Allow at least a minute after power has been restored and if error code reappears, replace control board (clock).

F1-E2 - UL A/D Error(s) - Disconnect power for at least 30 seconds and then reconnect. Allow at least a minute after power has been restored and if error code reappears, replace control board (clock).

F1-E4 - Model ID Error - Disconnect power for at least 30 seconds and then reconnect. Allow at least a minute after power has been restored and if error code reappears, replace control board (clock).

F1-E5 - Calibration Shifted - Disconnect power for at least 30 seconds and then reconnect. Allow at least a minute after power has been restored and if error code reappears, replace control board (clock).

F1-E6 - Latch Signal Mismatch Error - Disconnect power for at least 30 seconds and then reconnect. Allow at least a minute after power has been restored and if error code reappears, replace control board (clock).

F1-E9 - Stack Overflow - Disconnect power for at least 30 seconds and then reconnect. Allow at least a minute after power has been restored and if error code reappears, replace control board (clock).

F1-E3 - Wiring Harness Cavity Size Does Not Match Stored Value - Check the jumpers in the harness to make sure they agree with the actual oven size.

F2-E0 - Shorted Touch Pad (Keypad) - Check the connection between the touch pad (keypad) and control board (clock) to make sure it is secure. Select the 'cancel' function and wait 60 seconds. If error code reappears then replace the touch pad, or touch pad and control board (clock) if all one assembly.

F2-E1 - Touch Pad (Keypad) Cable Unplugged - Check the connection between the touch pad (keypad) and control board (clock) to make sure it is secure. Select the 'cancel' function and wait 60 seconds. If error code reappears then replace the touch pad, or touch pad and control board (clock) if all one assembly.

F2-E5 - Cancel Key Line Open - Check the connection between the touch pad (keypad) and control board (clock) to make sure it is secure. Select the 'cancel' function and wait 60 seconds. If error code reappears then replace the touch pad, or touch pad and control board (clock) if all one assembly.

F2-E6 - Cancel Key Line Open - Check the connection between the touch pad (keypad) and control board (clock) to make sure it is secure. Select the 'cancel' function and wait 60 seconds. If error code reappears then replace the touch pad, or touch pad and control board (clock) if all one assembly.

All F3-E Codes - Oven Temperature Sensor (RTD) or Warming Drawer Defect - Replace oven temperature sensor (RTD).

F4-E1 - Meat Probe Defect - This error indicates a problem with either the probe, receptacle, or probe circuit. Check the probe for pinched wires and make sure there is no condensation or contamination on receptacle. If ok, replace probe.

All F5-E Codes - Door Switch Defect - This occurs when the door switches do not match. If door is latched, disconnect power from unit and check wires and connections. If damage is found, replace appropriate part. If connections are not damaged, reconnect power and hold down any key until the F5 error clears. Once the F2 code appears, select 'cancel' and observe for one minute for errors. If door is NOT latched, disconnect power from unit and check wires and connections. If damage is found, replace appropriate part. If connections are not damaged, measure door switch (door open = latch open) and latch switch (unlatch = switch open) and replace either if defective. If corrections are made during any step, power should be reconnected and the unit should be tested. Press and hold any key to clear the error code and F2 code should appear. Select 'cancel' and observe for one minute for errors. If error continues, disconnect power and replace control.

F6-E0 - Return Line Not Connected - This error should appear within 60 seconds after power up to appliance. Replace control board (clock).

F7-E1 - Common Switch Wire Is Defective - This error occurs when common wire to latch switch and door switch is shorted. Check all connections at control board and at the latch switch and door switch. If connections are ok, then check individual switches as outlined for the F5 error code. Note: Double ovens will have two of each switch and one common wire.

2 Digit Failure Codes

F0 - Control Board Failure - Replace control board (clock).

F1 - Control Board Failure - Replace control board (clock).

F2 - Oven Temperature Is Too High - Check for welded contacts on bake and broil relays. If present, replace control board (clock). For SELF CLEAN models, check door lock operation. Check sensor, sensor harness, and the sensor harness connection at sensor and oven control. Also check for any causes of high resistance in the oven temperature sensor circuit. Remember: The oven control board (clock) measures resistance of sensor circuit, not actual oven temperature.

F3 - Open Oven Temperature Sensor (RTD) - Replace oven temperature sensor (RTD).

F4 - Shorted Oven Temperature Sensor (RTD) - Replace oven temperature sensor (RTD).

F5 - Control Board Failure - Replace control board (clock).

F7 - Function Key Stuck - Replace control board (clock).

F8 - Control Board Failure - Replace control board (clock).

F9 - Oven Door Lock Failure - Check door lock switches and wiring. Check for stuck lock switch.

Back to Main Forum.

Whirpool Duet Front Loading Automatic Washer Fault Codes

FH - Detects No Water Entering Machine or No Pressure Switch Trip - Select 'cancel' twice to clear this code. If there is NO water in the unit, make sure the valves are turned on all the way. Check for plugged or kinked inlet hoses, as well as plugged screens in the inlet valves. Verify that the inlet valve is operational. If there is water in the unit, verify the drain pump is working and the pressure switch hose is in good condition and properly connected. Make sure there is not a siphon problem and check all hoses for possible leaks. Unplug the unit and disconnect the power to check all wire harness connections to the inlet valve, pressure switch, drain pump, flow meter, and Central Control Unit (CCU). Reconnect the unit and power to verify the pressure switch is operational, as well as the flow meter (blow air through the flow meter and measure resistance). Check CCU is also operational by performing a diagnostic test or any cycle. Replace failed component.

F02 - Long Drain (Drain Exceeds 8 Minutes) - Select 'cancel' twice to clear error code. Note: You may see a "SUD" error code appear first during this failure. This should change to the F02 error code after a few minutes. Proceed by checking the drain hoses for proper connection and kinks. Unplug unit and disconnect power. Check the electrical connections at the pump and make sure it is operational with no debris or blockage. Reconnect power and plug unit in. If problem has not been corrected, replace the pump.

F05 - Water Temperature Sensor Error - Unplug and disconnect power to the unit and check all connections to the water temperature sensor, heating element and element relay. Also check all components for defects. Replace failed component.

F06 - Drive Motor Tachometer Error (Unable to Detect Motor Speed) - Disconnect power and unplug unit. Check wire harness connections between drive motor and Motor Control Unit (MCU), and between MCU and the Central Control Unit (CCU). Reconnect power and plug unit in. Check the MCU by looking for operations of the drive motor, and check drive motor for powered rotations. Replace failed component. Note: If this failure occurs during high-speed spin, the door will be unlocked after three minutes.

F07 - Motor Control Unit (MCU) Error - Disconnect power and unplug unit. Check wire harness connections between drive motor and Motor Control Unit (MCU), and between MCU and the Central Control Unit (CCU). Reconnect power and plug unit in. Check the MCU by looking for operations of the drive motor, and check drive motor for powered rotations. Replace failed component. Note: If this failure occurs during high-speed spin, the door will be unlocked after three minutes.

F09 - Overflow Condition (Pressure Switch Closed Too Long) - Check to make sure drain hose is not plugged or kinked and unplug the unit and disconnect power. Check wire harness connections to pressure switch, drain pump, and Central Control Unit (CCU). Check for drain pump failure and clean it of any debris. Check the inlet valve and pressure switch for proper shut off and operation. Replace failed component. Note: If this error occurs, the door will remain locked and the drain pump will run constantly even if 'cancel' is selected. Turn off hot and cold water to faucets and unplug the unit before proceeding.

F10 - Motor Control Unit (MCU) Heat Kink Thermal Trip (Too Hot) - Check for proper installation and ventilation, and make sure unit is not located near a heat source. Disconnect power and unplug the unit to check wire harness connections to the motor, MCU, and Central Control Unit (CCU). Check the drive system for any worn or failed components and reconnect power and plug unit in. Check MCU by looking for operations of the drive motor and check drive motor for powered rotations. Replace failed component.

F11 - Serial Communication Error Between MCU and CCU - Disconnect power and unplug unit. Check wire harness connections to the motor, Motor Control Unit (MCU), and Central Control Unit (CCU). Check the drive system for any worm or failed components and reconnect power and plug unit in. Verify CCU is working by performing diagnostic test or any cycle. Check MCU by looking for operations of the drive motor and check drive motor for powered rotations. Also check the motor and wire harness. Replace defective part.

F13 - Dispenser Circuit Error - Disconnect power and unplug unit to check mechanical linkage from dispenser motor to top of dispenser. Check wire harness connections to the Central Control Unit (CCU) and the dispenser motor. Check dispenser motor for powered rotations. Replace failed component.

F14 - EEPROM Error - Disconnect power and unplug unit. Verify Central Control Unit (CCU) is operating properly by running a diagnostic test or any cycle. Replace is defective. Note: A power glitch may cause this error. Try unplugging unit for two minutes to see if that fixes error.

F15 - Motor Control Unit (MCU) Error - Disconnect power and unplug unit to check wire harness connections to the motor, MCU, and Central Control Unit (CCU). Check the drive belt and reconnect power and plug unit in. Check the MCU by looking for operations of the drive motor and check the drive motor for powered rotations. Replace failed component.

FdU - Door Unlock Error - It is possible the door lock mechanism is broken or the door switch/lock unit has failed. Check the door switch/lock for any debris or foreign objects. Disconnect power and unplug unit to check wire harness connections to the Central Control Unit (CCU) and the door switch/lock unit. Note: Unit will attempt to unlock itself during this error six times before displaying this error code. To manually unlock the unit, unplug the power cord from the outlet and remove the toe panel. Reach up along the inside of the front panel and locate the bottom of the door latch assembly, where there should be a tear-drop shaped tab. Gently pull the tab down approximately 1/4 inch or until a 'click' is heard. The door should now be unlocked.

FdL - Door Lock Error - It is possible the door lock mechanism is broken or removed, or the door switch/lock unit has failed. Disconnect power and unplug unit to check door switch/lock unit. Check the wire harness connections to the Central Control Unit (CCU) and the door switch/lock unit. Note: Unit will attempt to lock itself during this error six times before displaying the error code.

SUD - Suds Lock (Too Much Detergent Detected) - Make sure drain hose is not plugged or kinked and disconnect power and unplug unit. Check wire harness connections to pressure switch, drain pump, and Central Control Unit (CCU). Make sure the drain pump is free from debris or foreign objects and then reconnect power and plug unit in. Check drain pump and pressure switch and verify CCU operation by running a diagnostic test or any cycle. Note: This error may signify a bad pump, an extra heavy load, excessive detergent, or excessive suds. If too much detergent was used, run the unit through a Rinse/Spin cycle, and then run a Normal cycle without adding detergent.

Back to Main Forum.

Whirpool Duet Front Loading Gas and Electric Dryer Fault Codes

PF - Power Failure - PF error code indicates a power failure during the dryer's cycle. Press and HOLD start to continue the cycle, or press off/pause to clear display.

E1 - Open Thermistor - Replace thermistor.

E2 - Shorted Thermistor - Replace thermistor.

Back to Main Forum.

Whirpool Calypso Automatic Washer Fault Codes

PF - Power Failure - PF error code indicates a power failure during the dryer's cycle. Press and HOLD start to continue the cycle, or press 'Stop/Cancel' to clear display and cancel cycle.

FL - Flood Condition - FL error code will appear when the unit detects an overfill, or excessive amounts of water in tub. When this error occurs, the pump should be cycled in drain mode for 30 seconds on and 30 seconds off until the switch resets. Press 'Stop/Cancel' to clear display.

Er - Processor Reset Error - This error will only occur if the unit fails to save cycle information during a power outage. Press 'Stop/Cancel' to clear display.

LF - Long Fill - If the water fill time exceeds ten minutes, the water valves will be shut off and this error code will display. Press 'Stop/Cancel' to clear display.

CE - Communication Error - Disconnect power and unplug unit. Check for conformal coating on serial communication pins between the machine controller and the motor controller. Make sure the harness does not have a faulty connection by checking the resistance values between serial communication pins with the connectors in place.

Ld - Long Drain - This error code will appear if unit takes longer than 5 minutes to pump out water to the point where the pressure switch resets. Press 'Stop/Cancel' to clear display.

CA / CI - Average Current Limit / Instantaneous Current Limit - This error code may signify a problem with the drive motor, thermal protector, or motor controller. Overloading the unit may also cause this problem.

ob - Off Balance - The lid switch must be opened at least once before reseting the cycle. Opening the lid will allow you to redistribute the load to avoid a further off balance error. Press 'Stop/Cancel' to clear display.

Sr - Stuck Relay - The machine control board may have a bad relay and may need to be replaced. Check pins 1 and 5 of P16 of the machine controller and pins 1 and 2 of P1 of the motor controller. This should have AC line voltage when the motor controller is powered. Press 'Stop/Cancel' to clear display.

LS - Lid Switch Error - This error will occur if unit cannot detect the lid switch opening or closing. It is also possible this error code will appear is there is a disagreement between the motor and machine controllers. Open the lid or press 'Stop/Cancel' to clear display.

Flashing Display Time - Open Lid - This will only occur if the lid is opened during a running cycle. Close the lid and press 'Start' to continue.

SL - Suds Lock - This error will occur if the unit detects suds but is unable to clean them out. The unit will attempt the clean out the suds three times before displaying this error. It can also indicate a bad pump, an extra heavy load, excessive detergent, or excessive suds. Press 'Stop/Cancel' to clear the display.

Back to Main Forum.

-----------------------------------------------------------------------------

ZANUSSI FAE-825V, FAE-1025V, TE855V, EWT1011

A START gomb feletti adja az egyes helyiértéket

A pr. vége adja a tizeseket (ebbe az is beleszámít, amikor együtt villognak)

E11: Probléma a vízfeltöltésnél a mosóprogram alatt

E13: Lyukadás

E21: Probléma a kiszivattyúzásnál

E23: Probléma az alkatrésznél (Triac), amit az öblíto szivattyú vezérel

E24: Az alkatrész (Triac) „Sensing”-kör, amit az öblíto szivattyú vezérel, hibás

E33: Következetlenség a túlfutésvédelem érintkezo és a nyomásellenorzo 1. szint érintkezo zárása

között

E35: Vízszint túl magas

E36: A túlfûtésvédelem-nyomásellenorzo „Sensing”-kör hibás

E37: Az 1. szint „Sensing”-kör hibás

E39: A túlfutésvédelem-nyomásellenorzo „Sensing HV”-kör hibás

E41: Ajtó nyitása (elso rész – berendezés 3 érintkezovel)

E41: Ajtó nyitása (második rész – berendezés 4 érintkezovel)

E42: Probléma az ajtónyitásnál (elso rész – berendezés 3 érintkezovel) (nem nyit a retesz)

E42: Probléma az ajtónyitásnál (második rész – berendezés 4 érintkezovel)

E43: Probléma az alkatrésznél (Triac), ami az ajtókéslelteto egységet vezérli (elso rész)

E43: Probléma az alkatrésznél (Triac), ami az ajtókéslelteto egységet vezérli (második rész)

E44: Zárt ajtó „Sensing”-kör hibás

E45: Probléma az alkatrész (Triac) „Sensing”-körnél, ami az ajtókéslelteto egységet vezérli

E51: Triac motortáplálás rövidre van zárva

E52: Nem jelez a motor-tachogenerátor (elso rész)

E52: Nem jelez a motor-tachogenerátor (második rész)

E53: Probléma az alkatrész (Triac) „Sesing”-körnél , ami a motort táplálja

E54: A motorrelé érintkezok beragadva

E61: Nem kielégíto felfutés a mosóprogram alatt

E62: Túlfutés a mosóprogram alatt

E66: A futoegység relé érintkezo mindig zárva

E71: Mosóprogram NTC-szonda zavar

E82: Hiba a programválasztó törlés/ki pozíció kiolvasásánál

E83: Hiba a programválasztó-kód kiolvasásánál

E93: Készülék konfigurálási hiba

E94: Mosóprogram konfigurálási hiba

E95: Kommunikációs hiba a mikroprocesszor és a programtároló (EEPROM) között

E96: Következetlenség a kezelopanel változat és a konfigurációs adatok között

E97: Következetlenség a választó kapcsoló és a konfigurációs adatok között

EA1: Hibás a dobpozicionáló rendszer DSP (felültöltõs)

EA6: Hibás a dobpozicionáló rendszer DSP (felültöltõs) villogás simán vagy kódkiolv. 10+6

EB1: Hibás hálózati frekvencia

EB2: Túl magas csatlakozó feszültség

EB3: Túl alacsony csatlakozó feszültség

-----------------------------------------------------------------------------

MP 2009.11.01.