## Description

Description: UT658 USB tester is a device aimed at testing the quality of charging equipment (charger or power bank) used in computer, communication, and consumer electronics fields. The output voltage, current, capacity, and stability can be thoroughly tested with this device, which will help to prolong the charging equipment’s lifetime. UT658 can also test the quality of charging cables through its charging current, which can help users to quickly choose the right selection. Data reset and view,10 memory sets for energy consumption. Large LCD display and high-resolution make the reading clearly and easily. Small size, makes this multimeter easy to carry, and always ready to use. Specifications: Model: UT658. Material: plastic. Size: 67*29*12mm. Color: show as pictures. Input Voltage Range (V): 3V-9V. Voltage Resolution: 0.01V. Voltage Monitoring AccuracyL: ±1%. Current Monitoring Range (A): 0A~3A. Current Monitoring Accuracy: ±(1%±2). Current Resolution: 0.01A. Capacity: 0~9999mAH. Capacity Data Storage: 10 Groups. Display Way: LCD. Warning: yes. Buttons: yes. Contamination Level: 2. Working Temperature: 0° C~40° C. Storage Temperature: -10° C~50° C. Relative Humidity: <75%. Note: Due to the light and screen setting difference, the item's color may be slightly different from the pictures. Please allow slight dimension difference due to different manual measurement. Package Include: 1 * UNI-T UT658 USB Tester.