| d | Function (pictographic model) | Unit |
| --- | --- | --- |
| 1 | "Coffee" cycle number | unit |
| 2 | "Steam" function number | unit |
| 3 | Cleaning number | unit |
| 4 | Scale removal number | unit |
| 5 | Cleaning & Scale removal warning overrides: Total of number of cycles (coffee or steam) carried out after Cleaning or Scale removal light has come on No zero reset | unit |
| 6 | Writing index of the last fault (0,1,2,3): Depending on the index displayed, consult the corresponding fault in line 7, 8, 9 or 10 See penultimate fault in the previous index (1 if index 2 displayed, 3 if index 0) | code |
| 7 | Index 0 fault | code |
| 8 | Index 1 fault | code |
| 9 | Index 2 fault | code |
| 10 | Index 3 fault | code |
| 11 | Total coffee volume (exclusive of actuator volume and pre-soaking) | mL |
| 12 | Times switched on number | unit |
| 13 | Operating time: ON/OFF light on | min |
| 14 | Rinsing number | unit |
| 15 | Auto cut-off duration, (1,2,3,4,5 hours) | hour |
| 16 | Water hardness (scale removal frequency), (level 0,1,2,3,4) | value |
| 17 | Coffee temperature (level 1,2,3) | value |
| 18 | Cakes in the tray number | unit |
| 19 | Coffee cycles carried out since the last cleaning | cycles |
| 20 | Number of cycles carried out since the last scale removal (coffee, steam, water wieghtings) | cycles |
| 21 | Number of tray emptyings before cleaning of draw | cycles |
| 22 | Extra grinding time added to basic time | 0,10, 20,30, 40 |
| 23 | Flag indicating whether injection of coffee is possible or not (actuator down or not): 1=fault (actuator in low position) | 0/1 |
| 24 | Flag indicating blocking of coffee, steam: positioned if machine cut off during cleaning or scale removal. 1=fault | 0/1 |
| 25 | Number of grindings | Unit |
| 26 | Software version | code |
| 27 | Date of board production | dd-mm-yy |

Exit from A-S mode via 0/1 key.