SERVICE MODE MENU

To enter service menu; open the “OVERVIEW	“ menu (keep the menu item cursor on the “Exit” item) and pres “ 1 9 2 3 ” .

- SERVİCE MENU :

    - Sw version

    - Setup

    - Geometry

    - Video

    - Sound

    - Pip Service

    - EEPROM Reset

Service Version : It shows software version.

Setup : It includes CRT, OSD, TXT,Tuner,Scart, No Signal adjustmens-options.

Geometry : All geometry adjustments can be done via this menu.

Video : Video adjustments (white point,Black level etc.)

Sound : This submenu includes sound adjustmens and options like Prescale values of FM,NICAM,Scart,LL’. Also tv systems can be choosen in this menu.

Pip Service : With this menu, Some Pip adjustmens can be done. Pip frame color, frame width etc.

EEPROM Reset : This is used for reset the TV. All geometry, sound, setup, pip values are set the default values.

- Setup Menu :

- CRT Type

- Translucency

- TXT Language

- Main Tuner Selection

- Pip Tuner Selection

- Main Tuner AGC

- OSD Brightness

- TXT Brightness

- OSD Contrast

- TXT Contrast

- Scart3 Option

- SVHS Option

- No Signal Status

CRT Type :

Options : 16/9 Tube – 4/3 Tube

This item is for tube type selection.

Translucency :

Adjustments : 0 … 128 step.

This is related to OSD visibility. At 0, it is hardly visible, at 128 OSD is solid.

TXT Language

Options : East – West

This is Teletext language option.

Main Tuner Selection :

Option : orega – samsung – philips – alps

After replacing the main tuner with the new one listed above, this option must be set.

Pip Tuner Selection :

Option : orega – samsung – philips – alps

After replacing the pip tuner with the new one listed above, this option must be set.

Main Tuner AGC :

Adjustment : -15 … 15

Default Tuner AGC value is “0” .  (Pip AGC adjustmen is in “Pip service” menu)

OSD Brightness :

Adjustment : 0 … 255

Default value is 50. Low values make the OSD dark.

TXT Brightness :

Adjustment : 0 … 255

Default value is 20. Low values make the Teletext dark.

OSD Contrast :

Adjustment : 0 … 64

Default value is 8. Low values make the OSD Black.

TXT Contrast :

Adjustment : 0 … 64

Default value is 7. Low values make the TXT Black.

Scart 3 Option :

Option : on – off

It should be off if the third scart is not available on the hardware.

SVHS Option :

Option : on – dvd – dvd logo – off

It configures the SVHS input. If DVD available on the hardware, then it can be set dvd. DVD logo option is for starting-up with DVD logo on the screen.If there is no SVHS input, it should be set to “off”

No Signal Status :

Option : on – off

If this option set to off, TV never shuts down in case of no signal available. It should be use at the time of production. Default value is “on”

- Geometry Menu

- V-Slope

- V-Position

- V-Amplitude

- V-S correction

- H-Blanking

- H-Shift

- EW- Width

- EW- Pin cushion

- EW- Trapezium

- EW- Upper Corner

- EW- Lower Corner

- H-Parallelogram

- H-Bow

- EW-EHT compens.

- Restore Default

This menu is for tube geometry  adjustmens.

- Video Menu:

- G2 Alignment

- White Point R

- White Point G

- White Point B

- Peak White Limiter

- Black Level Offset R

- Black Level Offset G

- Gain Pre-scale RGB

- Fast Blanking Delay

- Luma Chroma Delay

- Restore Default

- Brightness Offset

G2 Alignment :

To adjust G2, press left or right navigation key on the RC. There is a message box at the bottom of the screen. Increase or decrease the G2 until “G2 is ok.” Message appear in the message box.

White Point R :

White Point G:

White Point B :

Adjustment : 0 … 63

Black Level Offset R

Black Level Offset G

Adjustment : 0 … 15

These are for white balance adjustments. This adjustment is done automatically at the factory. If it is have to do with manually, these items can be used.

Peak White Limiter :

Adjustment : 0 … 15

It puts a limit for white points in dark scenes. Default value is “0”

Gain Pre-Scale RGB

Adjustment : -32 … 32

It adjust the scart input RGB level. Default value is 0.

Fast Blanking Delay :

Adjustment : -8 … 7

Default value is “0”.

Luma Chroma Delay:

Adjustment : -8 … 7

Default value is “0”.

Restore Default :

Reset values.

Brightness Offset :

Adjustment : -5 … 5

This is an offset value for OSD brightness. Default value is -2.

- Sound Menu

- L/L’ AGC Adj.

- PreSclScart

- PreSclFM

- PreSclNICAM

- ResvSndTh

- PreSclMONO

- TR

- BG

- DK

- I

- MN

- Default System

L/L’ AGC Adj. :

Adjustment : 0 … 20

Default value is 7. Adjust the L/L’ Agc level.

PreSclScart :

Adjustment : -24 … 24

This is for scart input sound level scale. Default value is “0”.

PreSclFM :

Adjustment : -24 … 48

Front End sound input level scaler. Default value is 19

PreSclNICAM :

Adjustment : -12 … 48

Front End NICAM sound input level scaler.

Resv Snd Th

Should be “0”

PreSclMONO :

Adjustment : -24 … 24

Front End MONO sound input level scaler. Default value is 5

TR :

Option : on – off

This is for Türkiye. It should be “off” in Europa.

BG :

DK:

I :

MN :

Option : on – off

These are TV systems. If multi-system tv feature is available on the tv set, all systems shoul be “on” except “MN”. MN system never be “on”.

Default System :

Option : BG – DK – I

- Pip Service

- Frame Color

- Frame Width Vert.

- Frame Width Hor.

- Pip Tuner AGC

This service is available if required hardware is mounted.

Frame Color :

Option : 0 – 1 – 2 – 3 – 4 – 5 – 6 – 7

0 : Black, 1 : Red, 2: Green, 3: Blue 4: Yellow, 5: Dark Gray, 6: Light Gray, 7: White. Pip frame color can be choosen one of them above.

Frame Width Vert. :

Option : 0 … 6

Frame vertical thickness is getting thick from 0 to 6. Default value is 3.

Frame Width Hor. :

Option : 0 … 4

Frame Horizontal thickness is getting thick from 0 to 4. Default value is 3.

Pip Tuner AGC :

Adjusts Pip tuner AGC value.

Warning : This is available if a Pip tuner mounted to the chassis. If any adjustment attemp without Pip tuner causes the software crash and restart the TV set.