VCT49xyl UOC

szervizmódok

- Beko C8 sasszi (CRT):

To enter “SERVICE MENU”  , edit “9301”  by remote control while main menu on the secreen.To exit from service menu, press TV/TXT button.

- Beko K1 sasszi (CRT):

To enter the Service Mode, ‘Service In/Out” button on the Service Remote Control or activate the “Picture Menu” with the user remote control and press “9301” (Press “0” button to exit the Service Mode). To exit from the service menu, TV/TX button should be typed on the Remote Control.

- Profilo-Telra PT1000 sasszi (TFT):

Service mode code - 1923

The Service Mode is activated by pressing ‘1923’ on the Remote Control, while the set is in the Main User Menu. The software provides menu flexibility and full control to the software. Service persons can adjust the TV in all manners. In the Service Menu, you find a list of parameters.

- Panasonic GP4 sasszi (CRT):

1. Set the Bass to maximum position, set the Treble to minimum position, set the Volume to minimum then press the down button (-/v) on the customer controls at the front of the TV and at the same time press the INDEX button on the remote control, this will place the TV into the Service Mode 1.

2. Press the RED / GREEN buttons to step up / down through the functions.

3. Press the YELLOW / BLUE buttons to alter the function values.

4. Press the OK button after each adjustment has been made to store the required values.

5. To exit the Service Mode, press the "N" button.

- Vestel 17MB21 sasszi (TFT):

SOFTWARE UPDATE AND AUTO CALIBRATION PROCEDURE

It is necessary to load LPT Driver, Visual I2C program and some .dll folders for starting software update process. Please load that important folders.

1) Setting up the LPT Driver

- Please set up the Setup_LptDrv….exe

- Please copy the .dll folders into the C:/Windows/System32.

- Please make a folder as C:/ProgramFiles/Micronas and create LptDrv into this

Micronas folder. (System creates all of that folders autometically, when Setup_LptDrv….exe is loaded)

- When Start→Programs → Micronas → LptDrv → LptDrvTest.exe is opened, a window appears like below.....

- LG ML041A, B sasszi (TFT):

1) Press the IN-START Key to convert to the adjustment

mode using the adjustment (SVC) remote controller, and

press VOL+ Key at the AutoGain menu.

2) Once the adjustment is completed, press the Enter Key to

save and finish the adjustment

- Samsung KS7A sasszi (CRT):

Service mode belépés:  Bekapcsolt TV-nél nyomd meg egymás után a távirányítón a következő gombokat:

power off – INFO – MENU – MUTE  – power on

- Samsung GMR23, 26 HEU sasszi (TFT):

Power Off - INFO - MENU - MUTE - Power On

- Samsung VC17EO, VE20EO sasszi (TFT):

Power Off - INFO - MENU - MUTE - Power On

- LG MC049A, C sasszi (CRT):

LG szervizmódok

(MC sasszik)

1) Egyszerre nyomjuk be az OK gombot a távirányítón és a készüléken.

2) Egyszerre nyomjuk be a MENU gombot a távirányítón és a készüléken.

(előbb a távon, ekkor megjelenik a menü, majd a készüléken, ekkor eltűnik a menü, és mindkettőt tartsuk benyomva, amíg megjelenik a szervizmenü)

- Grundig LC32IEA2 (TFT):

Service and Special Functions

Start of the Service Mode: Via " i " –> Service Code "8500"

Call up the Menu: Press button P+ / P– –> button "OK"

Adjustment: Press button  /  or "OK"

Break of the Menu: Press button " i "

End the Service Mode: Press button " i " after break of Menu

LG szervizmódok

(MC sasszik)

1) Egyszerre nyomjuk be az OK gombot a távirányítón és a készüléken.

2) Egyszerre nyomjuk be a MENU gombot a távirányítón és a készüléken.

(előbb a távon, ekkor megjelenik a menü, majd a készüléken, ekkor eltűnik a menü, és mindkettőt tartsuk benyomva, amíg megjelenik a szervizmenü)