FACTORY MODE

  - For remote controller of user

Push  [menu] key, -> display picture manual  -> push digital key 6483 -> enter into factory setting .

Push [standby] key , exit factory mode and TV will be standby.

If you want to enter “M5~M0”, push “lock” (lakat), then choose the relative number you want (5. 6...0).

3.2 BUS OPEN:

Push [-/--] key for in /out  BUS OPEN

3.3 Passport for child lock [4100]

3.4 Factory menu:

| MENU1 | Range |  |  |  |
| --- | --- | --- | --- | --- |
| V.SLOPE | 0~63 |  |
| V.SHIFT | 0~63 |  |
| V.SIZE | 0~63 |  |
| V.SC | 0~63 |  |
| H.SHIFT | 0~63 |  |
| PROGRAM NO | 0~199 |  |

Receive standard Crosshatch pattern signal for PAL system .

a)   Adjust VSLOPE value: to the horizontal line just appear from

half bottom shadow.

b) 	 Adjust VSHIFT value: the center horizontal line correspond to

CRT vertical center.

c) 	 Adjust VAMP value: to get 90% of vertical picture contents would be displayed on CRT.

d) 	 Adjust HSHIFT value: to get the picture horizontal center correspond to CRT horizontal center.

e) 	 Receive standard Crosshatch pattern signal for NTSC system, and again adjust.

| MENU2 | RANGE | YOU CAN CHOOSE |
| --- | --- | --- |
| AGC | 0~63 | 26 (32) |
| SEARCH SPEED | 0~3 | 0 |
| SHIPPING |  |  |

Receive 60dBu (1mV)VH color bar signal to adjust AGC value voltage, from high to low, to

picture noise reduce gradually to be just disappeared.

Select “shipping”, push [V+] [V-]key to be shipped.

| MENU3 | RANGE | YOU CAN CHOOSE |
| --- | --- | --- |
| BT | 0 ~ 100 | 75 |
| CT | 0 ~ 100 | 75 |
| SC | Ug2 beállítása |  |
| RB | 0 ~ 63 | 32 |
| GB | 0 ~ 63 | 32 |
| RD | 0 ~ 63 | 32 |
| GD | 0 ~ 63 | 32 |
| BD | 0 ~ 63 | 32 |
| SB | 0 ~ 63 | 32 |

Receive gray and white 2 steps signal.

a) CRT cut off adjustment.

- push [P+][P-] key to select “SC”, push [V+][V-] key then automatically vertical scan will be stopped.

- adjust SCREEN control on Flyback transformer to get the darkest single horizontal line (red,green,

or blue, sometimes shows more yellow, more purple or more white).

- push [V+][V-] key again, vertical scan work repeat.

b) white balance adjustment.

  - select RD/BD menu.

  - adjustment RD/BD to get color temperature as x=281, y=311.

c) sub-brightness adjustment (use stair case signal)

- select SB MENU.

- adjust SB to get the darkest step being out off.

| MENU4 | RANGE | YOU CAN CHOOSE |
| --- | --- | --- |
| OSD V.POS | 0~28 | 15 |
| OSD H.POS | 0~63 | 53 |

*WHEN “SCART”  push “PIN5” to “RGB”

LOGO Setting

First enter the factory setting menu  M9, choose LOGO item, setup to “ON”, exit menu  M9, press  [MENU2] or press  “calendar “key ,  press TV/AV  you can choose the following  items , if you want to exit ,pls  press “CALL”

- CHANGE ALL HIGH press   ”V+ or V-“, to change the LOGO height .

- CHANGE POSITION press  ”V+ or V-“, change LOGO position of left and right. Press “P+ or P-“ to change LOGO position of  up and down.

- CHANGE LINE1 SIZE press “V+ or V- “ change  the first line letter position

- CHANGE LINE2 SIZE press “V+ or V- “ change  the second  line letter position.

- CHANGE LINE1 COLOUR press “V+ or V- “  change  the first  line letter color (8 colors).

- CHANGE LINE2 COLOUR press “V+ or V- “ change  the second  line letter color (8 colors).     CHANGE DISTANCE press “V+ or V- “ change  the second  line letter position

- CHANGE CHARACTER press “V+ or V- “ choose the  position of letter . Press “P+ or P-“ you can write the letter with forward direction and reverse .

LOGO description press “P+ “ will appear follows

| - | . | / | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 9 | ： | ； | 《 | = | 》 | ？ | A | B | C | D | E |
| F | G | H | I | J | K | L | M | N | O | P | Q |
| R | S | T | U | V | W | X | Y | Z | a | b | c |
| d | e | f | g | h | i | j | k | l | m | n | o |
| p | q | r | s | t | u | v | w | x | y | z |  |
| ! | ” | % | ’ | ( | ) | * | + | , |  |  |  |  |  |

# Text boxes

| MENU5 | RANGE | YOU CAN CHOOSE |
| --- | --- | --- |
| PP MODE |  | STANDARD |
| BRIGHTNESS | 0~100 | 75 |
| CONTRAST | 0~100 | 75 |
| COLOR | 0~100 | 50 |
| SHARPNESS | 0~100 | 50 |
| SC BRIGHTNESS | 0~63 | 30 |
| COOL BD OFFSET | 0~32 | 10 |
| WARM RD OFFSET | 0~32 | 10 |
| YD PAL | 0~15 | 12 |
| YD NTSC | 0~15 | 12 |
| YD SECAM | 0~15 | 12 |
| YD AV PAL | 0~15 | 12 |
| YD AV NTSC | 0~15 | 12 |
| YD AV SECAM | 0~15 | 12 |

| MENU6 | RANGE | YOU CAN CHOOSE |
| --- | --- | --- |
| OSO | 0/1 | 1 |
| AGC SPEED | 0~3 | 1 |
| FFI | 0/1 | 0 |
| FSL | 0/1 | 0 |
| FMWS | 0/1 | 0 |
| HP2 | 0/1 | 0 |
| RPO | 0~3 | 1 |
| NTSC MATRIX | JAPAN/USA | USA |
| Vol Pin | PUSH PULL/OPEN DRAIN | OPEN DRAIN |
| Video Out | CVBS/IF | CVBS |
| PIN5 | NTSC/RGB | NTSC |

| MENU8 | RANGE | YOU CAN CHOOSE |  |  |  |
| --- | --- | --- | --- | --- | --- |
| CATHODE LEVEL | 0~15 | 6 |  |  |  |
| UOC VOLUME | ON/OFF | OFF |  |  |  |
| FM ATT | 0~63 | 40 |  |  |  |
| TDA9874 AVL | 0~3 | 0 |  |  |  |
| TDA9874 GAIN | 0-30 | 0 |  |  |  |
| DUAL OUT | ON/OFF | OFF |  |  |  |
| AUTO SOUND | ON/OFF | ON |  |  |  |
| HEADPHONE | 0~3 | 0 |  |  |  |
| TRUBASS | ON/OFF | OFF |  |  |  |
| Default lang | 0~16 |  |  |  |  |
| Lang opt |  |  |  |  |  |
| Lang SW | ON/OFF |  |  |  |  |
| CHOOSE THE LANGUAGE YOU WANT IN “LANG OPT” THEN PRESS THE “LANG SW”TO “ON” |

| MENU9 | RANGE | YOU CAN CHOOSE |
| --- | --- | --- |
| BAND MODE | 0/1/2 | 1 |
| START ON | 0~2 | 0 |
| ON DELAY | 6~15 | 6 |
| LOGO | ON/OFF | ON |
| NVM LOGO | ON/OFF | OFF |
| TXT BRIGHTNESS | 0~63 | 31 |
| SPANISH BIT | 0/1 | 0 |
| NOT0 | ON/OFF | ON |
| NOT1 | ON/OFF | OFF |
| NOT2 | ON/OFF | OFF |
| NOT3 | ON/OFF | OFF |
| NOT4 | ON/OFF | OFF |

Horizontal line

Shadow