11AK19-08A LOPTR(BU2508AF NOR NOD)+TCDT1102G/CQY80NG 150VN

11AK19-08A LOPTR(BU2508AF)+EW RASTER BUK444-200+R629(2R7)

11AK19-5 LO WIDTH/EW R629+EW CHOKE(ALV1034 CHAS HYDE)

11AK19-5 STBY , REMOVE EEPROM IC502(24LC08B)

11AK19-8 DEAD R806 22K

11AK19-8A LOPTX ARCING(ELDOR 4031800113/CPC TFFBT40681 /HR8029)

11AK19-8A WIDTH C630(0U27F),BUK444 +EW LOADING COIL(16MH)

11AK19-P4 BOWED SIDES R629(2R7)C630(680NF250V)

11AK19

11AK19 SERVICE MODE INSTALL MENU THEN 4725

11AK19 TV MAG APR/2005 PSU/STBY CIRCUIT Q807

11AK19 110DEG 150VN(27R) ONE4ALL=0037

11AK19 ALBA CTV5984 ALBA CTV6682A ONE4ALL=0037

11AK19 BUSH 2863NTXA BUSH 2866NTX BUSH 2867NTX BUSH 2868NTX

11AK19 BUSH 2871NTX LOPTX HR8029

11AK19 BUSH 2872NTX 2877NTX BUSH 2875NTX

11AK19 BUSH 2971NTX BUSH CTV2871NTX

11AK19 BUSH WS6671 BUSH WS6671GRN2

11AK19 DEAD/STBY C829(47UF160V)

11AK19 GOODMANS GTV288 GOODMANS GTV66N1 GOODMANS GTV66W1 GTV69W3

11AK19 HT=115VN ON 90DEG CRT 150VDC FOR 110DEG CRT

11AK19 INSTALL 00=35=RED 01=35=GREEN 02=35=BLUE 03=07 04=80

11AK19 INSTALL 08=004 09=006 10=4:3HEIGHT=020 11=4:3LSHIFT=018

11AK19 INSTALL 12=48 13=4:3VLIN=035 14=022=4:3HEIGHT 15=014=VLIN

11AK19 INSTALL 16=036=VLIN 17=4:3WIDTH=019 18=035=PIN

11AK19 INSTALL 17=4:3WIDTH 10,14,15,13=FIELD HEIGHT/LIN 13=VERTSHIFT 12=HSHIFT

11AK19 INSTALL 19=040=16:9HEIGHT 20=026 21=020 22=017

11AK19 INSTALL 23=TXTLINEPHASE=037 LSHFT 24=038=VLIN 25=022=16:9HEIGHT

11AK19 INSTALL 26=013=19:9HEIGHT 27=035=16:9VERTSHIFT

11AK19 INSTALL 28=16:9WIDTH=052 29=041=16:9EW=033

11AK19 INSTALL 31=023=16:9EW 32=011=ZOOMHEIGHT 33=042 34=037ZOOMLSHFT 35=042

11AK19 INSTALL 36=042 37=025=ZOOMHEIGHT 38=021=ZOOMTOPLIN

11AK19 INSTALL 39=045=ZOOMWIDTH 40=030=TRAP 041=012 42=022

11AK19 INSTALL 43=009=HEIGHT 44=063 45=037=HSHFT 46=045=VLIN 47=054=VH

11AK19 INSTALL 48=006=VH 49=013=VSHFT 50=045=HW 51=044=EW 52=018 53=048

11AK19 INSTALL 54=032=V 55=027=VSHFT 56=000=LSHFT 57=039=VLIN

11AK19 INSTALL 58=016=VLT 59=023 60=034=VERT

11AK19 INSTALL 61=049=HWIDE 62=025=EW 63=021 064=023 65=144=OSD.SHFT

11AK19 SERVICE MENU HOLD BOTH VOLUME BUTTONS 10 SECS

11AK19 SERVICE MODE ACCESS ENTER INSTALL MODE THEN PRESS "4725" TV=EXIT

11AK19 11AK10-15

11AK19 32" EW LO WIDTH,R629,RESOLDER ALL AROUND AREA TO LOPTR

11AK19 90 DEGREE 20" HT=114VN

11AK19 ARCING NOISE CRT,TR602

11AK19 BENT OSD/TEXT STARTUP TICK, SMALL COIL ON CRT BASE EARTH LEAD

11AK19 BENT SIDES EW C611 C610 C6626 C613 C630 Q603(BUK444),R629(2R7/27R)

11AK19 BLANK PIC,SND OK,R914(47R),TDA6108JF CAUSE CRT ARC ?

11AK19 BLANK RASTER CRT BASE SOCKET/PCB FROM CHS(ALB1614)

11AK19 BLANK RASTER SDA5255-A021 MICRO PRO

11AK19 BLANK RASTER TDA6108JF ON CRT BASE CAUSE CRT BASE PCB/SOCKET

11AK19 BLANK SCREEN. TOP RGB LINES,TDA8840, R704

11AK19 BLUE PICTURE SECAM,C415

11AK19 BRIGHT PIC FLYBACK LINES ,RESOLDER PIN 4 AND 5 ON MEMORY IC502

11AK19 BURNT SCAN COIL PLUG L604(SHOULD BE 2R7)

11AK19 CENTER SPOT ,Q601,C902,IC901

11AK19 COLORED SNOW,IC401,IC502

11AK19 CRT NECK ARCING,,CAUSE CRT BASE SOCKET(CPC AB3862021000)

11AK19 DARK PIC,R615,D608,D701,IC901

11AK19 DEAD 2.5AT FUSE CAUSE DEGAUSS POSISTOR

11AK19 DEAD 2A5T C804(220UF400V)

11AK19 DEAD 2A5T D802(UF4508)+D825(BA159)

11AK19 DEAD 320V OK, IC802,C807(1UF50V),R811(22K)

11AK19 DEAD 320V OK,HT LO AT 17V=STBY EEPROM(24LC08B/146 ON 90DEG/48CM)

11AK19 DEAD 320V OK,HT LO AT 40V TDA16846+OPTOISOL(TCDT1102G/CQY80NG)

11AK19 DEAD AFTER GREEN LED,D807(MR852/BA159)CATHODE TWARDS CHIP

11AK19 DEAD BUZ91 MC44604 ,D819(11V ZD),R835(22R)

11AK19 DEAD C833(220PF600V)+BRIDGE RECT DIODES,R817(2R25W)

11AK19 DEAD CHOPFET(2SK2545/BUZ90AF) D822(UF5407) D825()BA159*3 (2R2 5W)

11AK19 DEAD CHOPFET(3N60E/BUZ90A)+MC44604P+TCDT1102G (2R2 5W)

11AK19 DEAD CHOPFET(8SP7N60A)+R817(2R2)+MC44604P+CQY80NG(OPTO) CAUSE D816

11AK19 DEAD CHOPFET(BUZ80A+ISOL) Q802 R825 D807 D826 D827

11AK19 DEAD CHOPTX NOISE C829(47UF50V)

11AK19 DEAD D802 D804 D826,D827,R817,Q802

11AK19 DEAD D807(BA159/MR856),R822(22K)

11AK19 DEAD D811,R867(0R33)

11AK19 DEAD D823(UF5407),MC44604P

11AK19 DEAD GREEN LED FLASH R867(0R33)

11AK19 DEAD IC502,IC501,IC701,Q605,IC401, IC100,Q603,TR601,D603,D609, IC901,R605 11AK19 NO PIC,D609,IC901,IC401,IC701,IC502, IC501,Q601,D608,D701,C903, C708,Q701,Q426,D603,PL402

11AK19 DEAD LED BLINK,IC501,Q810,CRT,D605,IC801, IC401,IC901,D811,D812,Q605, IC100,Q805,Q806,Q807

11AK19 DEAD LED FLASHS LOPTX

11AK19 DEAD LED Q810,Q512,IC801

11AK19 DEAD LOPTR +JOINTS AROUND

11AK19 DEAD LOPTR(BU2508AF) ,CAUSE SCAN COIL PLUG

11AK19 DEAD LOPTR(BU2508AF) CAUSE CRT ARCING (LG TYPE W66QBD290X)

11AK19 DEAD LOPTR(BU2508AF), CAUSE HI HT

11AK19 DEAD LOPTR, EW FET,LED FLASHED 150VN LO AT 100V,D807 IN PSU

11AK19 DEAD LOPTR,LINK J613

11AK19 DEAD LOPTR,R629(2R7 OR 2R OR 68R),C617(1UF250V)

11AK19 DEAD LOPTX

11AK19 DEAD MC44604P+OPTO(TCDT1102G/CQY80NG)

11AK19 DEAD NO LEDS,C813(4700UF16V),R867(0R33)

11AK19 DEAD NOISE ,EW DOIDE D612(BY228)

11AK19 DEAD NOISE LO HT, C829(47UF160V) NR CHOPTX

11AK19 DEAD PSU OK,NO LINE DRIVE,CHECK EARTHS TO LOPTR/E TO ALL EARTHS

11AK19 DEAD PSU SQUEEK, NOISE ,EW DIODE D612(BY228)+ RESOLDER ALL CAPS

11AK19 DEAD PULSING,D606(BA159)

11AK19 DEAD PULSING,LO HT(20V 150VN) D814(+13V LINE MIDDLE ONE)

11AK19 DEAD R806(22K)LOC21,MC44604 LOC24

11AK19 DEAD R825(2M2)+R806(22K).

11AK19 DEAD SNUBBER CAP 2N2F 2KV ACROSS LOPTR+EW CHIP+C630(560NF250V)

11AK19 DEAD STBY.Q802,IC801,IC802,R806,R817, D801,D802,D803,D804,D807, D812,D823,Q810,TR802,F801,R813,R814,Q805,Q806,Q807, Q809

11AK19 DEAD TDA16846

11AK19 DEAD TICKING NOISE,C829(47UF250V)

11AK19 DEAD TICKS C827(470PF) IN PSU SECONDARY

11AK19 DEAD TICKS D807(BA159) IN PSU

11AK19 DEAD TICKS LOPTR(2SD2579/BU2508AF),C626(11N2KV/9N1/12N),R629(2R7/27R=11 0/56R=76CMW)

11AK19 DEAD TICKS LOPTR(2SD2579/BU2508AF),C626,R629(2R7/27R=110/56R=76CM)

11AK19 DEAD TICKS LOPTR(BU2508AF) (12NF2KV/9N1 ON 90 DEGREE CRT)

11AK19 DEAD TICKS LOPTR(BU2508AF) C613(10NF630V) LOC43

11AK19 DEAD TICKS LOPTR(BU2508AF),LOPTX(4031800111/HR8029),R629(2R7/27R=110/56 R=76CM)

11AK19 DEAD TICKS TDA2615

11AK19 DEAD TICKS TDA6108 ON CRT BASE PCB

11AK19 DEAD TICKS,BU2508AF/2SD2579,C626(11N2KV) ELDOR LOPTX(13420006)

11AK19 DEAD TICKS,LOPTR(BU2508AF),C626(12NF2KV)

11AK19 DULL FLICKY PIC, D608 RHS LOPTX.

11AK19 EW BENT SIDES C630(560N300V) Q603(BUK444/9NQ20T FET)

11AK19 EW BENT SIDES R629(56R/2R7/27R),C630(680NF250V ON 76CM)

11AK19 EW BENT SIDES,D612,L604,R629,Q603,IC401, D611,R606,C626

11AK19 EW BENT SIDES,R629(2R7),C630(430NF250V) ON A66EHJ43X01 CRT

11AK19 EW C613(12NF),C630(390NF250V GOES LO WHEN HOT) R629(2R7/27R=110/56R=76CM)

11AK19 EW C630(470NF)

11AK19 EW LO WIDTH R629(2R7)+RESOLDER ALL LOPTR AREA.

11AK19 EW RASTER C630(390NF250V)+2R7

11AK19 EW RASTER Q683(BUK444/PHF 9NQ20T)FET

11AK19 EW RASTER R629(2R7 3:4)/27R 16:9) 59CM=2R7

11AK19 EXCESS BRILL R914(47R) +TDA6108JF

11AK19 EXCESS BRILL R914(47R),TDA6107/TDA6108 ON CRT BASE PCB

11AK19 EXCESS BRILL TDA6107Q CAUSE CRT FLASHOVER

11AK19 EXCESS BRILL, TDA6107Q,R914(47R)

11AK19 FIELD COLLAPSE D606(BY157),TDA8351,R704(1R)

11AK19 FIELD COLLAPSE IC701(TDA8351),R704(100R) FROM LOPTX PIN5

11AK19 FIELD COLLAPSE IC701,IC401,IC901,IC502, R702, R703,D606

11AK19 FIELD COLLAPSE R704(100R),TDA8351,D606,C632(1000UF25V)

11AK19 FIELD COLLAPSE R704,TDA8351,D606 C632

11AK19 FIELD COLLAPSE TDA8356

11AK19 FIELD CRAMP PIN 6 OF IC701: +45V IC701,R704,IC502,C632,C702, R704,D605

11AK19 FIELD INT, SCAN COIL PLUG

11AK19 GREEN PIC,TDA6108JF

11AK19 GREY FLYBACK LINES, R914+IC901(ON CRT BASE PCB)

11AK19 HI HT, OPTO(CQY80NG)

11AK19 HUM BAR DEGAUSSING COILS

11AK19 INT BENT SIDES,L602

11AK19 INT BLANK RASTER,LINK J500

11AK19 INT BLUE PIC,TDA6108 ON CRT BASE PCB

11AK19 INT DEAD,L602

11AK19 INT NO SND VL301 NICAM PCB

11AK19 INT PIC,RESOLDER IC401(JUNGLE)

11AK19 JUST 4 COLOURED LINES SND OK,R704(100R)FROM PIN 6 OF THE FIELD CHIP

11AK19 LO HEIGHT/WIDTH TDA8351+C632(1000UF35V)

11AK19 LO WIDTH BENT SIDES R626 C630 (390NF,300V)

11AK19 LO WIDTH EW, R629(2R7/27R/56R),C630

11AK19 LO WIDTH, C630(430NF250V)+R629(2R7)

11AK19 LO WIDTH/EW Q603(BUK444-200A) R629 (2R7 FUSIBLE 90 DEGREE) 27R=110 DEGREE.

11AK19 LO WIDTH/EW Q603(BUK444-200A)R629(2R7): R629 (27R 110DEG TUBE)

11AK19 LOPTR 2SD2579 FIT BU2508AF

11AK19 LOPTR CAUSE SCAN COIL PLUG

11AK19 LOPTX ARCING(ELDOR 4031800113/CPC TFFBT40681 /HR8029)

11AK19 NO BLUE/YELLOW PIC TDA6108J

11AK19 NO COLOR IC401,X401,IC502

11AK19 NO LINE DRV,CAUSE LEAKY DIODE IN TDA( JUNGLE) HAVE TO UNSOLDER IT AND WITH A BATTERY, BLOW THE FAULTY DIODE.

11AK19 NO OSD PIN 45 OF IC501 : SANDCASTEL INPUT SIGNAL LEVEL MUST BE 4VPP (SCOP)

11AK19 NO OSD,PIN 38 AND 39 OF IC501: 4.5VPP OSC. SIGNAL (SCOP) ,PIN 26 OF IC401 : FAST-BLANK SIGNAL MUST BE +4VPP 11AK19 NO OSD,IC501,IC502,IC401,R486,Q420, R554,R488,L501,C511,C512

11AK19 NO PIC 3 COLOR LINES ,TDA8351+FUSIBLE

11AK19 NO PIC 3 MOVING LINES,TDA8351 FIELD CHIP

11AK19 NO PIC 4 COLOURED LINES R704(100R)FROM PIN 6 TDA8356.

11AK19 NO PIC BEAMLIMITER C604(47NF63V) S/C

11AK19 NO PIC C604(47NF63V)

11AK19 NO PIC CRT BASE PCB IC901(TDA6107Q)

11AK19 NO PIC CRT HEATERS LIT, LOPTX

11AK19 NO PIC IC401(TDA884X)

11AK19 NO PIC WHITE RASTER,TDA6108JF ON CRT PCB

11AK19 NO PIC,NO LINE DRV,C406(22NF)

11AK19 NO PIC/BLANK RASTER AQUADAG EARTH SHOULD READ 10K TO CHASSIS EARTH

11AK19 NO PIC/NO CRT HTRS,R611,PL602

11AK19 NO PIC/SND GREEN LED ON,145V OK,IC805(8V REG)

11AK19 NO PICTURE IN PIP,IC050

11AK19 NO REMOTE ACTION, MD501,IC100,IC501,IC502

11AK19 NO SCART SIGNAL TEA6415C

11AK19 NO SCART2 O/P R083(75R),R084(47R),RESOLDER SOCKET

11AK19 NO SND (MONO)SPEAKERS,IC100,IC502,IC401, Q402

11AK19 NO SND (SECAM L MONO) IC402

11AK19 NO SND (STEREO)SPEAKERS,SOUND BOARD,IC100,IC502

11AK19 NO SND IC100 PIN 5=12.5VDC IC100 PIN 7=+12.5VDC IC100 PIN 2=+12.5VDC IC100 PIN 9=INPUT

11AK19 NO SND IN THE NICAM MODE 11ST19A7,IC502

11AK19 NO T/TEXT ,SDA5255-A047

11AK19 NO TUNING(VST) PIN 6 OF TUNER: +5V DC ,PIN 1 OF TUNER: +2V DC (APROX.),PIN 2 OF TUNER: 0 TO33VDC,

11AK19 NO TUNING(VST)TU201,IC501,IC401,D604, Q502,Q510,Q508,Q501,Q407

11AK19 NO TUNING,(PLL)TUNER PIN 4 SCL 4.5VPP ,TUNER PIN 5 SDA 4.5VPP ,PIN 9 OF TUNER : +20V DC

11AK19 NO TUNING,(VST) TUNER PIN 3 +5V DC, (UHF) ,PIN 4 OF TUNER: +5V DC (VHF3) ,PIN 5 OF TUNER: +5V DC (VHF1)

11AK19 NO TUNING,PIN 7 OF TUNER : +5V DC,PIN 1 OF TUNER : +2V DC IC502,TU201,IC501,IC401, D604,Q407

11AK19 NO WIDTH/HEIGHT ADJUSTMENT,IC901,D609,C903,TR802

11AK19 NO/POOR PIC TRY S/C ACROSS BCI/EARTH ON CRT BASE ,TDA8843

11AK19 NO/SLOW PIC,C608(10UF250V).

11AK19 ODD COLORS , DEGAUSS POSISTOR

11AK19 OSD FAULTS ,D506,IC501,D507,D508,IC401, IC502

11AK19 PALE PIC,IC401 PIN 13: VIDEO SIGNAL INPUT 1.3VPP.IC401,IC701

11AK19 PIC LO WIDTH, C611,TR602,Q809

11AK19 PIC TOO WIDE, C611(2N2/2200PF2KV) LOC433,L602 LOC424

11AK19 PIC TOO WIDE, C621(1UF100V PLASTIC TYPE),L602 BEHIND LOPTX

11AK19 POOR EW WIDTH R629(2R7/27R=110/56R=76CM)

11AK19 POOR PIC ,LO A1'S CUT OFF RED CONNECTOR AND SOLDER DIRECT.

11AK19 POOR PIC R617(220K)

11AK19 POOR/NO SYNC ,IC401 PIN 13: VIDEO SIGNAL INPUT PALS MUST BE1.3VPP.IC502,Q407 11AK19 LINE FOLDOVER ,C611

11AK19 POWER SURGING/DEAD CRT

11AK19 PSU BLOWN CHECK FIELD OP CHIP

11AK19 SCAN COIL PLUG BURN UP L604(15MH 2R7N SEME TPAR2599 30002031).

11AK19 SND LO (MONO)IC401 PIN 55: 3V DC 2-500MVPP AUDIO 3-100MVPP RF SIGNAL Q401,IC100

11AK19 STBY C630(4U7F250V)L602(1MH),R629(2R7)

11AK19 STBY D816 NR CHOPTX

11AK19 STBY D825

11AK19 STBY GOOD HT,NO LINE DRIVE,D812(BYD33D),Q500(BC548),Q504(BC558)IN IF

11AK19 STBY GRN LED FLASH, R823(140K)

11AK19 STBY IC807

11AK19 STBY LED ON,Q810

11AK19 STBY LO/NO HT,EEPROM, FRONT REMOTE SENSOR

11AK19 STBY, R826(470K)R821(470K).

11AK19 STBY,CRT BASE PCB,TDA6108JK+R914(47R)

11AK19 STBY/DEAD LO HT,C829(47UF160V)

11AK19 TDA6109J CAUSE CRT BASE SOCKET

11AK19 TELETEXT,PIN 30 OF IC501 : VIDEO SIGNAL 1.2 VPPIC501,L501,IC502,Q702,R547,D506,D507,Q702

11AK19 TO BRIGHT,D408,IC401,IC502

11AK19 TOO WIDE BUK444 L604

11AK19 TOO WIDE/EW Q603(BUK444) L602 LOC42

11AK19 TRIP - TDA6107Q ON CRT BASE

11AK19 TRIP D814(UF5402) D815(UF5402) D816(UF5408)

11AK19 TRIP RED LED FLASHING,D807(BA159)

11AK19 TRIPPING, CHOPTX(TR802),CHOPTR GETTING HOT

11AK19 TUNER(CTT5045E) PIN 3=+5V(UHF) ,PIN 2 SWEEP 0-30V ,

11AK19 VERTICAL LINES ON PIC ,D420,Q810,D402,D601,IC401, C618, AQUA CABLE,C604,R717,C435,C436

11AK19 VESTEL R629(27R)+C630(560NF300V)

11AK19 W110DEG CAP=95.3 ACROSS LOPTR ON 200UF RANGE

11AK19 WARM NO PIC SND OK,TDA6108JF ON CRT BASE OR A1'S.

11AK19 WARM NO SND,CRACKLE/HISS, IC301 NICAM PANEL

11AK19 WIDESCRN ,EW LO WIDTH R629(2R7 OR 27R)+RESOLDER ALL LOPTR AREA.

11AK199B1 DEAD MC44604P OPTO CQY80NG

11AK19B DEAD R817(2R2 5W)+BRIDGE RECT

11AK19B DEAD TICKS LOPTR(BU2508AF)+RESOLDER LINKS BY LOPTX.

11AK19B LO WIDTH,NO PIC 3 COLOR LINES ,TDA8351+FUSIBLE R704(1R)

11AK19B WIDE SCREEN POWER PRESET CLOCKWISE IS HT DOWN HT=150VN.

11AK19B1 DEAD LOPTR,NO LINE DRIVE TDA8843(HOT) IN METAL CAN

11AK19E3 DEAD R806(27K)

11AK19E3 DEAD,R867(0R33)5V REG FEED.

11AK19E3 JUST FEW COLOR LINES NR TOP ,R704(100R) ON 45V LINE TO FIELD

11AK19E3 JUST SNOW, Q501(BF420)

11AK19E3 LED FLASHING R867(0R33).

11AK19E3 SPKR NOISE IN STBY,ADD 0U1F50V TWEEN D814 CATH AND D815 ANO

11AK19E3 SPKR NOISE IN STBY,R811(820K),R890(2M2),R821(470K),R826(470K)

11AK19E3 STBY IC805(8V REG),IC401(TDA8843)

11AK19E3 STBY LOPTR(BU2508AF)

11AK19E3 STBY Q805 Q806 Q833 Q834,IC401(TDA8843)

11AK19ES DEAD R867(0R33)+330K+CHOPTR(BUZ90)+CHOPTX+TDA4605-2.

11AK19ES DEAD R867(0R33)+CHOPTR +CHOPTX.

11AK19ES LOPTX 28" 110DEG 40348A-02 HT=150VN CLOCKWISE=DOWN

11AK19P DEAD D812(BYD33D)

11AK19P 1FS10DEG RAGGED VERTICALS,LOPTX 1342.0006/30002064 ARCING HR8029

11AK19P DEAD PSU CHIRPING DISCON TR802(Q816/MCR22-8) SCR MICROPRO

11AK19P DEAD R817(2R2) CHOPFET(2SK2545),D805(BA159)

11AK19P DEAD, D825(BA159)

11AK19P DEAD,CHOPFET(MTP6N60E),D822(MR856),D823(IN4148),MC44604P

11AK19P LOPTR(2508AF)+EW Q603(9NQ20T/BUK444-200A)WIDESCRN 28"

11AK19P TICKING LOPTX(1372.0006D/FBT40711/HR8339)

11AK19P3 INT NO/POOR LUMA, SUB PANEL NEXT TO VIDEO PROCESSOR. IC100(TDA9181P)

11AK19P4 /100D LO WIDTH, C630 560NF300V+R629(2R7)

11AK19P5 DEAD LOPTX(10593640 C/40348A-02/30002064=HR8029)+27R

11AK19P5 DEAD PULSING LOPTX(1342.0006B/HR8029)

11AK19POR DEAD PSU CHIRPING UNPLUG MICROPRO GREEN LED ? 115VN OK ?

11AK19PRO HITACHI 90DEG MONO HITACHI C2125T

11AK19PRO DEAD CHOPFET(MTP6N60E),MC46604,Q810(MCR22-6,SCR),Q806(BC548)

11AK19PRO DEAD D816(UF5408),CHOPFET,MC44604,D807,D826,D827,R814(47R),R817(2 R2 5W),L801,C848

11AK19PRO DEAD FAINT PSU CHIRPS,DISCON D818, IF PSU NOW OK IF IC804 HOT,MICROPRO

11AK19PRO DEAD Q810(MCR22-6,SCR),Q806(BC548)

11AK19PRO DEAD R817(2R2 5W)

11AK19PRO EXCESS BRILL/OFF TDA6108JF+R914(47R) CAUSE CRT FLASHOVER

11AK19PRO NO LINE DRV,,R866(0R33),IC805(8V REG),R628(2R2),Q603

11AK19PRO STBY D505(2.4V ZD) MICROPOR SUPPLY LINE

11AK19PRO SURGE STBY,D807(BA159)

11AK19PRO TICKING LOPTX(1372.0006/FBT40711/HR8339)

Hibajelenség:

11ak19-nél egy érdekes hibával találkoztam. Időnként a sorvégtranzisztor elszáll. A szóba jöhető kondenzátorokat ellenőriztem, ill. kicseréltem, a hiba mégis ismétlődött.

Oka1:

A sorvégtranzisztor emitterétől két átkötés – J612 és J613 - biztosítja a sorvégfok földelését. /Micsoda szellemes megoldás!/ Ezek rossz forrasztása okozta a visszatérő hibát. Még nagyítóval megnézve sem lehetett észrevenni. Ha valakinek tudtam segíteni ezzel már megérte.

Oka2:

A sorvégtranzisztort tönkretevő 11AK 19 -nél a kis sormeghajtó tranzisztor cseréje és a sok rejtett kontakthiba megszüntetése volt a megoldás.