PEAVEY SEMI-CONDUCTOR / TRANSISTOR CROSS-REFERENCE LIST

http://audiolist.cjb.net

ORIGINAL           ALTERNATE                 FIELD

IN-HOUSE            IN-HOUSE              REPLACEMENT            ORDER

NUMBER              NUMBER                 NUMBER               NUMBER           NOTES

TO-92

TRANSISTORS

2N3391(A)         SPS-953(A, B)          MPS-A18, 2N6539,     OBSOLETE     LEAD CONFIG. DIFF. ON

MPS-8097, 2N6520             SK-3919           70403919           3391

2N4249          SPS-690, 699-1,          2N5086, 2N4249        70404249    REPLACE WITH SPS

PN-2907A                                                  761 IN DIF. AMPS

2N3904        SPS-7239, MPS-3405,          MPS-8098            70403904   DIF. AMP REPLACE IN

MPS-3417, 30615,                                                  PAIRS

2N5550

2N4888             SPS-761               2N5400, 2N5401        70400761   DIF. AMP REPLACE IN

PAIRS

SPS761          2N5400, 2N5401                                 70400761   DIF. AMP REPLACE IN

PAIRS

2N5400          2N5401, SPS761                                 70400761   DIF. AMP REPLACE IN

PAIRS

2N5401         2N5400, SPS-761                                 70400761   DIF. AMP REPLACE IN

PAIRS

SPS-953 A, B*   SK-3919, MPS-8097,       2N3391(A), MPS-A18,     70403919      A=LOW NOISE

2N6520                   2N6539                        B=SUPER LOW NOISE

SK-3919         SPS-953(A, B),             2N3391(A)           70403919    2N3391 SEE ABOVE

MPS-8097, 2N6520

2N6520         SPS-953(A, B), SK-          2N3391(A)           70403919    2N3391 SEE ABOVE

3919, MPS-8097

SPS-690          2N4249, 699-1           2N5086, 2N4249        70404249

699-1         SPS-690, 2N4249           2N4249, 2N5086        70404249

SPS-7239         2N3904, 30615,        MPS-8098, MPS-3405,      70403904

2N5550                 MPS-3417

30615         2N3904, SPS7239                                 70403904

MPS-6530        2N3642, MPS6531              2N3642             70406530

MPS-6531        2N3642/MPS-6530              2N3642             70406531

MPS-6533        2N3638, MPS-6534             2N3638             70406533

MPS-6534        2N3638, MPS-6533             2N3638             70406533

Page 2

ORIGINAL       ALTERNATE              FIELD

IN-HOUSE        IN-HOUSE           REPLACEMENT         ORDER

NUMBER          NUMBER              NUMBER            NUMBER            NOTES

2N4403       2N3638, 2N6533,          2N3638          70406533

2N6534

2N3644       2N3638, 2N6533,          2N3638          70406533

2N6534

2N4401       2N3642, 2N5630,          2N3642          70406531

2N6531

786             2SD-78              2SD-786E         70400786

A13            MPS-A13               MPS-A13         70400013      NPN DARLINGTON

A63            MPS-A63               MPS-A63         70400063      PNP DARLINGTON

1815           2SC1815               2SC1815         70401815      NPN TRANSISTOR

2878           2SC2878               2SC2878         70402878

5550            2N5550               2N5550          70405550

2N3638     MPS-6533, MPS-6534,    2N3638, 2N3644      70403638

2N3644, 2N4403

2N3642     MPS-6530, MPS-6531         2N3642          70403642     3642 BACKSTAGE 30

(LIMITER)

TO-126

TRANSISTOR

SJE-5331     SJE-360, SJE-5919     MJE-243 CASE 77     70405331   LEAD CONFIG. MAY DIFFER

SJE-5332     SJE-5920, FT-417B    MJE-253, MJE-15029   70405332   LEAD CONFIG. MAY DIFFER

MJE-243/4        SJE-5331          MJE-243, CASE 77    70405331   + & - 42 VOLT RAILS ONLY

M-10049         SJE-5331                              70405331        SEE ABOVE.

MJE-253/4        SJE-5332              CASE 77         70405332        SEE ABOVE.

SJE-5986         SJE-5332              CASE 77         70405332        SEE ABOVE.

SJE-7036         SJE-5332              CASE 77         70405332        SEE ABOVE.

SJE-360    SJE-5331 SEE ABOVE                         70405331

SJE-6018           355-1          MJE-340, SJE-3517    70406018

SJE-6019                               MJE-350         70406019

SDS-7204           1034            2N6557, MPS-U10     70407204

SDS-7205     MPS-U60, BF-463,          MPS-U60         70407205   TUBE DRIVER, REPLACE

9058S, 0694                                                PAIR

Page 3

ORIGINAL     ALTERNATE            FIELD

IN-HOUSE      IN-HOUSE         REPLACEMENT         ORDER

NUMBER        NUMBER            NUMBER            NUMBER            NOTES

TO-220

TRANSISTOR

2005M        TDA-2005M           TDA-2005M        70402005         20W PWR IC

2008         TDA-2008            TDA-2008        70402008         12W PWR IC

2040         TDA-2040            TDA-2040        70402040       PWR OP-AMP IC

2152         SJE-2152             TIP-101        70402152      NPN DARLINGTON

2153         SJE-2153             TIP-106        70402153      PNP DARLINGTON

EP-430     TIP-31C, TIP-29C    TIP-31C, TIP-29C   70400430

EP-431         TIP-30C         TIP-30C, TIP-32C   70400431

TIP-29C        EP-430              TIP-31C        70400430

TIP-31C        EP-430              TIP-29C        70400430

TIP-30C        EP-431              TIP-32C        70400431

64278*     65837, SDS-7204,   2N3439, MJE-3439    70407204    TUBE DRIVER, REPLACE

1034                                                 PAIR

65837*     SDS-7204, 1034     2N3439, MJE-3439    70407204    TUBE DRIVER, REPLACE

PAIR

SJ-5884      MJE-15030        MJE-15028, TO-220   70405884    TUBE DRIVER, REPLACE

PAIR

CA-2004M                                           70402004

CA-2008                       TDA-2008, TO-220    70402008          12 WATT

TDA-2030                                           70402030       14 WATT TO-220

MJE-700T       SJE-5879        SJE-5879, TO-220    70400700      PNP DARLINGTON

MJE-800T       SJE-5880            SJE-5880        70400800      NPN DARLINGTON

SJE-5879       MJE-700T                            70400700

MJE-15030                                          70415030      NPN DRIVER 150V

MJE-15031                                          70415031      PNP DRIVER 150V

VOLTAGE

REGULATORS

LM-78L05                                           70407805        TO-92 5V REG.

MC-79L12                                           70407912       TO-92 12V REG.

7806                                             704007806      +6V REG. TO-220

Page 4

ORIGINAL     ALTERNATE      FIELD

IN-HOUSE      IN-HOUSE   REPLACEMENT         ORDER

NUMBER        NUMBER      NUMBER            NUMBER         NOTES

7810                                       70407810   +10V REG. TO-220

7812                                       70407812   +12V REG. TO-220

MC-7905CT                                    70427905       -5V REG.

7915                                       70400320      -15V REG.

7815                                       70400340      +15V REG.

MC-7824CT                                    70427824      +24V REG.

MC-7924CT                                    70427924      -24V REG.

MC-7815CK                                    70407815    +15V REG. TO-3

MC-7915                                     70407915    -15V REG. TO-3

MC-7824 CK                                   70407824    +24V REG. TO-3

TO-3 TRANSIS-

TORS

404118*       84140          2N3772         70484140         NPN

SJ-4096*      81200         MJ-15020        70481200   NPN 200V DRIVER

SJ-4097*      71200         MJ-15021        70471200   PNP 200V DRIVER

SJ-6343*      83180         MJ-15024        70483180   NPN 180V OUTPUT

SJ-6344*      81140         MJ-13330        70481180   NPN 140V DRIVER

SJ-6357*      84140         MJ-15003        70484140   NPN 140V OUTPUT

SJ-6387*      81180         MJ-13330        70481180   NPN 180V DRIVER

SJ-6392       83100     MJ-15015, 2N3055A   70483100   NPN 100V OUTPUT

SJ-6451*      83180         MJ-15024        70483180   NPN 180V OUTPUT

SJ-6465*                     MJ-4247        70406465   NPN TUBE DRIVER

SJ-6505*      73100     MJ-15016, 2N6228    70473100   PNP 100V OUTPUT

SJ-6506*      81180         MJ-15020        70481180   NPN 180V DRIVER

SJ6507*       71180         MJ-15021        70471180   PNP 180V DRIVER

SJ-6552*      81140         MJ-15018        70481180   NPN 140V DRIVER

SJ-6553*      71140         MJ-15019        70471180   PNP 140V DRIVER

SJ-8226*      84140         MJ-15052        70484140   NPN 140V OUTPUT

SJ-8227*      74140         MJ-15053        70474140   PNP 140V OUTPUT

Page 5

ORIGINAL     ALTERNATE         FIELD

IN-HOUSE      IN-HOUSE      REPLACEMENT      ORDER

NUMBER        NUMBER         NUMBER         NUMBER         NOTES

SJ-8306*       84200          MJ-15024      70484200   NPN 200V OUTPUT

SJ-8307*       74200          MJ-15025      70474200   PNP 200V OUTPUT

SJ-8332*       83180          MJ-15024      70483180   NPN 180V OUTPUT

SJ-8333*       73180          MJ-15025      70473180   PNP 180V OUTPUT

60142*        84140          2N3772        70484140   NPN 140V OUTPUT

62188         84140          2N3773        70484140   NPN 140V OUTPUT

62792*        84140          2N3055        70484140   NPN 140V OUTPUT

64601*        68271           1B05         70468271   CS-800 OUTPUT

67068*        68271           1B09         70468271    CS-800 DRIVER

SJ-63180                     MJW-3281A      70463180     NPN CS-150

SJ-53180                     MJW-1302A      70463180     PNP CS-150

66161*        83180           1B05         70483180   NPN 180V OUTPUT

67376         84140          2N5630        70467376     NPN OUTPUT

68271                        MJ-15024      70468271   CS-800 OUTPUT

73070                                      70473070   PNP-70V OUTPUT

83070                        MJ-3055       70483070   NPN-70V OUTPUT

MOSFET

TRANSISTORS

IRFP-360                        TO-3        70410360     N-CHANNEL

IRFI-634                       TO-220       70410634     N-CHANNEL

IRFP-9240                       200V         70419240     P-CHANNEL

RFM-1015                                     70420015

IRFP-350NM   USE 70900497   INSULATOR ONLY   70400350   HIGH POWER FET

IRF-634                                     70400634     N-CHANNEL

IRF-830                                     70400830     N-CHANNEL

BF-966S      DUAL GATE                      70400966     N-CHANNEL

VN-2222LL       TO-92       ENHANCEMENT      70402222

IRF-230                                     70420230

IRF-240                                     7040240

Page 6

ORIGINAL               ALTERNATE                    FIELD

IN-HOUSE                IN-HOUSE                 REPLACEMENT                 ORDER

NUMBER                  NUMBER                    NUMBER                    NUMBER                     NOTES

15N40*                 IRFP-350                                           70430350

IRFP-340                                               TO-3                70430340                 N-CHANNEL

IRFP-350                                               TO-3                70430350                 N-CHANNEL

IRFIP-351                                                                  70430351

634                                         IS0-220 PACKAGE             70410634              250V N-CHANNEL

* = Original in-house part obsolete; no longer available. N = Note: Save good devices left over for future use.

Our semi-conductors are selected for "safe operating area" and beta range. Commercially available equivalents may not

parallel these specs.

Page 7

Transistor Summary

*NOTICE*

When replacing power output devices, our designs do NOT require Banks or that all be replaced. We do require that any

defective device be replaced with the same part number by PEAVEY. DO NOT MIX BRANDS OR PART NUMBERS,

EXCEPTIONS LISTED BELOW.

ITEM NUM-                                                       NOTES

BER

64601                 No longer available; replace with RCA-68271, order by 70468271.

Driver output for 64601 is 68271, order by 70468271.

RCA-66161             No longer available. Replace with RCA-68271, order by 70468271. NOTE: Replacement of the

above devices with the RCA device 70468271 requires no circuit modification. Devices may be

mixed or totally changed over to 70468271.

SJ-6451               Motorola part 70406451. No longer available. Replace all ten in each module with 70483180.

DO NOT MIX 6451 with 831803. Driver output for 83180 is 70481180. Original driver number

was 6506.

SJ-8332               No longer available. Replace with 70483180. DO NOT MIX 8332 with 83180. Driver output for

83180 is 70481180.

SJ-6506               No longer available. Replace with 70481180. Driver output for 6343 (A&B), SJ-8332, or RCA-

68271.

SJ-6387               No longer available. Replace with 70481180. NOTE: DO NOT DRIVE 66161 with SJ-6387 OR

81180, Use 67068 or another 66161.

Motorola 6343 (A&B) No longer available. Replace with 70483180. O.K. to mix in pairs.

SJ-8332               No longer available. Replace with 70483180. NOTE: DO NOT MIX.

6344                  No longer available. Replace with 70481140. DO NOT MIX.

SJ-6552               No longer available. Replace with 70481140. DO NOT MIX.

SJ-6357               No longer available. Replace with 70484140. MIX IN PAIRS.

4096                  No longer available. Replace with 70481200. DO NOT MIX.

4097                  No longer available. Replace with 70471180. DO NOT MIX.

6507                  No longer available. Replace with 70471180. DO NOT MIX.

6553                  No longer available. Replace with 70471140. DO NOT MIX.

8226                  No longer available. Replace with 770484140. DO NOT MIX.

8227                  No longer available. Replace with 70474140. DO NOT MIX.

8306                  No longer available. Replace with 70484200. DO NOT MIX.

8307                  No longer available. Replace with 70474200. DO NOT MIX.

8332                  No longer available. Replace with 70483180. DO NOT MIX.

Page 8

ITEM NUM-                                                         NOTES

BER

8333                  No longer available. Replace with 70473180. DO NOT MIX.

Part numbering system for Peavey TO-3 power transistors. Example: 70484200 = Transistor/NPN/4 amps/200 volt.

CATEGORY/POLARITY/IC VALUE/BVCEO VALUE

704       X       Y        ZZZ

X = Odd number = (7) = PNP                         X = Even number = (8) = NPN

Y = Current value where "HFE" gain is specified.

PNP transistors will be "red ink, NPN transistors will be "black" ink.

ZZZ = Voltage value where ICEO is specified.

ORIGINAL               ALTERNATE                   FIELD

IN-HOUSE                IN-HOUSE                REPLACEMENT                   ORDER

NUMBER                  NUMBER                   NUMBER                      NUMBER            NOTES

SPECIAL

APPLICATIONS

PARTS

4025                                           MAC-525-6                 70404025       400V 25A TRIAC

Q4040P                                                                      70404040       400V 40A TRIAC

2N6346A                 SAC-187                                             70416346       200V 12A TRIAC

MAC-97                                          TO-92 CASE                 70400097        6A 400V TRIAC

TRIAC 99                                                                    70400099       400V 16A TRIAC

SAC-187                                            2N6346A                  70400187       200V 12A TRIAC

MAC-252-6                                      MAC-525-7/8/9/10              70400525       400V 25A TRIAC

MAC-223                                         TO-220 CASE                 70400223       25A 200V TRIAC

SBS-14                MBS-4992                     TO-92                   70400014         8V SWITCH

M0C-635A                                                                     70400635       OPTO-COUPLER

2IL628                                                                     70240102            LDR

21L565                                                                     70240101            LDR

SBS-14                                           MBS-4992                  70400014      TO-92 8V SWITCH

CL-60                                                                    70240200   IN RUSH CURRENT LIMITER

TDA-1074                                                                 704001074       DC CONTROLLED DUAL

POT

POT DITIGAL                 POT                     70401267                   14-PIN       DUAL DIGITAL POT

DIODES

FEP-16                                            POSITIVE                 70400009        HALF BRIDGE

Page 9

ORIGINAL    ALTERNATE          FIELD

IN-HOUSE     IN-HOUSE       REPLACEMENT     ORDER

NUMBER       NUMBER          NUMBER        NUMBER         NOTES

FEP-16                       NEGATIVE      70400010     HALF BRIDGE

1N34A        US-270                        70400034   5MA, 60V, GERM.

HER-130      MUR-120                       70400103     200V, 1AMP

1SS142                                     70400142   250V, SWITCHING

MUR-150                                    70400150     1 AMP, 500V

FEN16GT                                     70400160     HALF BRIDGE

FEP16GT                                     70400161     HALF BRIDGE

B-400*       IR20F-20        GEA-327B      70400400    10A, 200V STUD

P-300D    1N5402, 1N5403                   70400502     200V, 3 AMP

MR-502    1N5403, 1N5402                   70400502     200V, 3 AMP

BB-619A   SURFACE MOUNT                    70400619    TUNING DIODE

BAR -74S   SURFACE MOUNT                    70400740         G.P.

1N747A                                     70400747    3.6V, 5% ZENER

1N 751A                                    70400751    5.1V, 5% ZENER

MR-752       P-600D                        70400752     6 AMP, 200V

1N754A       1N9557B                       70400754    6.8V, 5% ZENER

1N757A       1N5239                        70400757    9.1V, 5% ZENER

1N968B                       5% ZENER      70400968       20V, .5W

1N969B                                     70400969    22V, 5% ZENER

1N978A      SZG-30720                      70430720      51V ZENER

D10LC40                                     70401040   FAST RECOVERY

1202                       PV LITE 2400   70401202        ZENER

15N40      KBP-2504                       70401540   25A, 400V BRIDGE

DB2504P                      BRIDGE RECT.   70402504   400V, 25A W/LEAD

2508                       BRIDGE RECT.   70402508     800V, 25 AMP

SR-2873      MR-2502       TUBE FLYBACK    70402873     2K PIV 250MA

1N4003                                     70464003     1A, 200V, SIL.

1N4004                                     70464004     1A, 400V, SIL.

1N4007                                     70464007    1A, 1000V, SIL.

Page 10

ORIGINAL     ALTERNATE           FIELD

IN-HOUSE      IN-HOUSE        REPLACEMENT        ORDER

NUMBER        NUMBER           NUMBER           NUMBER         NOTES

***1N270                          1N270         70410270      200 MA, 80V

**SZ-13886      SZ-13551          MZ-2361        70413886      DUAL DIODE

1N5239C                          2% ZENER        70415239       9.1V, .4W

1N4148          (LL34)                          70418026      SMT (1134)

1N751          (LL34)                          70418027      SMT (LL34)

RL-25227B                                        70418028    3.6V ZENER SMT

MBR-350                                         70420350   MRB-350 SCHOTTKY

1N758A                          5% ZENER        70420758      10V, 400MW

RUR-820                                         70420820    FAST RECOVERY

FAST REC.                                        70420830      300V, 8 AMP

1N4150                                          70424150     SIGNAL DIODE

SPZ-30050       1N4745                           70430050    16V, 1W ZENER

SZ-30720                        10% ZENER        70430720     51V, .5W T&R

SZG-40102       1N4744                           70440102   15V, 1W 5% ZENER

1N4003                                          70464003    200V, 1A DIODE

1N4004                                          70464003    400V, 1A DIODE

1N4007                                          70464007     1000V, 1A SIL.

1N4148        1N914, 1N4                        70464148     75V, 10MA SIL.

1N4742                                          70464742   12V, 1W, 5% ZENER

1N5393                                          70465393      200V, 1.5A

1N4749        SPZ-20100                         70466164    24.5V, 1W ZENER

MR-812       4933, 1N4935                       70404933    FAST RECOVERY

BA-5CS*        1N4003            1N4003         70464003       1A, 400V

MA5CS*      MR-752, P-600D                      70400752       6A, 200V

1N4744                           1N4744         70440102    15V, 1W ZENER

SZP-20100       1N4749                           70466164    24.5V, 1W ZENER

15AF40        KBP-2504       BRIDGE RECTIFIER   70401540       25A, 400V

FE-186                                          70400161     HALF BRIDGE

P-300D      1N5402, 1N5403                      70400502       3A, 200V

Page 11

*     Original in-house part number; no longer available.

**    SZ-13886 is a special selection from MZ-2361 for voltage drop characteristics. Commercially available parts may not

perform to these specs.

***   To be used only in the Studio Chorus 70, not the same part as 70400034 branded #US-270.

Page 12

ANALOG IC'S

Warnings: All integrated circuits are static sensitve. PLEASE HANDLE WITH CAUTION, USE GROUNDED STATIC-

FREE WORKSTATION.

ORIGINAL           ALTERNATE                FIELD

IN-HOUSE            IN-HOUSE             REPLACEMENT             ORDER

NUMBER              NUMBER                NUMBER                NUMBER                 NOTES

TK-11745                                      TO-92             70411745           4.5V REGULATOR

TLO-72          4558, 3678, 5532,                              70400072            BI-FET DUAL JG

4560

TLO-74          TLO-84, XR-4741,                               70400074           QUAD BI-FET PKG

MC-33179

BA-682                                                         70400682             L.E.D. DRIVER

UA-741         REPLACES TL-071,                                70400741           SINGLE BI-POLAR

LF-355, SC-5278

LB-1412                                                         70401412             L.E.D. DRIVER

RS-232                                      DPM-C8             70401488            LINE DRIVER IC

RS-232                                      DPM-C8             70401489            LINE RECEIVER

SCM-2017P                                                        70402017           AUDIO PREAMP IC

TLE-2062CP                                                        70402062              DUAL J-FET

TLE-2064CN                                                         7042064              QUAD J-FET

1281                                        12X8X1            70402093           CROSSPOINT SW

MC-142100                                      4X4X1             70402100           CROSSPOINT SW

RA-3678             4560, 5532              LOW NOISE           70403678            DUAL BI-POLAR

LA-4170                                                         70404170           HEADPHONE AMP

RC-4558              BA-4560             (NOT IN REVERB)        70404558            DUAL BI-POLAR

BA-4560              RC-4558             (NOT IN REVERB)        70414560            DUAL BI-POLAR

L-4962                                  5V TO 40V, 1.5A        70404962             REGULATOR

NE-5532**            4560, 3678         LOW NOISE OP-AMP         70405532            DUAL BI-POLAR

NE-5534FE            LOW NOISE            CS DRIVE BOARD         70405534           SINGLE BI-POLAR

ICL-7660S                                                        70407662           VOLTAGE INVERT

MC-33179             TLO-74/84                                   70433179            BI-POLAR QUAD

MC-34071AP                                                        70434071           SINGLE BI-POLAR

MC-34181                                                         70434181             SINGLE J-FET

Page 13

ORIGINAL        ALTERNATE               FIELD

IN-HOUSE         IN-HOUSE            REPLACEMENT         ORDER

NUMBER           NUMBER               NUMBER            NUMBER             NOTES

UAA-180                              MC & MR MIXER      70467180        L.E.D. DRIVER

SN-75150                                                70475150      QUAD LINE DRIVE

87478            CA-3094                               70487478        SINGLE O.T.A.

87C751                                                 70487751      MICRO-CONTROL

TL-604          SN-99661           SPECIAL HANDLING    70400604            CMOS

MC-3302                               COMPARATOR        70403302          BI-POLAR

LM-325                              MC & MR MIXERS     70400325        REGULATOR IC

LM-3915                                 BI-POLAR        70403915        L.E.D. DRIVER

SC-5278*     LF-355, UA-741, TLO-                       70405534      CS DRIVE BOARD

71

LF-355*       UA-741, TLO-71                           70405534      CS DRIVE BOARD

TLO-71*      UA-741, LF-355N,

SC-5278

TLO-84            TLO-74                               70400074

XR-4741       TL-O74, TL-O84,                           70404741         XR-4741 EQ

MC-33179

SN-99661           TL-604           SPECIAL HANDLING    70400604        CMOS DEVICE

CA-3094            87478                                70487478        SINGLE O.T.A.

MF-6           MF-6CN-50              (6 POLE)        70400650      BUTTERWORTH FIL

MC-1436P1         MC-1436P1           STUDIO CHORUS      70401436       HI VOLT OP AMP

TDA-2005M         20 WATTS              MC-1436P1        70401436         BRIDGE AMP

TDA-2040                                TDA-2040        70402040         POWER AMP

CD-4511                                 CD-4511         70404511        7 SEG. DRIVER

SLK-2452-02                             SLK-2452-02      70402452       COUNTER/TIMER

3005                                MN-3005, 4096     70403005       STAGED BBD IC

3007                              MN-3007/1024-ST     70403007        LO-NOISE BBD

3101                                  MN-3101         70403101      BBD CLOCK GEN.

CA-32080E        DUAL O.T.A.             CA-3280G        70403280         DUAL INLINE

3302N          DUAL INLINE         LM-3302N, MC-3302   70403302       COMPARATOR IC

PWM-25                                 IP-3525A        70400025   IF IP-3525A IS USED, CALL

FOR MODIFICATION

Page 14

ORIGINAL              ALTERNATE                    FIELD

IN-HOUSE               IN-HOUSE                 REPLACEMENT              ORDER

NUMBER                 NUMBER                    NUMBER                 NUMBER                  NOTES

BA-6144                                                 BA-6144         70406144            5 SEG. LED DRIVE

BA-6209                                                 BA-6209         70406209             MOTOR DRIVER

STK-6327A            16-PIN SIP PACK                STK-6327A            70406327              EQ PACKAGE

8038CP                                                  XR-8038         70408038            PREC. WAVEFORM

GENERATOR

665                                              TEA-0665             7040665             DOLBY B/C NR IC

LM-323                                         LM-323/LT-323AK         70420323            +5V 3A TO-3 REG.

*     Original in-house part obsolete; no longer available.

**    When used as input chip in UT series amps, can cause scratch or DC on pregain control.

NOTE: Numbers with NO SUBSTITUTES must be replaced with the original number.

ORIGINAL              ALTERNATE                    FIELD

IN-HOUSE               IN-HOUSE                 REPLACEMENT              ORDER

NUMBER                 NUMBER                    NUMBER                 NUMBER                  NOTES

DIGITAL I.C.

LIST

ADC-0804                                                 (8 BIT)        70400804             A/D CONVERTER

AD-565AJN                                                (12 BIT)        70420565             D/A CONVERTER

AD-7524                                                                 70407524               CMOS DAC

AD-7528                                                                 70407528             DUAL CMOS DAC

AD-7545KN                                                (12 BIT)        70427545             D/A CONVERTOR

AD7580                                          10 BIT SAMPLER          70407580             A/D CONVERTOR

AM-25L04PC                                                               70422504               12 BIT SAR

AM-6012DC                                                                70426012                12 BIT P/A

BA-6209                                                                 70406209               BA-6209 I.C.

CA-3086                                                                 70423086               TRN ARRAY

CA-3280E                                                                70403280               CA-3280 I.C.

CD-74HC04                                                                70410004            HEX INVT. BUFFER

CD-74HC27                                                                70430027               3 INPUT NOR

CD-74HCT11                                                               70430011         CMOS TRIPLE INPUT AND ?

Page 15

ORIGINAL      ALTERNATE          FIELD

IN-HOUSE       IN-HOUSE       REPLACEMENT       ORDER

NUMBER         NUMBER          NUMBER          NUMBER         NOTES

CD-74HCT257   CD-74HCT257E                      70400257          I.C.

74HCT4066     CD-74HCT4066E                     70424066   QUAD BI-LATERAL

CD-22402E                                       70422402    SYNC TIMER GEN.

CD-4001DE                                       70404001    CMOS QUAD NOR

CD-4013BE                       (FLIP-FLOP)     70404013     CMOS DUAL D

CD-4016                                       70404016    ANALOG SWITCH

CD-4021                                       70404021    CMOS PARALLEL

CD-4051                      MULTIPLEXER      70404051       ANALOG

CD-4053B                                       70404053    TRIPLE 2:1 MUX.

CD-4066                         SWITCH        70404066   QUAD BI-LATERAL

CD-4071                     BUFFER OR GATE    70404071     QUAD 2 INPUT

CD-4081                                       70404081   BINARY ENCODER

CD-4532                                       70404532   PRIORITY ENCODE

CD-40106BE                                      70440106   SCHMITT TRIGGER

CDM-6264E3                    STATIC CMOS RAM   70480008         8K X8

DG-211                                        70420211        CJ I.C.

DM-2502                                        70422502      8 BIT SAREG

DS-0026                                       70420026   CMOS C/K DRIVER

HDPL-2601                                       70422601    OPTOCOUPLER

HCPL-2611                                       70422611   H.P. OPTOCOUPLER

HD-6409                                       70406409   ENCDR/DECODER

KM-41256                         256K X 1      70480256    DYM RAM MICRON

L-296                                        70400296    SWITCHNG REG.

LF-398N                                       70420398   SAMPLE/HOLD AMP

LF-398N                                       70420398   SAMPLE/HOLD AMP

LH-324                                        70415019        OP AMP

LM-308                                        70420308        OP AMP

LM-311                                        70420311    V COMPARITOR

LM-317                                        70400317    ADJ REGULATOR

Page 16

ORIGINAL       ALTERNATE          FIELD

IN-HOUSE        IN-HOUSE       REPLACEMENT     ORDER

NUMBER          NUMBER          NUMBER        NUMBER           NOTES

LM-325N                                       70400325   TRACKING REGULATOR

LM-399                                       70400399     QUAD DIFF. COMP.

LM-555CN                                       70420555          TIMER

LM-3080N                                       70403080          O.T.A.

LM-3080N     CUSTOM SELECTED                   70413080          O.T.A.

LM-3086                                       70423086        TRN ARRAY

LM-3189                                       70403189       IF AMP/DET.

LM-835                                       70400835     DIGITAL CONT. EQ

MB-504                                        70400504       PRESCALER

MC-1408P6                          (8 BIT)     70420806     D/A CONVERTOR

MC-14011                                       70414011         CD-4011

MC-14081B                                      70414081     REVERB GATE ARR

MC-145157                                      70405157       FREQ. SYNTH

MCM-4116                          16K X 1      70424116       BP DYN RAM

6665AP20      MCM-6665AP20        64K BIT      70426664       DYNAMIC RAM

MF-650                          6 POLE       70400650     BANDWITH FILTER

MPQ-918                         XTR ARRAY     70400918        QUAD AMP

NE-566N                                       70420566     V CONTROL OSC.

NE-571N                                       70420571     COMPANDER I.C.

NE-572         SA-572        PROG. ANALOG    70420572       COMPANDER

P-80C31BH                                      70400031    CMOS MICROPROSS

PCM-54                                        70420054        16 BIT V D/A

PCM-56                         SERIAL INPUT   70410056        16 BIT DAC

PCM-61                                        70401860        18 BIT DAC

QPC-4621                                       70424621   HI SLEW OPTOCOUPLER

S-3528                                       70403528       PROG. FILTER

SN74LS00N                       (NAND GATE)    70420000       QUAD 2 INPUT

SN-74LS04N                                     70420004      HEX INVERTER

SN-74LS10N                      (NAND GATE)    70420010      TRIPLE 8 INPUT

Page 17

ORIGINAL      ALTERNATE      FIELD

IN-HOUSE       IN-HOUSE   REPLACEMENT      ORDER

NUMBER         NUMBER      NUMBER         NUMBER         NOTES

SN-74LS11N                 (NAND GATE)     70420011    TRIPLE 8 INPUT

SN-74LS14N                                 70420014   SCHMITT TRIGGER

SN-74LS42N                                 70420042   1 OF 10 DECODER

SN-74LS74AN                                70420074   DUAL D FLIPFLOP

SN-74LS153N                                70420153    DUAL 4 IN MUX

SN-74LS157N                                70420157    QUAD 2 IN MUX

SN-74LS161N                                70420161     4 BIT BIN CTR.

SN-74LS174N                                70420174   HEX-D FLIP-FLOP

SN-74LS193N                                70420193   UP/DOWN BINARY

SN-74LS283N                                70420283   4 BIT FULL ADDR.

SN-74LS374N                                70420374          I.C.

SN-74LS393N                                70420393      COUNTER

SN-74LS624N                                70420624          I.C.

STK-6237                    70406237      70406237     GRAPHIC EQ

TC-9135                                  70409135    HEX PANEL SW

TC-9144                                  70409144      LOGIC CHIP

TDA-7000                                  70407000     FM TUNER I.C.

TDA-8444                     (DAC)        70408444    OCTUPLE 6 BIT

TLC-274B                                  70400274       OP AMP

TLC-549                     (8 BIT)      70400549   A/D CONVERTER

TLJC-5411                                 70400541   A/D PERIPHERAL

UC-3637                                  70423637   PWM CONTROLLER

UC-3825                                  70403825       PWM I.C.

UM-8250A                                  70408250         UART

UPB-569C                                  70400569     PRESCALER

1 MEG SIMM                                 70400248    1 MEG X 8 SIMM

6N138                                   70400138    OPTOCOUPLER

68HC705C8                                  70407058   8 BIG MICRO CON.

74AC157                  QUAD EXCLUSIVE   70410157       OR GATE

Page 18

ORIGINAL   ALTERNATE      FIELD

IN-HOUSE    IN-HOUSE   REPLACEMENT      ORDER

NUMBER      NUMBER      NUMBER         NUMBER         NOTES

74AC175                  (HI SPEED)     70420175     D FLIP-FLOP

74H238                                 70410238   3 TO 8 DECODER

74HC02                 QUAD 2 INPUT    70410002      NOR GATE

74HC04                                 70430004   CMOS HEX INVERT

74HC08                                 70430008   QUAD AND GATE

74HC10                                 70430010        CMOS

74HC14N                   (SCHMITT)     70420014   TRIGGER INVERT

74HC32P                                 70410032

74HC85                    (4 BIT)      70410085   MAGNITUDE COM.

74HC86                QUAD EXCLUSIVE   70410086       OR GATE

74HC123                  (ONE SHOT)     70430123    DUAL TRIGGER

74HC132                 QUAD 2 INPUT    70400132      NAND GATE

74HC221                                 70430221   DUAL NON RETRIG

74HC148                                 70400148   LIINE PRTY ENCOD

74HC164                    (8 BIT)      70400164   SHIFT REGISTER

74HC175                                 70410175    4 BIT REGISTER

74HC257                                 70400257   QUAD MULTIPLEX

74HC393                                 70400393    HI SPEED CMOS

74HC404                 HI-SPEED HEX    70400104   CMOS INVERTER

74HC573                                 70410573    OCTAL LATCH

74HC574                                 70410574   OCTAL REGISTER

74HC590                                 70410590   BINARY COUNTER

74HC4020                                70404020   BINARY COUNTER

74HC4040                                70414040   BINARY COUNTER

74HCT00N                                70410000   CMOS NAND GATE

74HCT04                    CMOS         70430004    HEX INVERTER

74HCT11                                 70430011        CMOS

74HCT42                                 70430042        CMOS

74HCT74                    CMOS         70430074   DUAL FLIP-FLOP

Page 19

ORIGINAL   ALTERNATE      FIELD

IN-HOUSE    IN-HOUSE   REPLACEMENT      ORDER

NUMBER      NUMBER      NUMBER         NUMBER         NOTES

74HC5138                                70420138    3 TO 8 DECODER

74HC5153                                70430153   DUAL 4 INPUT MUX

74HCT157                                70430157    CMOS DUAL MUX

74HCT161                   (CMOS)       70430161    BINARY COUNTER

74HCT174                 CMOS HEX       70430174      D FLIP-FLOP

74HCT193                                70430193    CMOS UP/DOWN

74HCT245                                70400245

74HCT283                                70400283   CMOS FULL ADDER

74HCT373                                70400373    OCTAL BUFFER

74HCT374                                70400374    TRI. STATE OSC.

74HCT541                                70410541    OCTAL BUFFER

74HCU04                                 70400104    HI-SPEED CMOS

74LS08                                 70420108    INPUT AND GATE

80C31                                  70414501   MICROPROCESSOR

87C751                                 70487751   MICROCONTROLLER

604                                   70400604    SN99661P-CMOS

2105                 DIGITAL SIGNAL   70402105     PROCESSOR

3765                  FLOPPY DISK     70403765       CONTROL

4028B                  BCD TO DEC      70404028      DECODER

4328                     (18 BIT)     70404328   STEREO D/A CONV.

4464                     64K X 4      70424464     100NS D-RAM

4465                  64K X 4 D-RAM   70424465        120NS

4515                    (LATCH)       70404515    ADDRESSABLE

5380                                  70405380   SCSI CONTROLLER

6116                    2K X 8 BIT    70406116      STATIC RAM

7406                                  70407406     HEX INVERTER

8155                                  70408155     I/O EXPANDER

8751                     (8 MHZ)      70408751   MICROCONTROLLER

8038CP                                 70408038    WAVEFORM GEN.

Page 20

ORIGINAL               ALTERNATE                    FIELD

IN-HOUSE                IN-HOUSE                 REPLACEMENT                  ORDER

NUMBER                  NUMBER                    NUMBER                     NUMBER                     NOTES

53528                                          PROGRAMMABLE                70403528                    FILTER

Warning: All integrated circuits are static sensitive. Please handle all with caution; use grounded static-free work station.

Page 21

ORIGINAL               ALTERNATE                    FIELD

IN-HOUSE                IN-HOUSE                 REPLACEMENT                ORDER

NUMBER                  NUMBER                    NUMBER                   NUMBER                    NOTES

FET IN-HOUSE

CROSS

REFERENCE

J-111                   J-112                     35 VOLT               70400111          SPECIAL APPLICATION

J-174                 2N5461**                   SPS-576**              70400174                  30V P-CH.

J-177                                                                   70400177                  30V P-CH.

J-231            J-202, SKA-3586**               2N5462**               70400231                  40V N-CH.

SPS-3008**

SPS-576*            2N5461, 2N5462                 SPS-3008               70400576                 40 V P-CH.

2N5459*                                                                   70405951                  25V N-CH.

2N5951            SKA-3586, J231**                                       70405951                  30V N-CH.

SPF-558*                2N5951**                                          70405951                  25V N-CH.

MPF-161*                2N5461/2                     J-175**              70400576                  30V P-CH.

2N5458*                 2N5951**                                          70405951                  25V N-CH.

E-203*                 2N5951**                  SKA-3586**              70405951                  40V N-CH.

J-175*                SPS-576**                   2N5462**               70400576                  30V P-CH.

J-270*                SPS-576**                   2N5462**               70400576                  30V P-CH.

2222+                                             (MOSFET)               70402222            60V ENHANCEMENT

SK-3586*            2N5951, J-231**                                       70405951                  40V N-CH.

SPS-3008*          MPF-161, 2N5461/2            J-175**, SPS-576           70400576                 40 V N-CH.

2N5461/2*            SPS-576, J-175**                                      70400576                  40V P-CH.

** = Warning: Basing different; check basing diagram below.

* = Original in-house part number now obsolete; no longer available.

Note: Use only 40V FET's in all transient suppressor circuits. Also, note voltage rating when cross referencing FET's.

Page 22

FET BASING DIAGRAM

From              Bottom

S D G

-----------------------

– o                 o –     2N5461, 2N5462, MPF-161, SPS-3008, SPS-576

–          o          –

–                 –

–       –

D G S

-----------------------

– o                 o –     J-177, J-174, J-270, J-175

–          o          –

–                 –

–       –

D S G

-----------------------

– o                 o –     2N5459, 2N5458, J-231, J-111, J-112

–          o          –

–                 –

–       –

G D S

-----------------------

– o                 o –     SKA-3586, 2N5951

–          o          –

–                 –

–       –

S G D

-----------------------

– o                 o –     2222

–          o          –

–                 –

–       –

Page 23

CAPACITORS

Nearly all recent model Peavey circuits utilize glass/tubular capacitors which are often mistaken for diodes.

They are distinguishable by their clear body and the capacitance value is printed on the side. The values

are expressed as shown below.

1 uf 10%..........................................105

.001 uf 10% 50V..............................102

.0015 uf 10% 50V............................152

.0022 uf 10% 50V............................222

.0033 uf 10% 50V............................332

.0068 uf 10% 50V............................682

.015 uf 10% 50V..............................153

.022 uf 10% 50V..............................223

.033 uf 10% 50V..............................333

.047 uf +80 -20 50V.........................473Z

.047 uf 10% 50V..............................473K

.068 uf 10% 50V..............................683

.1 uf +80 -20 50V.............................104K

.1 uf 10% 50V..................................104K

Capacitors with values in picofarads are light green in color and are marked in the same manner as resistors,

with color bands. These are often mistaken for resistors.

Capacitors with light blue or pink bodies and color coded bands have values in microfarads and are read as

follows:

1st band - brown = 1             2nd band - green = 5                   3rd band - orange = 3

153 = .015 (see chart above)

f:\wp51\service\crossref.lst (01/04/94 - lfw)

Page 24

Peavey Electronics Corporation / 326 Highway 11/80 / Meridian, MS 39301 / U.S.A. / (601)483-

5365, Fax: 486-1361