TPS2.1E-LA Tuner

5.4.3 Tuner

Attention: In case the tuner is replaced, always check the tuner options.

7.5 Tuner (TAFT-S710D)

The tuner has the following specifications:

• 2 in1 tuner for Analog.

• Covers all bands in VHF and UHF including hyper

channels for CCIR system.

• I2C- bus control of tuning, address selection, Broadcasting

system.

• Built-in DC/DC Converter (5v to 33V) & PAL(B/G, I, D/K) /

SECAM L/L’ Demodulator/NTSC(B/G)

Repair tip: After replacement of the tuner, the option code

should be checked, even when the set appears to function

correctly! Refer also to chapter 5 “Service Modes, Error Codes,

and Fault Finding”.