GRUNDIG CUC2130

Vertical problems

1. Vertical geometrical image distortion in upper image half.

Defective image tilt - deflection - R50048 (10R) and Z-diode 5400.  Align Z-diode with 2 Z-diode ZDY (3,9).

2. Upper half picture distorted.

Replace screen IC50020 (STV9306), R50048 (10R security resistor) and

check value C52004 (22nF).

3. Reduced vertical deflection (when cold). Pincushion distortion.

Check service menu and if E/W corrections are missing then SDA and SCL, error in data bus. Replace Q34043.

4. Picture compressed on top.

R50048 (10R) defective.

STV9306 pins DC voltages