PANASONIC

EURO4 szervizmód

- Set the Bass to maximum position, set the Treble to minimum position,  press the F button followed by the volume down (-V) button on the customer controls at the front of the TV and at the same time press the "INDEX" button on the remote control,  this will place the TV into the Service Mode.

- Press the RED / GREEN buttons to step up / downthrough the functions.

- Press the YELLOW / BLUE buttons to alter the function values.

- Press the STR button after each adjustment has been made to store the required values.

- To exit the Service Mode, press the "N" button.

NOTE: This TV also has the option of using a Memory Pack which enables you to copy the preset TV channels into the

Memory Pack and then download them onto this or any other EURO-4 TV set.