| IC packages:Classification of Through-Hole Packages |
| --- |
| Style(EIAJ) | Package | Characteristics | Material |
| Dual In-Line | DIP | DIP | Leads are on two opposite sides of the package. | Plastic |
|  |  | SDIP | DIP with a shrunk lead pitch | Plastic |
|  |  | HDIP | DIP with a heat sink | Plastic |
|  |  | WDIP | DIP with a permeable window or DIP encapsulated with permeable resin | Plastic/ Ceramic |
| Single In-Line | SIP | SIP | Leads are on one side of the package in a straight line. | Plastic |
|  |  | SSIP | SIP with a shrunk lead pitch | Plastic |
|  |  | HSIP | SIP with a heat sink | Plastic |
|  | ZIP | ZIP | Leads protrude from two opposite sides of the package in a staggered configuration. | Plastic |
|  |  | SZIP | ZIP with a shrunk lead pitch | Plastic |
|  |  | HZIP | ZIP with a heat sink | Plastic |
| Area Array | PGA | PGA | Leads are on the top or bottom of the package in area array format. | Plastic/ Ceramic |
|  |  | HPGA | A heat sink is attached internally, and leads are on the top or bottom of the package in either peripheral or area array format. | Plastic/ Ceramic/ Glass Shield |

Top of this page

## Surface-Mount Packages

| IC packages:Classification of Surface-Mount Packages |
| --- |
| Style(EIAJ) | Package | Characteristics | Material |
| Peripheral Leads | QFP | QFP | Leads are on four sides of the package in a gull wing configuration. | Plastic/ Ceramic/ Glass Shield |
|  |  | HQFP | Thermally-enhanced QFP with either a radiation fin on its leads or an internal heat spreader under the die | Plastic |
|  |  | LQFP | QFP with a seated height of 1.7 mm | Plastic |
|  |  | TQFP | QFP with a seated height of 1.2 mm or less | Plastic |
|  | QFJ | QFJ | Leads are on four sides of the package and are bent downward in the shape of letter J. | Plastic |
|  | QFN | QFN | Leads are on four sides and the bottom of the package. | Plastic |
|  | QON | QON | - | Plastic |
| Two-Sided Leads | SOP | SOP | Leads are on two opposite sides of the package in a gull wing configuration. | Plastic |
|  |  | SSOP | SOP with a lead pitch of 1.0 mm or less | Plastic |
|  |  | HSOP | Thermally-enhanced SOP with either a radiation fin on its leads or an internal heat spreader under the die | Plastic |
|  |  | TSOP I | SOP with a seated height of 1.2 mm or less, a lead pitch of 0.8 mm or less. Leads are on the short sides in a gull wing configuration. | Plastic |
|  |  | TSOP II | SOP with a seated height of 1.2 mm or less, a lead pitch of 1.27 mm or less. Leads are on the long sides in a gull wing configuration. | Plastic |
|  |  | TSSOP | SSOP with a seated height of 1.2 mm or less | Plastic |
|  |  | VSSOP | SSOP with a seated height of 1.0 mm or less | Plastic |
|  |  | ESOP | - | Plastic |
|  |  | WSOP | SOP with a permeable window or DIP encapsulated with permeable resin | Plastic |
|  | SHP | SHP | SVP designed for horizontal mounting | Plastic |
|  | SOL [JEDEC]standard | SOL [JEDEC]standard | Leads are on two opposite sides of the package in a gull wing configuration. | Plastic |
|  | SOJ | SOJ | Leads are on two opposite sides of the package and are bent downward in the shape of letter J. | Plastic |
|  | SON | SON | Leads are on two opposite sides and the bottom of the package. | Plastic |
|  |  | CSON | - | Ceramic |
| Single Row of Vertical Leads | SVP | SVP | Leads are on one side of the package and are bent in the shape of letter L | Plastic |
| Area Array | BGA | BGA | An array of solder balls are over or underneath the package. | Plastic/ Ceramic |
|  |  | FBGA | 1.2mm<FBGA BGA with a minimum ball pitch of 0.8 mm or less and a maximum seated height of over 1.2 mm | Plastic |
|  |  | TFBGA | 1.0mm<TFBGA≤1.2mm BGA with a minimum ball pitch of 0.8 mm or less, a minimum seated height of over 1.0 mm and a maximum seated height of 1.2 mm or less | Plastic |
|  |  | VFBGA | 0.8mm<VFBGA≤1.0mm BGA with a minimum ball pitch of 0.8 mm or less, a minimum seated height of over 0.8 mm and a maximum seated height of 1.0 mm or less | Plastic |
|  |  | WFBGA | 0.65mm<WFBGA≤0.8mm BGA with a minimum ball pitch of 0.8 mm or less, a minimum seated height of over 0.65 mm and a maximum seated height of 0.8 mm or less | Plastic |
|  |  | UFBGA | 0.5mm<UFBGA≤0.65mm BGA with a minimum ball pitch of 0.8 mm or less, a minimum seated height of over 0.5 mm and a maximum seated height of 0.65 mm or less | Plastic |
|  |  | XFBGA | XFBGA≤0.50mm BGA with a minimum ball pitch of 0.8 mm or less and a maximum seated height of 0.5 mm or less | Plastic |
|  | LGA | LGA | Land grid array with a standoff height of 0.1 mm or less and a maximum seated height of over 1.2 mm | Plastic |
|  |  | TFLGA | 1.0mm<TFLGA≤1.2mm LGA with a minimum ball pitch of 0.8 mm or less, a minimum seated height of over 1.0 mm and a maximum seated height of 1.2 mm or less | Plastic |
|  |  | UFLGA | 0.5mm<UFLGA≤0.65mm LGA with a minimum ball pitch of 0.8 mm or less, a minimum seated height of over 0.5 mm and a maximum seated height of 0.65 mm or less | Plastic |
|  |  | XFLGA | XFLGA≤0.50mm LGA with a minimum ball pitch of 0.8 mm or less and a maximum seated height of 0.5 mm or less | Plastic |

- Products

  - Package & Packing Information

    - IC packages

- Applications

- Company Profile

- News and Event

- Support

- Environmental Activities

- Terms of Use

- Site Map

Top of this page