PHILIPS GR2.1 hibák2

- INT SHUTDOWN

CNR50 POWER CONTROL  IC

- Int shutdown & poor response to R/C & OSD corrupted

CNR50 POWER CONTROL  IC

- Narrow pic - e/w fault

Dry joints TR7533 E/W mod driver - tr7530 BC848 faulty

- "S" in screen, cannot go from service mode.

Diode 6705 (BZV55; 4822 130 80914) leaks.

- Bad search tuning GR2.1 mono versions on local cable nets.

Add on the monocarrier between junction R3714/R3735 and earth an electrolitic capacitor 1 uF/16V (4822 124 40242) mount the capacitor on the location of the reserved item number 2707. 
The problem has been observed on local cable nets special on the lower

- Bended horizontal lines at top and bottom of the picture

Mount correction module 4822 212 31384 (seagull), and do the alignments on this module.

- Black picture with unsynchronised teletext bars

Measure on pin 47 IC7800 (SAA5246); if period time is smaller then 1 micro second, replace crystal 1800 (4822 242 81191).

- Buzz on sound in mono sets

Only The buzz on sound on VCR playback can be reduced by replacing the sound quadrature coil 5035 on the sound IF module. (4822 157 63077).  Realign the new coil for optimum sound quality. Changing option codes. It has been discovered that changing the option code for nicam (from ON to OFF or vice versa) will not effect this change. If this problem occurs, the option code can be changed as follows:
Change option code for nicam as requested. Change option code fo

- Crackling noise in left loudspeaker. When after replacing R3207 (R3214 for nicam) by a special version code 4822 116 83726 you still hear the cracking noise it can be helpful to resolder the 6 components of the amplifier stage arround  7232 (7217 for nicam).

- Dark screen, LED blinks

If the LED obeys RC, uP is OK. Fault in power supply or TDA4680 (IC7309; 4822 209 63733). The problem occurs in sets produced in the beginning of the series. There is no problem if the software is MR5.

- Distorted picture during high contrast scenes (picture breathing) A production change has been applied to the east/west circuit to maintain the picture shape during scenes with high contrast transients, i.e. between sky and earth.

Position	Old		New
R3526		82K(100K)	47K

- Does not start from cold situation. Replace resistors R3610 (15B).

R3624 (330K) and R3625 (560K
R3624 330K 1W 5% TOL  4822 053 10334
R3625  560K 0.5W 5% TOL  4822 053 21564
R3610 (4822 050 25601) 10R (Safety) 4822 052 10109
Add resistor of 560R in parallel with C2660 4822 050 25601

- Does not take (new) channels into memory I2C bus were low in 15s intervals.

Replacing NICAM unit helps.

- Error nicam, no tuning on VHF channels.

Replace processor IC7708 software version MR4.0 by MR5.2 (4822 209 31209).

- Euro module connections Euro module connections.

Stereo models based on the GR2.1 chassis have two SCART sockets, one of which is coloured orange and is located on a pluggable sub-panel referred to as the Euro module.
If the Euro module`s three wiring connectors are unplugged f

- Green coloured stripes in picture.

Replace IC7307 (TDA4660; 4822 209 63108), on main panel

- Hotel mode

Hotel mode Receivers employing the GR2.1 chassis are equipped with a  "Hotel mode" facility.  In this mode certain functions are restricted.
To engage the hotel mode proceed as follows: 
First set the volume to the maximum level required when in hotel m

- How to enable/disable "Child Lock"

Press "MENU" button on Remote Control. When the menu appears on the screen, you select "SPECIAL FEATURES" (this expression is language dependent)
Within "SPECIAL FEATURES", the "CHILD LOCK" can be enabled or disabled.

- Hum in loudspeaker in stand-by. In some cases the spread of the resistors R3673 and R3674 causes a too high +16V in stand-by and this provoke a hum in the LS. To solve this problem the 2 resistors have to be changed:       R3673 into 4K64 1% 4822 051 54642,
R3674 into 1K05 1% 4822 051

- Hum on standby untill serial number QG079207 A production change has been introduced changing the value of R3673 from 4.7K to 4.64K, and R3674 from 1.1K to 1.05K.
In cases of specific complaint, this change can also be applied as a service solution.

- List of the microprocessors used in GR2.1 List of the microprocessors used in GR2.1 
DEV. CODE: FSL2-4.0 SUPPLY CODE: U209
DESCRIPTION: STEREO (Eng,Fin,Dan,Swe,Nor,Spa) CRYSTAL: 4.19
REPLACEMENT: 4822 900 10569  Change X-tal 1702 by a 6 Mhz version (4822 242 70392)

DEV. CODE: FSL1-4.0 SUPPLY CODE: U211
DESCRIPTION: STEREO (Eng,Ger,Fr,It,Du,Port) CRYSTAL: 4.19
REPLACEMENT: 4822 209 31209  Change X-tal 1702 by a 6 Mhz version (4822 242 70392

DEV. CODE: VSL2-4.1 SUPPLY CODE: U111 DESCRIPTION: MONO (Eng,Fin,Dan,Swe,Nor,Spa) CRYSTAL: 4.19 SERVICE CODE: 4822 209 63947

- Modification Modification East-west circuit has been changed to lower the voltage in transistor 7533 at the moment of switch off. The values of the following components have been changed in production: R3526 to 47k  (4822 051 10473).
C2526 to 10nF (4822 122 32442).

- Moire in picture.

Instead of changing the tuner UV916/UV917, add a electrolytic capacitor of 10 uF 25V between pin 12 and pin 16 of the tuner.
REMARKS :

1. The capacitor is introduced in production from week 9130 onwards.
2. When changing the electrolytic capacitor C2646  Philips GR2.1 MR4 to MR5 software change MR4 to MR5 software change.
After changing a microprocessor with MR4 software by a version with MR5 software  it is recommendable to check the option, white balans and peak white limit values. Some values may be overwritten.

- No sound when the set is warm, led blinks

Defective IC7309 (TDA4680; 4822 209 31592) blocks IIC bus.

- No sound, no functions and no picture.

On firstly checking the power supply this proved to be OK. On then checking the power on reset circuit, this was identified to be fault.

Replacing D6665 (4.7V Zener; 4822 130 80883) and T7663 (BC858; 4822 130 42513) restored operation.

- No start voltage on pin 7 and 8 of IC7600 Voltages should be 2,95V on pin 7 and 14,8V on pin 8 when starting up.Check or replace R3624 (330 kOhm) and R3625 (560 Ohm).

- Picture disappears, no sound

Flat cable to horizontal deflection coil is too close to RGB flat cable to picture tube base board. Philips GR2.1 Picture mutes every 6 sec., in sets with memory protection panels Remove C2721.

- Protection circuit working from time to time

Diode 6592 (LL2C30; 4822 130 80928) leaks. Voltage to protection circuit was ca. 400 mV, it should be 28...23 mV.

- Revised picture tube drive adjustments in service

Revised picture tube drive adjustments in service manual GR2.1. The electrical adjustments 1.13, 1.14 and 1.15 on page 7.1 of the GR2.1 chassis service manual 4822 727 18334 have been revised as follows: 
1.13  White balance
Put the TV into the  service Philips GR2.1 Service manual corrections Service manual corrections The parts lists of GR2 service manuals should be corrected as follows: 
Service manual for 21ST2731/05B 4822 727 19403
Add control panel code no. 4822 432 10957
Service manual for 25ST1750/25B 4822 727 19042

- Set can only be operated with Remote Control Check whether "Child Lock" is disabled. To check this, see "Frequently Asked Questions", "How to disable Child Lock". Philips GR2.1 Set does not start up from standby The following change has been introduced in production : 
Position		Old		New		Code no. 
R3663			4K7		5K6		4822 051 10562
R3674			1K1		1K		4822 050 11002

- Set is humming.

Hum is caused be a bended coil 5605 touching the SOPS heatsink.
Bend the coil to avoid touching of the heatsink.

- Sound mute on cable networks and with some VCRs.

Remove R3064 on stereo IF module, replace R3065 by 4K7 (4822 051 10472).
Add on R3070 8K2 (4822 051 10822).

- Sound rattle when white pattern and on some cable networks. Replace coil 5035 on the IF module by 4822 157 63077. Realign S5035 to have a good picture and sound.

- Spot on screen when switching off, possibly burnt in CRT

Replace C2450 by 100 uF (4822 124 80059) on the chassis.
Replace on CRT-panel C2433 by 680 pF (4822 126 12269).
Desolder R3432 on the CRT-panel and make a shortcircuit on this position.
Remove jumper between C2432 and T7345, solder R3432 between collec

- Survey of codenumbers CRT GR2.1, GR2.2 AA/AB.

For your info the code numbers of the CRT. This info can be used to complete your SI 92.02. (4822 727 19535).
A51 EAM 31X45 21" mini neck   4822 131 20324
A51 EAL 55X73  21" narrow neck  4822 131 20483

- The NICAM option remains on.

Symptom occurs after switching NICAM on and then off and leave by stand by. To avoid that the nicam option remains on you have to change an other option at the same time. E.g. change UHF only to off and again to on then the nicam remains off after saving.

- Thyristor TH6670 (SROR5043) warms too much

Change the value of R3663 to 5k6 (4822 051 10688).

- Totally dead.

Check and replace R3624 and R3625 in the power supply. Codenumbers: R3624 330 kOhm 4822 053 10334, R3625 560 kOhm 4822 053 21564.

- Whistling LOT. Discharge is audible. Loudness depends on picture. As a result line output transistor becomes defective.
Break earth pin A. This pin connects ferrite core to earth via spring. Cut as close to the plastic holder as possible. This pin is not in the Service Manual. 
REMARKS :
From week 9223 onwards transf Philips GR2.1 White stripes in picture in 25" and 28" sets Change value of R3501 from 75 Ohm into 100 Ohm (4822 051 10101).

- You cannot change all options in the service mode at the same time. If you save all changed options by selecting stand by it can happen in sets with MR5 software that some values are not stored. To avoid this, store each option group separately.

- DEAD WITH POWER SUPP. RUNNING

CHECK IC7880  PCA84C81AP/098  (  UNPLUG TEXT PCB TO PROVE  )

- EHT BUT NO SOUND OR PIC AND A FLASHING LED

WHEN TDA2579B PRODUCING WRONG S.CASTLE PULSES

- Dead

C2545 1500pf 2kv s/c connected to BU508AF LOPTr

- Raster present with green LED flashing HT was low when connected to LOP but ok on bulb. Audio o/p chip was s/c

- Thump from spkr then trips

Dis'd TDA2613 audio o/p chip brought back pic but replacement along with R3241 8R2 failed to cure; soft start cct faulty - T7247 BC848 s/c