PM435 3 1/2 DIGITAL PANEL METER

| Click for larger photo | Display | 3 1/2 digits LCD with a Max. Reading of 1999 |
| --- | --- | --- |
|  | Polarity | Automatic, positive implied, negative polarity indication |
|  | Over Range | (1) or (-1) is displayed |
|  | Measurement Rate | 2 times per sec. nominal |
|  | Low battery | Auto display |
|  | Backlight | YES |
|  | Operating Environment | 0°C to 50°C at <70% relative humidity |
|  | Accuracy | Stated accuracy at 23±5°C <75% relative humidity |
|  | Applications | Item No | Range and resolution |
|  | DC Voltmeter | PM435L | 0.1uV~500V |
|  | AC Voltmeter | PM435AL | 0.1uV~500V |
|  | DC Current Meter | PM435BL | 10pA~5A |
|  | AC Current Meter | PM435DL | 10pA~5A |
|  | Thermometer | PM435CL | 1°C~300°C |
|  | Frequency Meter | PM435FL | 1Hz ~ 200KHz |
|  | Resistance Meter | PM435RL | 0.1Ω~20MΩ |
|  | Other Industrial & DIY Users | Capacitance Meter* | *conversion circuit not included |
|  |  | dB Meter* |  |
|  |  | PH Meter* |  |
|  |  | Watt Meter* |  |
|  |  | Lux Meter* |  |
|  |  | LCR Meter* |  |
|  | Dimension | 78*42*18mm |
|  | Supply Voltage | 8 - 12 VDC |

| Click for larger photo | Display | 3 1/2 digits LCD with a Max. Reading of 1999 |
| --- | --- | --- |
|  | Size | 78×42×18mm |
|  | Install Size | 76.5×39.2 |
|  | Input Voltage | 36V-220V(The input voltage can also be power supply,extra power supply unneeded.) |

| Click for larger photo | Display | 3 1/2 digits LCD with a Max. Reading of 1999 |
| --- | --- | --- |
|  | Size | 78×42×18mm |
|  | Install Size | 76.5×39.2 |
|  | Input Voltage | 36V-220V(The input voltage can also be power supply,extra power supply unneeded.) |

| Click for larger photo | Display | 3 1/2 digits LCD with a Max. Reading of 1999 |
| --- | --- | --- |
|  | Size | 78×42×18mm |
|  | Install Size | 76.5×39.2 |
|  | Input Voltage | 36V-220V(The input voltage can also be power supply,extra power supply unneeded.) |