PHILIPS MG2.1, MG3.1 szervizmód

Philips MG3.1E CTV Service Mode:

Option 1:

In the TV-set itself is a 3-pin connector with which either SERVICE-DEFAULT or SERVICE-MODE can be activated. This connector is depicted 0356 (SERVICE-PINS) on page K7 (TXT&CONTROL).

Shorting pins 1-2 will activate SERVICE-MODE.

Shorting pins 2-3 will activate SERVICE-DEFAULT.

Option 2:

Activate these modes using the remote control. Obviously option 2 is the preferred method because the settings have to be changed using a remote control anyway....

To activate SERVICE-DEFAULT:

Press 0 6 2 5 9 6 and then the [menu] button. The message ‘Service Default’ appears and channel ‘SER T’ will be selected. This only sets some settings to a preset value (color/brightness/volume and such). This mode is primarily intended to be used when the non volatile memory has been replaced. It is then loaded with the default values.

To activate SERVICE-MODE:

Press 0 6 2 5 9 6 and then the [i+] button. After pressing 0 6 2 5 9 6 the message ‘Dealer’ should have appeared. Do not worry about the channel changing while you press the numbers.

Service technicians have the means service mode using a special remote control device.