|  | Date | Chassis | Problem | Repair Tip |
| --- | --- | --- | --- | --- |
| 1 | 15.04.2005 | P6 | SW upgrade for AD9887KS-100 | In the first stages of production, instead of IC AD9887AKSZ-100 (453262R) AD9887KS-100 (453262) was used on U2 position. If SW has to be updated then 01 versions needed (for ex. SP642_LG01_T13). -02 versions are for new IC. |
| 2 | 15.04.2005 | P6 | Switched mode PSU 8KHz Whistle | Replace the IC on position U454 with LM2596S-5.0 (parts code 453007). U454 is on the corner near DVI connector. |
| 3 | 15.04.2005 | P6 | TV does not start up from standby | Check the value of R574. If it is 4K7 then replace it to 10K. |
| 4 | 15.04.2005 | L6 | TV does not start up from standby | Check the value of R574. If it is 4K7 then replace it to 10K. |
| 5 | 15.04.2005 | 14.2 | D507 is being damaged. | Please check and replace L503. Also check if D507 touches to chassis holder or not. |
| 6 | 01.04.2005 | C7 | Black boxes on the picture (tetris effect) | Please measure pin 24 of IC101 with volmeter. If it is higher than 1.8V then check and replace IC601. |
| 7 | 22.03.2005 | C7 | White line on the top of screen or black screen | 1. Check "protection" item of service mode is set to "N/A". 2. Replace following R673 to 18K SMD and C624 to 100NF 50V SMD. |
| 8 | 21.03.2005 | L5 | Additional information of Service mode for service manual | AUTO AV 16:9 : Automatically 16:9 detection via pin 8 of scart (default is ON) BACKLIGHT POL : Polarization of Backlite of panel is activated or not. FACTORY MODE : If it is on then service mode was accessible by pressing the Info button on the remote control. BRI = 130 CON=158 COL=128 AGC=19 FACTORY RESET : After activation, following service mode items are changed into default values: hotel mode, stdby recall, msp carier mute, wss rf, auto av 16:9, first ats, backlight pol, white r, white g, white b, prescale fm, prescl nicam, prescl scart, hotel volume, agc, tuner type, teletext, timer mode, msp chip, swap/zapp TIMER MODE: off timer: in timer off mode. Sleep timer: in sleep timer mode SWAP/ZAPP: Swap active or Zapp active |
| 9 | 14.03.2005 | L4 | Sound generated from Power board of 30" | Replace the capacitors on positions C1 and C2 with 1uF/400V MKP type or 2 parallel 470nF/400V MKP type capacitors. Pin distance to be 15mm. |
| 10 | 21.02.2005 | 22.1 | L603 makes sound | Please check the soldering of pins of C663 |
| 11 | 08.02.2005 | L6 | Switched mode PSU 8KHz Whistle | Replace the IC on position U454 with LM2596S-5.0 (parts code 453007). U454 is on the corner near DVI connector. |
| 12 | 02.02.2005 | L6 | SW upgrade for AD9887KS-100 | In the first stages of production, instead of IC AD9887AKSZ-100 (453262R) AD9887KS-100 (453262) was used on U2 position. If SW has to be updated then 01 versions needed (for ex. SL6.26W-LG01). -02 versions are for new IC. |
| 13 | 24.01.2005 | 22.1 | Broad vertical strips (bars) in dark picture area | Fix the routing of the cable from X807 to X205 as seen picture in TCN01/2005. If it is on the other side (CPT) of Feature Box then the problem occurs. Please apply this after all Feature Box replacements. |
| 14 | 18.01.2005 | 22.1 | DDP3315C-G3 (IC803) version change | Software versions SBZ200-13 onwards support DDP G3 version. Please also check the resistor R856 connected DDPs pin 46 should be 1kR %1 (D2 versions have 10kR on this position). |
| 15 | 23.12.2004 | 10.3 | The screen is cutting in the top (need vertical adjustment). | Adjust P702 potentiometer in the main chassis (P701 is for horizontal) |
| 16 | 21.12.2004 | 12.8 | Snow effect problem at band Band I and II due to SMPS noise | Connect "minus" pin of 68 uF/500V capacitor on position C605 to the heat sink of STP3NB60FP on T601 with a wire of 3 cm |
| 17 | 17.12.2004 | PA | Hum noise from speakers | Please use line filter module for LG V6 panel (code:X56180). This part will be replaced with 4-pin cable which is located between connector CN802 (30V line) of the Power Supply Board and the AV-Tuner Board. |
| 18 | 16.12.2004 | 22.2 | C-type and U-type FBTs | For some CPT types of chassis 22.1 and 22.2 more than one FBT type are used. FBT (LOT) Type was added in column E of the attached “CPT Variance List 22.1 22.2.xls” file. Type 1 : C-type (Termal brand, 29 kV) Type 2 : U-type (Eldor brand) Type 3 : C-type (Termal brand, 32 kV) The FBTs differ electrically as well as their dimensions. There are two versions of circuit diagrams (please see the files attached). |
| 19 | 16.12.2004 | 22.1 | C-Type and U-Type FBTs | For some CPT types more than one FBT type are used. FBT (LOT) Type was added in column E of the “CPT Variance List 22.1 22.2.xls” file. Type 1 : C-type (Termal brand, 29 kV) Type 2 : U-type (Eldor brand) Type 3 : C-type (Termal brand, 32 kV) The FBTs differ electrically as well as their dimensions. There are two versions of circuit diagrams |
| 20 | 19.11.2004 | 14.1 | Replacing Termal Brand FBT with Eldor | Please apply TCN13/2002 |
| 21 | 01.11.2004 | 22.1 | The LED is switched off late when standby activated (sometimes 30 secs). | If 1W Standby module is used then this phenomenon is normal. The module issupplied by the DC capacitor on the main chassis. Since it takes time for discharging this voltage, there is a time lag in switching off of the LED on the cabinet when standby is activated. |
| 22 | 27.10.2004 | 16.1 | Picture is jumping up and down | Check and replace IC501, C510, C508 and C509 |
| 23 | 04.10.2004 | PA | V3 (Samsung) and V6 (LG) panel board spare parts codes | Please see TCN07/2004 |
| 24 | 24.09.2004 | 12.6 | IC NN5198K are defected due to the flash-over comes from CRT to IC NN5198K | Replace the damaged IC NN5198K and apply the below modifications: 1-) Adding 3 diods on the chassy : That means, 3 pcs. of diodes (1N4148 ) are connected between the pin of 9V power supply of the IC101 and the intersection point of the X101 socket and on positions R134,R135,R136 . The connecting must be done as the cathodes of diodes 1N4148 will be connected to the pin 9V of the IC101. 2-) Replace the old CRT board with the new CRT board : That means, the CRT board was modified again for preventing to damage of IC NN5198K due to flash-over comes from CPT . The location of two ground cables was changed on the new CRT PCB. The code of new CRT board is AD4165. |
| 25 | 24.09.2004 | 12.1 | Vertical line visible during start up for 2-3 secs | Check and replace R519, R520, R521, R527 and C512. |
| 26 | 31.08.2004 | 14.1 | Defected horizontal transistor BU508DF (T504) | Check and replace C129 - 2.2nF on pin 42 of IC101 |
| 27 | 04.08.2004 | 12.1 | tuning drift ( the TV stations go off tune ) | please check and replace following components: C961-C403-C460-C461-R453-R454-R455 |
| 28 | 04.08.2004 | 14.2 | Audio problem | When the unit warms up the sound disappears first, then it stops reacting to the remote control or the frontpanel buttons. Picture can still be seen. Then you turn power off (mains button) and after you turn it back again, no sound, no reaction to remote AND THE PICTURE DISAPPEARS too. Check and replace C304 which is connected to pin 24 (Reset input) of IC301. |
| 29 | 04.08.2004 | 14.2 | Colours disappearing | Please change the C412 connected pin 62 and 63 of IC 101 ( IC TDA9563H/N1) from 56 pF to 39 pF and C413 from 33 pF to 39. Note : If the colours are still not correct, please insert 47 pF on pos. C412 and 22 pF on pos. C413. |
| 30 | 04.08.2004 | 10.3 | child lock deactivation | 1. Switch off the set by on/off switch 2. Press and hold "Volume- and Volume +" buttons on the front panel of the set 3. Switch on the set by on/off switch 4. TV displays "Service Mode" 5. Switch off the set by on/off switch If this method does not help, repeat the procedure but apply following at stage 2: press "Program- and Program +" buttons on the front panel of the set . |
| 31 | 04.08.2004 | 14.2 | Picture is enlarging and then getting normal. Power supply voltages are normal. | Please check bad solder on pins of C519. |
| 32 | 04.08.2004 | 12.3 | Picture pumping | Separate the 4 pin cable (which goes from Stereo module to main chassis) from Video IC and RGB cable (which goes to CRT module). |
| 33 | 04.08.2004 | 11.1 | The drive transistor T102 (Darlington type) has exploded and resistor R101 (safety 4,7ohm) have been burned | Please replace R101 resistor with 4R7 1W. |
| 34 | 04.08.2004 | 12.6 | Snow effect problem at band Band I and II due to SMPS noise | Connect "minus" pin of 68 uF/500V capacitor on position C605 to the heat sink of STP3NB60FP on T601 with a wire of 3 cm |
| 35 | 04.08.2004 | 12.1 | IC 151: if you take off pins 42 and 22 the voltage 9VA stays OK. But if you connect either or both pins 22 and 42 the voltage drops down to 1,5V | the "On-off" signal is given to pin 1 of IC951 (LM317T) from pin 37 of IC401 (uP). It is "high" during normal operation and "low" during standby. we advise you to disconnect pin 37 of uP and observe whether the +9.5VA is normal or not. if it is normal then there is problem with uP or its peripheral components. - The crystal may be defected connected Pin 31 and 32 - Reset circuitry connected to pin 33 (R412, T403, etc) may be defected - uP itself can be defected |
| 36 | 29.07.2004 | 22.2 | The clock display (osd) goes wrong in stby (20 min in 24 hrs) | Check and replace the SW IC with version 07 or higher (parts code S-SBD128). |
| 37 | 26.07.2004 | 22.1 | The tuning voltage of the tuner (33V) is missing. | Resoldering of resistor R 532 - bad soldering point. |
| 38 | 16.07.2004 | 22.1 | Subwoofer doesnt work, No sound comes out of the Subwoofer. | Please check R637, and be sure that it isnt dislocated, or broken |
| 39 | 09.07.2004 | 12.7 | No channel | Check ZD 601 33V |
| 40 | 09.07.2004 | 12.7 | TV does not work | 1) Check fuse 2) Check IC601,R606,R608 3) Check R606-1 OHM T601-K2750 4) Check R615 01 OHM, D608 |
| 41 | 09.07.2004 | 12.3 | No picture | 2) IC601,R606,R608 kontrol edin |
| 42 | 09.07.2004 | 14.2 | Does not work by remote control | 3) R606-1 OHM T601-K2750 kontrol edin |
| 43 | 09.07.2004 | 14.1 | No picture | 4) R615 01 OHM, D608 RGB |
| 44 | 09.07.2004 | 22.1 | protection activated | kontrol edin |
| 45 | 09.07.2004 | 14.2 | P+ is put on the use | Check and replace IC101 |
| 46 | 09.07.2004 | 12.7 | Horizontal is shifting | Check C410 |
| 47 | 09.07.2004 | 22.1 | Broatcast losts sometimes | Check tuner |
| 48 | 09.07.2004 | 12.7 | Contrast and brightness is low | Check STV 2246 |
| 49 | 09.07.2004 | 14.2 | No picture | 1) Check and replace C143-100NF 2) Check and replace IC101 |
| 50 | 09.07.2004 | 12.5 | Could not catch a channel | Check and ZD 601 33V |
| 51 | 09.07.2004 | 22.1 | There is a rainbow on picture | Check and replace R530 |
| 52 | 09.07.2004 | 22.1 | TV does not work | Check and replace R643, R635 , DJ1 160 Featurebox , IC601, T601 |
| 53 | 09.07.2004 | 22.1 | Sound is going and returning frequently when using scart | Check IC301 if there is cald solder or not |
| 54 | 09.07.2004 | 14.2 | AV does not work | Check and replace IC101 |
| 55 | 09.07.2004 | 14.2 | Picture is comming 1 min later after running on standby | Check and replace IC401 |
| 56 | 09.07.2004 | 14.2 | Picture is shifting on sides | Check if R514 contacts heatsink or not |
| 57 | 09.07.2004 | 12.7 | Contrast and brightness is low | Check IC101 STV2249 |
| 58 | 09.07.2004 | 12.7 | Blue line on the screen | Check C624 1000UF 25V |
| 59 | 09.07.2004 | 12.7 | Sound exists but no picture | Check and replace C712 2.2NF2KV |
| 60 | 09.07.2004 | 12.7 | Picture is flickering | Check and replace C503 1000UF 35V |
| 61 | 09.07.2004 | 12.3 | After working a little time sound is turning off | Check and replace IC STV2246 |
| 62 | 09.07.2004 | 22.1 | Picture is getting narrow from right and left sides | Check and replace R516 |
| 63 | 09.07.2004 | 12.5 | Vertical defected | Check IC401 SDA 5535 |
| 64 | 09.07.2004 | 14.2 | No sound | Check and replace C178-4.7 nF |
| 65 | 09.07.2004 | 14.2 Mono | Channels can not be set | Check and replace IC401 |
| 66 | 09.07.2004 | 20.2 | Picture is narrow on left and right sides | Check and replace R210, R218, c215 ve L201 |
| 67 | 09.07.2004 | 12.7 | No picture | Check and replace IC401 and R615 |
| 68 | 09.07.2004 | 12.5 | TV can not get ON mode | Check IC401 |
| 69 | 09.07.2004 | 14.2 Mono | TV shuts off intermittently | Check and replace R529 |
| 70 | 09.07.2004 | 12.3 | No picture whenTV is operated by remote control at start up | Check and replace R112 |
| 71 | 09.07.2004 | 14.2 Mono | speaker sound distorted | Check and replace C166 ve R130 |
| 72 | 09.07.2004 | 14.1 | Picture is indistinct | Check and replace C705 |
| 73 | 09.07.2004 | 16.1 | Picture is green | Check and replace Degauss coil |
| 74 | 09.07.2004 | 14.2 | left speaker sound distorted | Check and replace C326 |
| 75 | 09.07.2004 | 12.3 | TV does not work | 1) Check S901 2) Check C605 3) Check IC901 TDA 16846 4) Check R959 5) Check S601 6) Check IC701 TDA6107Q 7) Check and replace T552 BU808 and replace C129 with 100NF capacitor (if LED is lighting) 8) Check and replace D553- IC 501 |
| 76 | 09.07.2004 | 14.2 Mono | TV can not get ON mode | Check and replace C403-C634 |
| 77 | 09.07.2004 | 12.7 | Shuts off automatically | Check and replace C605 68UF 400V |
| 78 | 09.07.2004 | 14.2 | Unfocused snowy picture | Check and replace R162-47OHM |
| 79 | 09.07.2004 | 22.1 | Led is lighting but TV does not work | 1) Check T501 2) Featurebox R436 470R may be open circuit |
| 80 | 09.07.2004 | 22.1 | Sometimes flyback lines | Featurebox D804 may be open circuit |
| 81 | 09.07.2004 | 12.7 | There are ping spots on picture | Check X703 CRT socket |
| 82 | 09.07.2004 | 14.2 | Picture is going and returning frequently | Check R529 1R if there is a cold solder or not |
| 83 | 09.07.2004 | 14.2 | Picture is getting bigger and smaller when turning up the sound | Check and replace R606, R607 0.47R |
| 84 | 09.07.2004 | 14.2 | TV does not work | 1) Replace ST 601 with 3.15 2) Check SW1 3) Check C150 MF 400V 4) Check IC 101 ; IC 401(24C08); IC 601 (MC44608); T601 K2545; R639 (15 OHM); R607 (0.47 OHM) ; ST601; PH601 |
| 85 | 09.07.2004 | 14.2 | After switching on at the first time there are lines on the upper part of picture | Check and replace IC501 TDA 8359 |
| 86 | 09.07.2004 | 14.2 | Picture is bad | Check and replace R162-47OHM |
| 87 | 09.07.2004 | 14.1 | TV does not work | 1) Check C555-T552 2) Check C905 150 mf 400 V 3) Check PH601,PC123,IC601,TH601, T601 4) Check S901-F60 5) Check R121 CHİP (If no OSD) 6) Check R639 DİRENÇ (If T601 is demaged) 7) Check C506 8) Check IC701, D511 9) Check TR502, T504 10) Check I601 |
| 88 | 09.07.2004 | 14.2 Mono | Sound is available but no picture | Check PCB near FBT, if it is crack or not |
| 89 | 09.07.2004 | 14.2 | TV works sporadic on standby | Check and replace TH601-MCR22 |
| 90 | 07.07.2004 | 14.2 Mono | TV does not work | Check and replace S601, T601, IC601, R606, R607 |
| 91 | 07.07.2004 | 14.2 | protection activated at standby mode | Check R529 if there is a cold solder or not |
| 92 | 07.07.2004 | 14.2 | Channels are changing by one selves | Check and replace IC101 |
| 93 | 07.07.2004 | 14.2 | There is a high-pitched noice | 1) Check and insulate Vertikal chock coil 2) Check nad varnish L502 coil 3) Check DST 4) Check L601 |
| 94 | 07.07.2004 | 14.2 | No teletex | Check from service menu whether teletex is open or not |
| 95 | 07.07.2004 | 14.2 | White lines on picture | Check and replace R709 on CRT |
| 96 | 07.07.2004 | 14.2 | Picture is indistinct and mat | Check and replace R162 |
| 97 | 07.07.2004 | 14.2 | Vertical lines on picture | Check the solder of DST |
| 98 | 07.07.2004 | 14.2 Mono | Channels are changing automatically | Check and replace IC101 |
| 99 | 07.07.2004 | 14.2 Mono | A cracking sound is comming on Standby | Check and replace TH601 410026 THRYSTOR MCR22-8 |
| 100 | 07.07.2004 | 14.2 Mono | Picture is getting dark | Check and replace R529 |
| 101 | 07.07.2004 | 12.4 | No syncronization | Check and replace IC101 |
| 102 | 05.07.2004 | 12.6 | “8500” code does not work for entering service mode | Try “9301” code (from SW version SB7120-08 onwards). |
| 103 | 01.07.2004 | 22.1 | The picture is dark | Please check the version of CRT PCB. If it is -09 or lower then replace the value of R708 to 10K from 6.8K. |
| 104 | 01.07.2004 | 22.1 | selecting source" is lost in the user menu in Secam LL system | This is normal. In LL system the line for PIP is used for AM mono sound. Consequently, there is no PIP sound can be supplied to headphones. |
| 105 | 01.07.2004 | 22.1 | white line effect on the borders of the objects | Replace the Feature Box with a one that has SW version 12 or newer. |
| 106 | 10.06.2004 | 22.1 | Geometry can not be adjusted properly for 16:9 screen | Change following components on the main chassis: C519 : 1uF 250V from 4.7uF C527 : 10nF from 68nF |
| 107 | 31.05.2004 | 22.1 | Horizontal lines on the screen | Decrease "FLYBACK DELAY" of GEOMETRY ADJUSTMENTS" by 10 units. |
| 108 | 18.05.2004 | 22.1 | Protection icon on the screen - three blinking pattern | Please check and replace R625 and R626 |
| 109 | 04.05.2004 | 14.1 | Entering service mode for Multimedia sets | In main menu press "7592" buttons. |
| 110 | 04.05.2004 | 22.1 | What do 120Hz geometry values do? | these 120 Hz values are for NTSC playback and 100 Hz for PAL/SECAM. You can see the difference when connecting a VCR or DVD that is playing NTSC movie or a simply pattern generators Scart cable in NTSC mode. |
| 111 | 30.04.2004 | PA | How can the SW be uploaded/upgraded? | Please see TCN06/2004. |
| 112 | 26.04.2004 | 14.2 | TV can not enter service mode by service remote control | With the following software versions onwards, to enter service menu, first activate the “Picture Menu” with the user remote control and press “9301” (Press “0” button to exit the Service Mode). Stereo versions : SB8973-A02, SB8975-A02 (For B,C and D versions will be apllied in time). Mono versions : SC3325-A05, SC3325-B07, SC3325-C06, SC3325-D05 |
| 113 | 26.04.2004 | 22.1 | TV can not enter service mode by service remote control | With the software versions SBZ200-15 onwards, the activation with service remote was cancelled. To enter service menu, first activate the “Picture Menu” with the user remote control and press “9301” (Press “TV/Text” button to exit the Service Mode). |
| 114 | 22.04.2004 | 12.6 | D607 and D608 type change | New ones are: D607 DIODE RGP15K 303400 D608 DIODE RGP30D 303228 |
| 115 | 22.04.2004 | 12.7 | D607 and D608 type change | New ones are: D607 DIODE RGP15K 303400 D608 DIODE RGP30D 303228 |
| 116 | 21.04.2004 | L2 | 20" chassis (MI2110 ) do not work | The reason is that SW is not suitable for the panel. For AU panel SW label on chassis should read SL4.200-A.. For Chimei panel SW label on chassis should read SL4.200-C.. |
| 117 | 15.04.2004 | 12.7 | How smart loader (G70520) works for Hotel mode | Please read 12.7 Hotel Mode + Smart Loader.doc*** Requirement: It should be produced as Hotel TV 1) Is Eeprom 24C16? 2) Is I2C connection to the Scart port available? Otherwise apply:- Connect a cable between Pin 10 of SCART and connection point of R470 and D407 (SDA) - Connect a cable between the pin 12 of SCART and connection point of R469 and D406 (SCL) |
| 118 | 02.04.2004 | 22.1 | When the set is cold and switched on, it does not start up and stays in standby. It can go to normal operation mode if it is switched off and on again. | Add a 1uF 16V (250111) capacitor in parallel to C451 (which is connected to Vcc pin of IC406 on Featurebox). |
| 119 | 18.03.2004 | 12.6 | Jitter during max volume | The value of R624 was changed from 0? to 820? (parts code 171824). |
| 120 | 16.02.2004 | 22.2 | IC801 of Feature Box changed | With the new IC 801 (C3), software version was upgraded to 6 from 5 (version is shown during exiting service mode). If new IC needs to be replaced with the B11 old version (which we do not recommend), Software IC404 should be upgraded to version 6 onwards. However, old IC801 can be used with version 6 onwards SW IC404. |
| 121 | 16.02.2004 | 22.1 | IC801 of Feature Box changed | With the new IC 801 (C3), software version was upgraded to 14 from 12 (version is shown during exiting service mode). If new IC needs to be replaced with the B11 old version (which we do not recommend), Software IC404 should be upgraded to version 14. However, old IC801 can be used with version 14 SW IC404. |
| 122 | 19.01.2004 | 14.2 | No picture | Check and replace R162 -47R connected to +8V |
| 123 | 19.01.2004 | 16.1 | Defected horizontal transistor BU808DFI (T552). | Add another 82R 3W resistor in parallel to the 82R 3W (110823) on position R554. |
| 124 | 19.01.2004 | 12.3 | Defected horizontal transistor BU808DFI (T552). | Add another 82R 3W resistor in parallel to the 82R 3W (110823) on position R554. |
| 125 | 19.01.2004 | 14.2 | No sound | Check and replace C178 - 4.7nF on pin 26 of IC101 |
| 126 | 19.01.2004 | 14.2 | Defected horizontal transistor BU508DF (T504). | Check and replace C129 - 2.2nF on pin 11 of IC101 |
| 127 | 27.12.2003 | 22.1 | speaker sound distorted, TV shuts off intermittently and does not get any broadcast | Check and replace Q201 |
| 128 | 27.12.2003 | 22.1 | Keyboard is switched off TV can not be controlled by remote control | Check and replace Q201 |
| 129 | 27.12.2003 | 22.1 | When TV is switched on from the on-off switch, picture comes directly without staying at standby | Check and replace Q201 |
| 130 | 25.12.2003 | 22.1 | TV making continuously program up | Please check and replace following components on Feature Box for cold solder or defect: C439, R441, R440, C441, R442, R443, R444, R446, C444, ZD401, ZD402, ZD403 (connected pin 80, 79, 78 of IC401) |
| 131 | 16.12.2003 | 14.2 | Is Hotel Mode available | Not available. Hotel mode in service mode is for application only. |
| 132 | 15.12.2003 | 14.2 | If the unit is in power off state long enough (for example over night) then always when you switch it on, the complete upper part of the picture is messed up and fuzzy. | Please check and replace vertical IC, TDA8359J on position IC501. |
| 133 | 12.12.2003 | 14.2 | Coloured spots on the corners (Degaussing problem) | Please replace 9R PTC on R602 with two 18R PTC’s (code 154222) in parallel. |
| 134 | 12.12.2003 | 20.2 | Coloured spots on the corners (Degaussing problem) | Please replace 9R PTC on R108 with two 18R PTC’s (code 154222) in parallel. |
| 135 | 11.12.2003 | 20.2 | Yellowish spots on Teletext (Local Dooming) | In the service menu , options 2, there are NVM-edit address, NVM-edit data. For the text contrast the address is "5F6" and value must be "33". If it is not "33", please set this value. Even this value is "33" but text contrast is high, you can decrease this value up to "25". |
| 136 | 10.12.2003 | 20.2 | Q204 horizontal transistor, R210, R218, R206, R222 are damaged | Replace R206 with RW 47R J 7W (120472) and R222 with RWF 1K J 1.5W (122114) |
| 137 | 03.12.2003 | 14.2 | Sometimes flyback lines | Replace 220R 1/4W R709 with a stronger one (example 101223). |
| 138 | 03.12.2003 | 22.1 | For 33" sets - If local keyboard buttons are pressed, TV does not start up from standby when a RGB source is connected to SCART. | Change the value of L605 on the primer side of SMPS to 2.2 uH (053781). The problem occurs with 10uH. |
| 139 | 17.11.2003 | 14.2 | Microprocessor spare parts codes in the service manual are not correct | Please see TCN's 2003/10, 2003/08 and 2002/17 |
| 140 | 07.11.2003 | 20.2 | TV shuts off intermittently | 1. Fasten the connectors of Featurebox, uP/IF (CN501B, CN502B) and I/O Scart modules 2. Resolder Vprot (Vertical protection) line from IC201 (vertical IC on main chassis) to pin 11 of IC804 (DDP on Featurebox) 3. Resolder pin 2 (+10v) and pin 4 (-10v) of IC201 (vertical IC) 4. Check H-driver circuit (C205, R205, TR201, Q203 etc.) 5. Check and replace R158 (0.1R) and R161 (0.1R) on SMPS outputs. |
| 141 | 27.08.2003 | 14.2 Mono | Channels are changing automatically, TV is operating automatically from standby, Sound is bad and there are lines on picture, TV is closing automatically | Check and replace IC101 |
| 142 | 23.06.2003 | 12.1 | Some channels are absent | Replace R101 with 2.5Kohm potentiometer |
| 143 | 23.06.2003 | 14.1 | Some channels are absent | Replace R129 with 2.5Kohm potentiometer |
| 144 | 23.06.2003 | 12.3 | Some channels are absent | Replace R102 with 2.5Kohm potentiometer |
| 145 | 23.06.2003 | 12.7 | Some channels are absent | Replace R102 with 2.5Kohm potentiometer |
| 146 | 23.06.2003 | 14.2 | Some channels are absent | Replace R129 with 2.5Kohm potentiometer and change the value of C143 as 47N |
| 147 | 19.06.2003 | 22.1 | Protections, LED Blinking Procedure, Dynamic Focus, SVM, Tilt are not explained in the service manual | Please see TCN's 2003/06 |
| 148 | 19.06.2003 | 12.7 | “9301” code does not work for entering service mode | Try “8500” code (SW can be 12.8). |
| 149 | 15.05.2003 | 12.4 | sync fault | Check and replace C158/10nF |
| 150 | 15.05.2003 | 12.3 | Sound exists but no picture | Check and replace D702 D703 D704 BAV21 |
| 151 | 15.05.2003 | 12.7 | NO OSD, it seemslike a line on the screen | Check and replace C410/1NF |
| 152 | 15.05.2003 | 12.3 | Picture is getiing narrow | Check and replace R998 |
| 153 | 15.05.2003 | 12.4 | There are white flyback lines | Check and replace IC402 |
| 154 | 15.05.2003 | 12.4 | No broadcast reception | 1) Check and replace C150/120P 2) Check and replace C437 100 nF |
| 155 | 15.05.2003 | 12.3 | Protection activated | Check and replace IC401 |
| 156 | 15.05.2003 | 12.4 | Vertical fault | Check and replace C507, C510 |
| 157 | 15.05.2003 | 12.5 | Vertical fault | Check and replace C507, C510 |
| 158 | 15.05.2003 | 22.1 | Amplitute adjustments can not be corrected | Check and replace D505 |
| 159 | 15.05.2003 | 12.4 | OSD is shifting | Check and replace T404 |
| 160 | 15.05.2003 | 20.2 | No color or not stable | Check Feature box |
| 161 | 15.05.2003 | 20.2 | Amplitute adjustments can not be corrected | Check and replace Q204 Q206 Q207 |
| 162 | 15.05.2003 | 14.1 | After getting warm colors are going and returning frequently | Check and replace R420/330K |
| 163 | 15.05.2003 | 12.5 | OSD is shifting | Check and replace T404 |
| 164 | 15.05.2003 | 12.5 | There is white flyback lines on screen | Check and replace IC402 |
| 165 | 14.05.2003 | 12.5 | No color | Check and replace C162 47 nf |
| 166 | 14.05.2003 | 12.3 | Picture is darn and a line exists on the upper part of picture | Check and replace R 112 1 kohm |
| 167 | 14.05.2003 | 12.4 | Picture is narrow from bottom to top | Check and replace C 507 1nF ve C512 10nF |
| 168 | 14.05.2003 | 12.4 | Shuts off automatically | Check and replace C526 |
| 169 | 14.05.2003 | 12.4 | No menu | Check and replace T413 BC 848 |
| 170 | 14.05.2003 | 12.3 | TV can not be powered from standby by remote control | Check and replace C 907 470 P |
| 171 | 14.05.2003 | 12.5 | Picture is white | Check and replace T109 BC 848 |
| 172 | 14.05.2003 | 12.5 | Picture is getting narrow from bottom to top | Check and replace C507 1 nF ve C512 10 nF |
| 173 | 14.05.2003 | 12.4 | Sound exists but screen is dark | Check and replace C 521 220 nF |
| 174 | 14.05.2003 | 12.3 | Picture is dark and flyback lines exist | Check and replace R 135 270 ohm |
| 175 | 14.05.2003 | 12.4 | No color | Check and replace C162 47 nF |
| 176 | 14.05.2003 | 12.5 | Shuts off automatically | Check and replace C526 |
| 177 | 14.05.2003 | 12.4 | sync fault | 1) Check and replace C158 10 nF ve ZD101 2) Check and replace C437 100 nF |
| 178 | 14.05.2003 | 14.1 | Picture is getting dark and returning back to the normal level | Check and replace C630 |
| 179 | 14.05.2003 | 14.1 | TV is switching off at max volume | Check abd replace R 607 0.33 Ohm |
| 180 | 14.05.2003 | 14.1 | TV stays at standby, can not be operated by remote control | 1) Check and replace D505 1N 4148 2) Check and replace R115 150 kohm |
| 181 | 14.05.2003 | 14.1 | Sound exists but screen is dark | Check and replace TU101 tuner |
| 182 | 14.05.2003 | 12.5 | No menu | Check and replace T413 BC 848 |
| 183 | 14.05.2003 | 12.5 | sync fault | 1) Check and replace C437 100 nf 2) Check and replace C158 10 nf and ZD101 Dıode 6V |
| 184 | 14.05.2003 | 12.5 | No channel | 1) Checkand replace C437 100 nf 2) Check and replace C150/120P |
| 185 | 14.05.2003 | 12.5 | Sound exists but picture is dark | Check and replace C521 220 nf |
| 186 | 14.05.2003 | 12.4 | Screen is white | Check and replace T109 BC 848 |
| 187 | 12.05.2003 | 12.4 | Menu color is different | Check and replace IC953 |
| 188 | 12.05.2003 | 12.7 | Vertikal line on the screen | Check vertical IC |
| 189 | 12.05.2003 | 12.5 | Menu color is different | Check and replace IC953 |
| 190 | 12.05.2003 | 12.5 | Screen is white, RASTER | Check and replace IC701 TDA6107 |
| 191 | 12.05.2003 | 14.1 | Vertical faullt on top of screen | Check and replace R521 0.47R |
| 192 | 12.05.2003 | 12.5 | OSD is bad | Check and replace IC953 |
| 193 | 11.05.2003 | 12.4 | Vertical fault | Check and replace R511 |
| 194 | 11.05.2003 | 12.4 | No picture but horizontal line exists on the sreen | Check and replace R709 |
| 195 | 11.05.2003 | 12.5 | Picture is narrow at bottom and top | Check and replace C145 |
| 196 | 11.05.2003 | 12.5 | TV does not work | 1) Check R623 2) Check C617 150 UF400V (LED is blinking) 3) Check IC701 TDA6107 4) Check C623 (if R623 demaged) 5) Check TDA 6107 (LED is blinking) |
| 197 | 11.05.2003 | 12.5 | No AV | Check and replace IC101 SDA555 XFL |
| 198 | 11.05.2003 | 12.4 | Picture is dark | Check and replace R705 |
| 199 | 11.05.2003 | 12.4 | Picture is indistinct and contrast is low | Check and replace R531 ve C524 |
| 200 | 11.05.2003 | 12.4 | Teletex is flickering | Check and replace T501 |
| 201 | 11.05.2003 | 12.4 | There is horizontal line on the screen | Check and replace D501 |
| 202 | 11.05.2003 | 12.4 | No OSD | Check and replace ZD503 |
| 203 | 11.05.2003 | 12.5 | Picture is indistinct and contrast is low | Check and replace R531 ve C524 |
| 204 | 11.05.2003 | 12.4 | Bottom side of picture is black and vertical fault | Check and replace C507 |
| 205 | 11.05.2003 | 14.1 | No broadcast, only snowy picture | Check and replace C157 |
| 206 | 11.05.2003 | 12.5 | Protection activated, CRT flashing | Change CRT |
| 207 | 11.05.2003 | 12.8 | TV does not work | 1) Check and replace R959 2) Replace IC901 3) Replace D901 D903 D904 with RF2007 |
| 208 | 11.05.2003 | 12.8 | No broadcast | Choose tuner type from service menu |
| 209 | 11.05.2003 | 14.1 | Comes a cracking sound inside from TV | Check TR502 |
| 210 | 11.05.2003 | 14.1 | No sound and picture | Check S601 |
| 211 | 11.05.2003 | 12.3 | Stays at standby | Check and replace R959 and T552 |
| 212 | 11.05.2003 | 14.1 | Sound is bad at some channels | Check and replace IC101 |
| 213 | 11.05.2003 | 12.5 | No sound and picture | Check and replace R623 |
| 214 | 11.05.2003 | 14.1 | Picture is snowy | Check and replace C143 |
| 215 | 11.05.2003 | 14.1 | No teletex | Check and replace C143 |
| 216 | 11.05.2003 | 14.1 | No sound and TDA7263 is getting warm | Check and replace C265, C364, C365, C332, C333, C348 |
| 217 | 11.05.2003 | 14.2 | There is a bad noice at some channels | Check and replace IC101 |
| 218 | 11.05.2003 | 12.3 | No OSD | Check and replace C437 CHİP |
| 219 | 11.05.2003 | 12.3 | No AV | Check and replace IC101 STV 22461C |
| 220 | 11.05.2003 | 14.1 | Linearity coil humming | Insulate L502 |
| 221 | 11.05.2003 | 12.4 | TV does not work | 1) Check and replace R623 2) Check and replace C623 3) Check and replace C167 (İf LED is blinking) |
| 222 | 11.05.2003 | 12.3 | OSD exists but no picture | Check and replace R113 |
| 223 | 11.05.2003 | 12.5 | No channel | Choose tuner type from service menu |
| 224 | 11.05.2003 | 12.3 | Sound is bad and no color | Check and replace C128 CHİP |
| 225 | 11.05.2003 | 12.3 | Sound exists but no picture-RASTER | Check and replace C108 CHİP |
| 226 | 11.05.2003 | 12.3 | Sound exists but no picture , IC951 gets warmer | Check and replace C123 CHİP |
| 227 | 11.05.2003 | 12.3 | Picture is narrow and aline exists on the screen | Check and replace IC401 |
| 228 | 11.05.2003 | 12.5 | No broadcast | 1) Check C460 and C141 |
| 229 | 11.05.2003 | 12.4 | Bad color on corners | Check and replace R607 |
| 230 | 11.05.2003 | 12.5 | Picture is red | Check and replace IC101 IC NN5099K |
| 231 | 11.05.2003 | 12.5 | Turns to standby | Check and replace IC701 TDA6107Q |
| 232 | 11.05.2003 | 12.5 | Hick-up mode | Check and replace T552 TRN BU808 |
| 233 | 11.05.2003 | 12.5 | No sound | Check and replace IC101 452842-01 STV2246 |
| 234 | 11.05.2003 | 12.5 | Sound exists but no picture | 1) Check and replace IC701 TDA6107Q 2) Check and replace C155 (if L105 gets warm) |
| 235 | 11.05.2003 | 12.5 | Sound is high-pitched | 1) Check L501 LİNEARİTE 2) Check deflection coil 3) Check DST |
| 236 | 11.05.2003 | 12.3 | No teletex | Check and replace C414 CHİP |
| 237 | 11.05.2003 | 12.4 | Could not catch a channel | Check and replace R408 |
| 238 | 11.05.2003 | 12.5 | There is a horizontal line on picture | Check and replace D501 |
| 239 | 11.05.2003 | 22.1 | Horizontal wide lines on screen | Replace FB501 with jumper |
| 240 | 11.05.2003 | 12.3 | Protection activated, CRT flashing | Check and replace T552 BU808 |
| 241 | 11.05.2003 | 12.4 | Could not catch a channel | Choose tuner type from service menu |
| 242 | 11.05.2003 | 14.2 | No horizontal sync | Check and replace IC101 |
| 243 | 11.05.2003 | 12.4 | No broadcast reception | Check and replace C141 |
| 244 | 11.05.2003 | 12.4 | Sound exists bu no picture, L105 is getting warm | Check and replace C155 |
| 245 | 11.05.2003 | 22.1 | Picture is green | Check and replace X501 FEATURE BOX |
| 246 | 11.05.2003 | 12.5 | No OSD | Check and replace ZD503 |
| 247 | 11.05.2003 | 22.1 | Upper side of picture is empty | Check and replace X501 FEATURE BOX |
| 248 | 11.05.2003 | 12.5 | Vertical fault on top of picture | Check R511 |
| 249 | 11.05.2003 | 12.5 | Teletex is flickering | Check and replace T501 |
| 250 | 11.05.2003 | 12.5 | Bottom side of picture is black and vertical fault | Check and replace C507 |
| 251 | 11.05.2003 | 12.5 | No picture and there is horizontal line on screen | Check and replace R709 |
| 252 | 11.05.2003 | 12.5 | Picture is dark | Check and replace R705 |
| 253 | 11.05.2003 | 22.1 | Bad noice is coming from speakers | 1) Combine ground of C334 and C307 2) Take the ground of cable, which goes from CRT modul to tube, away from deflection coil |
| 254 | 11.05.2003 | 12.4 | Picture height is narrow | Check and replace C145 |
| 255 | 11.05.2003 | 12.3 | No teletex | Check and replace IC402 ST92T195 |
| 256 | 11.05.2003 | 12.3 | Flyback lines | Check and replace IC701 TDA6107Q |
| 257 | 11.05.2003 | 12.3 | Picture is dark | Check and replace C439 CHİP |
| 258 | 11.05.2003 | 12.4 | No AV | Check and replace IC101 SDA555 XFL |
| 259 | 11.05.2003 | 12.3 | No broadcast | Check T100 tuner |
| 260 | 11.05.2003 | 22.1 | Picture is shifting to right side | Check and replace X501 FEATURE BOX |
| 261 | 11.05.2003 | 12.3 | Choosing of Tuner type is lost | Choose tuner type from service menu |
| 262 | 11.05.2003 | 12.3 | No sound and picture | Check and replace IC701 TDA 6107 ve L102 |
| 263 | 11.05.2003 | 22.1 | Vertical lines on screen | Check and replace IC501 STV9379 |
| 264 | 11.05.2003 | 20.2 | TV can not be operated from standby by remote control | Check and replace R158 and R161 |
| 265 | 11.05.2003 | 20.2 | Only RASTER | Check for cold soldering on microprocessor/IF board |
| 266 | 09.05.2003 | 22.1 | Subwoofer sound is not good, sometimes does not work | Check and replace R330 18ohm |
| 267 | 09.05.2003 | 20.2 | EAST/WEST Foult | Check and replace R218-, R210, L201 ve C215 |
| 268 | 09.05.2003 | 20.2 | TV does not work | 1) Check and replace R153, R158, R161 2) Check and replace 0.1RJ 75W R161 3) Check and replace R206 (if Q204 is demaged) |
| 269 | 09.05.2003 | 12.5 | menu is flickering | Check R507 100KOHM |
| 270 | 09.05.2003 | 22.1 | Bad noice is coming inside from TV | Check and replace L603 |
| 271 | 11.04.2003 | 12.4 | OSD is defected or colours are not good | Check and replace IC953 |
| 272 | 11.04.2003 | 12.5 | OSD is defected or colours are not good | Check and replace IC953 |
| 273 | 11.04.2003 | 14.1 | Screen size is increasing and decreasing | Check and replace R606 and R607 on power supply circuit |
| 274 | 11.04.2003 | 12.3 | Whistling sound | Check and replace Linearity coil L551 |
| 275 | 10.04.2003 | 14.2 | Sound is distorted | Check and replace C112 |
| 276 | 10.04.2003 | 20.2 | Lines on the screen | Check Feature box |
| 277 | 09.04.2003 | 14.1 | No colour | Check C113 and C115 capacitor |
| 278 | 09.04.2003 | 12.8 | Horizontal syncronization is not good and no OSD | Check 1nF C410 |
| 279 | 09.04.2003 | 12.5 | No picture | Check 120pF on pos. C150 |
| 280 | 09.04.2003 | 12.5 | Horizontal screen is shifting | Check and replace 27R on R529 pos. |
| 281 | 09.04.2003 | 12.1 | In some scenes, the CPT seems to have low emission | Check 2nF on C806 pos. |
| 282 | 09.04.2003 | 12.5 | Sometimes no colour | Check 8.2pF on pos. C130 |
| 283 | 09.04.2003 | 14.1 | No horizontal sync | Check 1N4148 on pos. D503 |
| 284 | 09.04.2003 | 14.2 | Subwoofer sound is not good, sometimes distorted | Check 1nF on position C361 which is parallel to the speaker |
| 285 | 09.04.2003 | 12.1 | Sound is distorted | Check 10nF on C107 pos. |
| 286 | 09.04.2003 | 14.1 | Sound distortion from central speaker | Check trystor TH601 |
| 287 | 09.04.2003 | 14.1 | Set starts up but RC and keyboard do not response. No picture. | Check 330pF on C170 pos (on IC101 pin 18 line) |
| 288 | 09.04.2003 | 12.1 | Channels are shifting | Check and replace C961-C403-C460-C461-R453-R454-R455 |
| 289 | 09.04.2003 | 12.5 | Picture is snowy | Resolder 150R on position R116 |
| 290 | 09.04.2003 | 12.3 | In some scenes, the CPT seems to have low emission | Check 2nF on C705 pos. |
| 291 | 09.04.2003 | 14.2 | Spot on the CPT during shut off | Please check if C704 on CRT module is short circuited |
| 292 | 09.04.2003 | 14.1 | Sometimes flyback lines | Replace 220R 1/4W R709 with a stronger one (example 101223). |
| 293 | 09.04.2003 | 14.2 | Sound is distorted during start up | Check C350 capacitor |
| 294 | 07.04.2003 | 14.1 | Colors are bad | Check and replace Q101 |
| 295 | 07.04.2003 | 12.5 | Some channels are absent | Choose tuner type from service menu |
| 296 | 07.04.2003 | 12.3 | Stays at standby but does not work | Check and replace IC701 |
| 297 | 07.04.2003 | 12.4 | Some channels are absent | Choose tuner type from service menu |
| 298 | 07.04.2003 | 14.1 | No sound | Check and replace IC303-IC304 |
| 299 | 07.04.2003 | 12.4 | Stays at standby but does not work | Check and replaceT506 TRN BU808DFI ve C517 47MF/35V |
| 300 | 07.04.2003 | 12.3 | No Standby | Check and replace T901 TRN 2SK2545 ve sigorta 2.5A |
| 301 | 07.04.2003 | 14.1 | No Standby | Check T601 TRN 2SK2545,IC601 IC MC44608 ve ST601 2.5A |
| 302 | 07.04.2003 | 12.8 | No Standby | Check T901 TRN 2SK2545 and S901 2.5A |
| 303 | 06.03.2003 | 12.3 | A low amplitude whistle sound (typically 2-3 kHz) can be heard from speakers at near distance. | 1) Replace 12K resistor on position R329 (connected to pin 9 of IC317) with 10K resistor 2) Replace 12K resistor on position R330 (connected to pin 9 of IC318) with 15K resistor. 3) Check L551 |
| 304 | 26.02.2003 | 22.1 | No color at PIP | Check F103 |
| 305 | 20.02.2003 | 12.8 | Microprocessor spare parts codes in the service manual are not correct | Please see TCN 2003/04 |
| 306 | 20.02.2003 | 12.5 | Microprocessor spare parts codes in the service manual are not correct | Please see TCN 2003/04 |
| 307 | 04.02.2003 | 12.8 | Some malfunctioning will be encountered in channel frequency setup, when Hotel option is changed to “Hotel TV” in Service Mode. | This is due to Eeprom capacity. For Hotel mode usage, the eeprom in IC402 must be changed to BR24C16F (452637) from AT24C04N (453002). |
| 308 | 04.02.2003 | 12.8 | The picture is shifted towards the right of the screen when TV is turned on (There is black band on the screen). The defect disappears after a few minutes. | Replace BU808DFI on position T552. The problem is due to a quality problem of BU808DFI for a small period. |
| 309 | 04.02.2003 | 12.7 | Some malfunctioning will be encountered in channel frequency setup, when Hotel option is changed to “Hotel TV” in Service Mode. | This is due to Eeprom capacity. For Hotel mode usage, the eeprom in IC402 must be changed to AT24C16N SC2.7 (452662) from AT24C08N-10SI-2.7 (453031-01) |
| 310 | 20.11.2002 | 20.2 | Adjustments are not available in the service manual (supply voltage, AGC, IF) | Please see TCN 2002/09 |
| 311 | 20.11.2002 | 14.2 | Vertical defects :IC501 (TDA8359J) and R522 (Fuse Resistor) | Please apply TCN 2002/14 |
| 312 | 20.11.2002 | 12.8 | For Secam DK versions: STV2249C defected (No sound) | 1. Replace STV2249C (452990) 2. Remove J143 (jumper) and insert 1K 1/4W resistor in that position |
| 313 | 20.11.2002 | 20.2 | Options are not complete in the service manual (Tuner Type, etc.) | Please see TCN 2002/09 |
| 314 | 20.11.2002 | 20.2 | Set can not be switched on from standby. Defect of fuse resistors 0.1R 0.4W of position R158 and R161 | Replace 0.1R 1/4W (119109 ) resistors of positions R158 and R161 to 0.1R 0.25W (119113). |
| 315 | 20.11.2002 | 14.1 | Mono version microprocessor codes | Please see TCN 2002/18 |
| 316 | 19.09.2002 | 20.2 | TV enters Service Menu randomly | Replace IC503 with SW version SBC256_05 (452286) |
| 317 | 19.09.2002 | 12.5 | Position of teletext / OSD is not correct after replacing IC401 (from MB7120-03 to MB7120-04 or 06) | Enter service menu - Press green button to enter Geometry Menu - Adjust the window when OSDH and OSDV items selected (change value of these items). |
| 318 | 15.08.2002 | 14.2 | Replacing Termal Brand FBT with Eldor | Please apply TCN 2002/13 |
| 319 | 01.07.2002 | 12.3 | Defected TDA6107 on CRT module | Please apply TCN 2002/10 |
| 320 | 01.07.2002 | 12.8 | Defected TDA6107 on CRT module | Please apply TCN 2002/11 |
| 321 | 01.07.2002 | 12.3 | Brightness of the picture changes constantly like flashing | Separate the 4 pin cable (which goes from Stereo module to main chassis) from Video IC and RGB cable (which goes to CRT module). In this way, the interference is minimized. |
| 322 | 19.06.2002 | 12.5 | Defected TDA6107 on CRT module | Please apply TCN 2002/08 |
| 323 | 19.06.2002 | 12.4 | Defected TDA6107 on CRT module | Please apply TCN 2002/08 |
| 324 | 02.05.2002 | 14.2 | Mono, PIP versions are not available in the manual | Please see the soft copy on the web page |
| 325 | 13.03.2002 | 20.2 | During switch off, SPOTS can be seen in the middle of screen | Replace C930 (2.2 uF/250V) capacitor on CRT board with 4.7 uF/250V capacitor. |
| 326 | 13.03.2002 | 12.5 | When TV is adjusted 16:9 mode, shading can be seen on top of the screen. | Replace R504 (470 R 1/2W) resistor with 220R 1/2W resistor. (This modification will be done TV sets for 20” SAMSUNG CPT’s .) - Replace R504 with 270R 1/2W resistor for other CPT’s. |
| 327 | 13.03.2002 | 20.2 | Poor color and contrast | 1) Remove R922-R927-R933 (43K 1/2W) resistor and insert 47K 1W resistor. 2) EnterVIDEO adjustments in service menu with service RC. - Increase RED DRIVE-GREEN DRIVE-BLUE DRIVE values “+3 “ then the factory presets. - Increase BCL THRESHOLD value “+1” then the factory presets. |
| 328 | 13.01.2002 | 14.1 | There is sometimes bad noice | Put 1nF capacitor parallel to C363 1nF |
| 329 | 04.11.2001 | 12.1 | Channels are shifting, colors are going and returning frequently, picture is being ripped | 1) Replace C101,which is on the 1. leg of IC101, with 100pF capacitor 2) Remove the ground of IC101 from PCB and combine 1.5 Kohm potentiometer between ground of IC101 and PCP |
| 330 | 31.10.2001 | 12.5 | LED is lighting on standby. It is going out when ON button is pressed | Check and replace IC 701 |
| 331 | 19.05.2001 | 14.1 | When TV is switched on from the switch comes a cracking sound 4-5 times inside from TV | Replace C610 15mF with 47mF and put 10mF capasitor on poz C642 parallel to C610 |
| 332 | 10.05.2001 | 12.1 | Turns to standby automatically and sometimes could not be operated from standby | Replace C913 1UF 25V with 1UF 50 V capacitor |
| 333 | 09.05.2001 | 14.1 | when channels are changed by using remote control, OSD is shifting, sometimes color is bad | Check and replace C117 270 pF on the leg of Q102 |
| 334 | 01.05.2001 | 11.1 | Distorted sound is coming inside from TV | Check and replace C408 0.1UF 63 V |
| 335 | 01.05.2001 | 12.1 | Vertical is open too much | Check C503-C509 |
| 336 | 28.03.2001 | 12.1 | Picture is snowy, no OSD , Picture is getting dark after some minutes | Check C155 at the 7. pin of IC151 |
| 337 | 30.01.2001 | 12.1 | Colors and OSD dissipate | Check C806 on CRT module |
| 338 | 28.10.2000 | 12.1 | TV does not work (LED is doing flip flop,does not work with switched mode transformer) | Replace C914 with 4.7 uF/50V capacitor. |