SONY AE6AB G2&AKB problems

G2 adjustment:

1. Input a dot signal from the pattern generator.

2. Set the Picture, Brightness and Colour to minimum.

3. Apply 165V DC from an external power supply to the R, G

and B cathodes of the CRT.

4. Whilst watching the picture, adjust the G2 control [SCREEN]

located on the flyback transformer to the point just before the

flyback return lines disappear.

Layout of each control

Note : If you are unable to adjust the corner convergence properly,

this can be corrected with the use of permalloy magnets.

FIVE (5) Blinks: AKB circuit (AKB) problem

The timer/standby indicator blinks for about 30 seconds then goes to the self-diagnosis function. Something is wrong with the video.

Check video out, Q705, 732, 761 and other components on the C board.

Also check Q218, 219, 220 on the A board.

Also unit be in IK blanking, try turning up screen slightly.