| RF Inductors – Color Coding You can also view an Adobe Acrobat version of this document. |
| --- |
| 0201, 0302, 0402, 0403 and 0603 Series Because of their small size, 0201, 0302, 0402, 0403 and some 0603 parts are not marked. |
| 0603, 0805 and 1008 Series 0603 (except 0603CT and 0603AF), all 0805 and some 1008 parts are marked with a single color dot. The inductance value represented by the dot is shown on the data page for each series The dot is for identification only and does not indicate polarity. |  |
| 1008, 1206, 1812 and Midi Spring Series Some 1008 parts are marked with one dot. The inductance value represented by the dot is shown on the data sheet for the series. The dot is for identification only and does not indicate polarity. Other parts are marked with three color dots. The dots do not indicate polarity. The table below shows the significance of each color. Dots 1 and 2 indicate the inductance in nanoHenries. Dot 3 indicates the number of zeroes to be added. Examples: Gray Red Black = 82 nH Brown Red Brown = 120 nH Yellow Violet Red = 4700 nH Values below 10 nH On these parts, the third dot is not a multiplier. Refer to the table below for the specific inductance values represented by the color dots. 1008CT Series Black Yellow Black Black Gray Black 1008HT Series Black Orange Black Black Blue Black Black Violet Black 1008HQ Series Black Orange Black Black Yellow Black Black Violet Black 1206CS Series Black Orange Black Black Blue Black . 4.7 nH 8.2 nH . 3.3 nH 6.8 nH 7.2 nH . 3.0 nH 4.1 nH 7.8 nH . 3.3 nH 6.8 nH . 1008CT-040X_LC 1008CT-080X_LC . 1008HT-3N3T_LC 1008HT-6N8T_LC 1008HT-7N2T_LC . 1008HQ-3N0T_LC 1008HQ-4N1T_LC 1008HQ-7N8T_LC . 1206CS-030T_LC 1206CS-060T_LC | 0 = Black 1 = Brown 2 = Red 3 = Orange 4 = Yellow 5 = Green 6 = Blue 7 = Violet 8 = Gray 9 = White |