G

accessory! www.panelook.com

T315XW03 VE Product Specification

Rev. 1.0

© Copyright AUO Optronics Corp. 2010 All Rights Reserved. Page 8 / 29

3-2 Interface Connections

_ LCD connector: Starconn 093G30-B0001A-1

_

PIN Symbol Description

1 VDD Power Supply, +12V DC Regulated

2 VDD Power Supply, +12V DC Regulated

3 VDD Power Supply, +12V DC Regulated

4 VDD Power Supply, +12V DC Regulated

5 GND Ground

6 GND Ground

7 GND Ground

8 GND Ground

9 LVDS_SEL Open/High(3.3V) for NS, Low(GND) for JEIDA

10 N.C. AUO Internal Use Only

11 GND Ground

12 CH1_0- LVDS Channel 1, Signal 0-

13 CH1_0+ LVDS Channel 1, Signal 0+

14 GND Ground

15 CH1_1- LVDS Channel 1, Signal 1-

16 CH1_1+ LVDS Channel 1, Signal 1+

17 GND Ground

18 CH1_2- LVDS Channel 1, Signal 2-

19 CH1_2+ LVDS Channel 1, Signal 2+

20 GND Ground

21 CH1_CLK- LVDS Channel 1, Clock -

22 CH1_CLK+ LVDS Channel 1, Clock +

23 GND Ground

24 CH1_3- LVDS Channel 1, Signal 3-

25 CH1_3+ LVDS Channel 1, Signal 3+

26 GND Ground

27 N.C. AUO Internal Use Only

28 N.C. AUO Internal Use Only

29 GND Ground

30 GND Ground