Issued Date: April 14, 2009

Model No.: V315B5 - L02

Approval

Version 2.0

1

TFT LCD Approval Specification

MODEL NO.: V315B5 - L02

5. INTERFACE PIN CONNECTION

5.1 TFT LCD MODULE

CNF1 Connector Pin Assignment

Pin No. Symbol Description Note

1 VCC Power supply: +12V

2 VCC Power supply: +12V

3 VCC Power supply: +12V

4 VCC Power supply: +12V

5 GND Ground

6 GND Ground

7 GND Ground

8 GND Ground

9 SELLVDS Select LVDS data format (2)

10 ODSEL Overdrive Lookup Table Selection (3)

11 GND Ground

12 RX0- Negative transmission data of pixel 0

13 RX0+ Positive transmission data of pixel 0

14 GND Ground

15 RX1- Negative transmission data of pixel 1

16 RX1+ Positive transmission data of pixel 1

17 GND Ground

18 RX2- Negative transmission data of pixel 2

19 RX2+ Positive transmission data of pixel 2

20 GND Ground

21 RXCLK- Negative of clock

22 RXCLK+ Positive of clock

23 GND Ground

24 RX3- Negative transmission data of pixel 3

25 RX3+ Positive transmission data of pixel 3

26 GND Ground

27 NC No connection (4)

28 NC No connection (4)

29 GND Ground

30 GND Ground