MP03AB chassis

O Convergence Adjustment

1. Preliminary steps

This adjustment should be performed after warming up 60

minutes.

1) Adjust after Horizontal/Vertical Raster position,Beam

alignment magnet, and focus adjustments have been

completed.

2) Do it always with crosshatch pattern.

3) Adjust for both PAL and NTSC system.

4) Use the JIG screen with the cross hatch pattern for

Adjustment.

2. Convergence Key

1) Convergence Mode : IN_START, ‘3’

2) Cursor shift

3) Cursor Movement/Adjustment Selection : ENTER

4) Cursor Color Selection : TV/AV

5) Adjustment mode out : IN_START

*Note: When cursor flashes,set is in adjustment mode When

R,G or B selected color flashes,the set is in cursor movement

mode.

O PAL Mode Adjustment

1. Preliminary steps

1) Receive the EU 05CH signal.

2) Press the buttons IN_START, ‘3’ of Remote Controller for

adjustment to get into the convergence adjustment mode.

2. Horizontal/Vertical phase adjustment

1) Press the buttons 9 & 5 to get into the phase adjustment

mode.

2) Horizontal Phase Adjustment.

Move the convex part to the quarter of vertical center by

pressing the Volume F,G key.

3) Press the ENTER Key to escape from the adjustment.

O Auto-Convergence Check (option)

1) Check the Auto-Convergence in PAL/NTSC/1080i(option)

mode separating.

2) Press the IN_START key on R/C for adjustment and press

the CAPTION key to check whether Auto-Convergence

works normally in each mode.

3) If not,check the Convergence condition or Measuring

condition and SENSOR condition.

4)The shipment must be done after restoring the final auto

convergence data value.

* Restore a Convergence data

IN_START -> ‘3’ -> TEXT